## Slide 1: Updates from Address Selection Design Team
Arifumi Matsumoto
NTT PF Labs.

## Slide 2: Address Selection Design Team
Who ?
  Chartered to work on RFC3484 policy table updating mechainsm
  Composed of XX people, working for 2 years !
What have we done ?
  Examined the problematic cases to see:
    how dynamic the updating mechanism needs to be.
    what kind of policy needs be distributed.
  Examined the solution space including a policy merging algorithm. draft-arifumi-6man-addr-select-conflict

## Slide 3: After IETF 77
We worked intensively after IETF77
  to discuss the remaining issues and reach consensus within the DT.
  kicked by BBF’s demands for a mechanism to update address selection policy.
    draft-troan-ipv6-multihome-without-ipv6-nat
  to propose the next step forward, after the investigation and discussion.

## Slide 4: Proposal 1/3
Re. Policy Merging
  By its nature, conflict always happens when you merge two set of policies.
    A heuristic approach can merge policies. But, there is no distinct/established algorithm for it.
  So, we propose not to standardize the merging process. (at least for now)
    This issue should be up to an implementation or a user, just like DNS server selection.
    e.g. The NIF metrics are used for choosing primary interface and can be used for policy set selection.
Host
Policy
Policy

## Slide 5: Proposal 2/3
Re. What protocol carries the policy
  RA is better to work with the routing.
    Easy to reflect routing status, easy to update.
  DHCP is better in management.
    it has a lot more space.
    host-specific policy enforcement.
    DHCP-relay function is useful in large-scale network.
  Don’t see any other good protocols if we will support general environments like enterprise, residential network, etc.
So, we propose to go with DHCP, and if necessary RA.

## Slide 6: Proposal 3/3
Re. RFC 3484 revision
  It’s known to have several faults, and oviously needs update
  DT improves the revision proposal:
    draft-arifumi-6man-rfc3484-revise-03
    6to4/teredo is de-prioritized than IPv4
    protection from mis-use of deprecated addresses
  Some universal problems can/should be solved by revising RFC 3484.
  DT proposes these changes should be made, along with policy distribution mechiansm.

## Slide 7: In the end
Ready for WG adoption ?
6man should be the right place for RFC3484 revision.
  draft-arifumi-6man-rfc3484-revise-03
The home for DHCP policy distribution mechanism should also be 6man, with some review from dhc wg.
  draft-fujisaki-dhc-addr-select-opt