Network Work group                                              N. Kumar

Internet-Draft                                              C. Pignataro

Intended status: Standards Track                     Cisco Systems, Inc.

Expires: August 9, 2021                                         N. Akiya

Big Switch Networks

L. Zheng

Individual Contributor

M. Chen

Huawei Technologies

G. Mirsky

Ericsson

February 5, 2021

BIER Ping and Trace

draft-ietf-bier-ping-08

Abstract

Bit Index Explicit Replication (BIER) is an architecture that

provides optimal multicast forwarding through a "BIER domain" without

requiring intermediate routers to maintain any multicast related per-

flow state.  BIER also does not require any explicit tree-building

protocol for its operation.  A multicast data packet enters a BIER

domain at a "Bit-Forwarding Ingress Router" (BFIR), and leaves the

BIER domain at one or more "Bit-Forwarding Egress Routers" (BFERs).

The BFIR router adds a BIER header to the packet.  The BIER header

contains a bit-string in which each bit represents exactly one BFER

to forward the packet to.  The set of BFERs to which the multicast

packet needs to be forwarded is expressed by setting the bits that

correspond to those routers in the BIER header.

This document describes the mechanism and basic BIER OAM packet

format that can be used to perform failure detection and isolation on

BIER data plane.

Status of This Memo

This Internet-Draft is submitted in full conformance with the

provisions of BCP 78 and BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF).  Note that other groups may also distribute

working documents as Internet-Drafts.  The list of current Internet-

Drafts is at https://datatracker.ietf.org/drafts/current/.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

Kumar, et al.            Expires August 9, 2021                 [Page 1]

Internet-Draft                  BIER Ping                  February 2021

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

This Internet-Draft will expire on August 9, 2021.

Copyright Notice

Copyright (c) 2021 IETF Trust and the persons identified as the

document authors.  All rights reserved.

This document is subject to BCP 78 and the IETF Trust's Legal

Provisions Relating to IETF Documents

(https://trustee.ietf.org/license-info) in effect on the date of

publication of this document.  Please review these documents

carefully, as they describe your rights and restrictions with respect

to this document.  Code Components extracted from this document must

include Simplified BSD License text as described in Section 4.e of

the Trust Legal Provisions and are provided without warranty as

described in the Simplified BSD License.

Table of Contents

1.  Introduction  . . . . . . . . . . . . . . . . . . . . . . . .   3

2.  Conventions used in this document . . . . . . . . . . . . . .   3

2.1.  Terminology . . . . . . . . . . . . . . . . . . . . . . .   3

2.2.  Requirements notation . . . . . . . . . . . . . . . . . .   4

3.  BIER OAM  . . . . . . . . . . . . . . . . . . . . . . . . . .   4

3.1.  BIER OAM message format . . . . . . . . . . . . . . . . .   4

3.2.  Return Code . . . . . . . . . . . . . . . . . . . . . . .   7

3.3.  BIER OAM TLV  . . . . . . . . . . . . . . . . . . . . . .   8

3.3.1.  Original SI-BitString TLV . . . . . . . . . . . . . .   8

3.3.2.  Target SI-BitString TLV . . . . . . . . . . . . . . .   9

3.3.3.  Incoming SI-BitString TLV . . . . . . . . . . . . . .  10

3.3.4.  Downstream Mapping TLV  . . . . . . . . . . . . . . .  11

3.3.5.  Responder BFER TLV  . . . . . . . . . . . . . . . . .  14

3.3.6.  Responder BFR TLV . . . . . . . . . . . . . . . . . .  14

3.3.7.  Upstream Interface TLV  . . . . . . . . . . . . . . .  15

3.3.8.  Reply-To TLV  . . . . . . . . . . . . . . . . . . . .  15

3.4.  Multipath Entropy Data Encoding . . . . . . . . . . . . .  16

4.  Procedures  . . . . . . . . . . . . . . . . . . . . . . . . .  16

4.1.  BIER OAM Processing . . . . . . . . . . . . . . . . . . .  16

4.2.  Per BFER ECMP Discovery . . . . . . . . . . . . . . . . .  17

4.3.  Sending BIER Echo Request . . . . . . . . . . . . . . . .  17

4.4.  Receiving BIER Echo Request . . . . . . . . . . . . . . .  18

4.5.  Sending Echo Reply  . . . . . . . . . . . . . . . . . . .  20

4.6.  Receiving Echo Reply  . . . . . . . . . . . . . . . . . .  21

5.  IANA Considerations . . . . . . . . . . . . . . . . . . . . .  22

5.1.  BIER OAM Registry . . . . . . . . . . . . . . . . . . . .  22

Kumar, et al.            Expires August 9, 2021                 [Page 2]

Internet-Draft                  BIER Ping                  February 2021

5.2.  Message Types, Reply Modes, Return Codes  . . . . . . . .  22

5.3.  TLVs  . . . . . . . . . . . . . . . . . . . . . . . . . .  22

6.  Security Considerations . . . . . . . . . . . . . . . . . . .  23

7.  Acknowledgement . . . . . . . . . . . . . . . . . . . . . . .  23

8.  References  . . . . . . . . . . . . . . . . . . . . . . . . .  23

8.1.  Normative References  . . . . . . . . . . . . . . . . . .  23

8.2.  Informative References  . . . . . . . . . . . . . . . . .  24

Authors' Addresses  . . . . . . . . . . . . . . . . . . . . . . .  24

1.  Introduction

[RFC8279] introduces and explains BIER architecture that provides

optimal multicast forwarding through a "BIER domain" without

requiring intermediate routers to maintain any multicast related per-

flow state.  BIER also does not require any explicit tree-building

protocol for its operation.  A multicast data packet enters a BIER

domain at a "Bit-Forwarding Ingress Router" (BFIR), and leaves the

BIER domain at one or more "Bit-Forwarding Egress Routers" (BFERs).

The BFIR router adds a BIER header to the packet.  The BIER header

contains a bit-string in which each bit represents exactly one BFER

to forward the packet to.  The set of BFERs to which the multicast

packet needs to be forwarded is expressed by setting the bits that

correspond to those routers in the BIER header.

This document describes the mechanism and basic BIER OAM packet

format that can be used to perform failure detection and isolation on

the BIER data plane without any dependency on other layers like the IP layer.

2.  Conventions used in this document

2.1.  Terminology

BFER - Bit Forwarding Egress Router

BFIR - Bit Forwarding Ingress Router

BIER - Bit Index Explicit Replication

ECMP - Equal Cost Multi-Path

OAM - Operation, Administration, and Maintenance

SI - Set Identifier

Kumar, et al.            Expires August 9, 2021                 [Page 3]

Internet-Draft                  BIER Ping                  February 2021

2.2.  Requirements notation

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT",

"SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this

document are to be interpreted as described in [RFC2119].

3.  BIER OAM

BIER OAM is defined to stay within the BIER layer by

directly following  the BIER header without mandating the need for an IP

header.  [RFC8296] defines a 6-bit field as "Proto" to identify the

payload following the BIER header.  When the payload is BIER OAM, the

"Proto" field will be set to 5 as defined in [RFC8296]

3.1.  BIER OAM message format

The BIER OAM packet header format that follows BIER header is as

follows:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  Ver  | Message Type  |                 Reserved              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                        OAM Message Length                     |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

~                  Message Type Dependent Data                  ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Ver

Set to 1.

Message Type

This document defines the following Message Types:

Type      Value Field

--------  ---------------

1      BIER Echo Request

2      BIER Echo Reply

OAM Message Length

This field defines the length of the OAM message, including the

header and Dependent Data field.

Kumar, et al.            Expires August 9, 2021                 [Page 4]

Internet-Draft                  BIER Ping                  February 2021

The Echo Request/Reply header format is as follows:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  Ver  | Echo Req/Rep  |                Reserved               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|   QTF |   RTF |   Reply mode  |  Return Code  |    Reserved   |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                        Sender's Handle                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                        Sequence Number                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                    TimeStamp Sent                             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                  TimeStamp Sent                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                  TimeStamp Received                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                TimeStamp Received                             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

~                              TLVs                             ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

QTF

Querier Timestamp Format.  When set to 2, the Timestamp Sent field

is (in seconds and microseconds, according to the Initiator's

clock) in NTP format [RFC5905].  When set to 3, the timestamp

format is in IEEE 1588-2008 (1588v2) Precision Time Protocol

format.  Any other value SHOULD be considered as sanity check

failure.

This field MUST NOT be set to any other values upon transmission.

Any other values MUST be ignored upon reception.

RTF

Responder Timestamp Format.  When set to 2, the Timestamp Received

field is (in seconds and microseconds, according to the

Initiator's clock) in NTP format [RFC5905].  When set to 3, the

timestamp format is in IEEE 1588-2008 (1588v2) Precision Time

Protocol format.  Any other value SHOULD be considered as sanity

check failure.

Kumar, et al.            Expires August 9, 2021                 [Page 5]

Internet-Draft                  BIER Ping                  February 2021

This field MUST NOT be set to any other values upon transmission.

Any other values MUST be ignored upon reception.

Reply mode

The Reply mode is set to one of the below:

Value      Meaning

--------  ---------------

1        Do not Reply

2        Reply via IPv4/IPv6 UDP packet.

3        Reply via BIER packet

When Reply mode is set to 1, the receiver will not send any reply.

This mode may be used for unidirectional path validation.  The Reply mode by

default would be set to 2, and the Responder BFR will encapsulate the

Echo reply payload with IP header.  When the Initiator intends to

validate the return BIER path, the Reply mode will be set to 3 so that the

Responder BFR encapsulates the Echo Reply with the BIER header.

Return Code

Set to zero if Type is "BIER Echo Request".  Set to one of the

value defined in section 3.2, if Type is "BIER Echo Reply".

Reserved

Set to all zero value.

Sender's Handle, Sequence Number, and Timestamp

The Sender's Handle is filled by the Initiator and returned

unchanged by responder BFR.  is the value may be used for matching the replies

to the request.

The Sequence Number is assigned by the Initiator and can be used

to detect any missed replies.

The Timestamp Sent is the time when the Echo Request is sent.  The

TimeStamp Received in Echo Reply is the time (accordingly to

responding BFR clock) that the corresponding Echo Request was

received.  The format depends on the QTF/RTF value.

TLVs

Carries the TLVs as defined in Section 3.3.

Kumar, et al.            Expires August 9, 2021                 [Page 6]

Internet-Draft                  BIER Ping                  February 2021

3.2.  Return Code

The responder uses the Return Code field to reply with a validity check or

other error message to Initiator.  It does not carry any meaning in

Echo Request and MUST be set to zero.

The Return Code can be one of the following:

Value      Value Meaning

--------  ---------------

0      No return code

1      Malformed Echo Request received

2      One or more of the TLVs was not understood

3      Replying BFR is the only BFER in header Bitstring

4      Replying BFR is one of the BFER in header Bitstring

5      Packet-Forward-Success

6      Invalid Multipath Info Request

8      No matching entry in the forwarding table.

9      Set-Identifier Mismatch

10     DDMAP Mismatch

"No return code" will be used by Initiator in the Echo Request.  This

value MUST NOT be used in Echo Reply.

"Malformed Echo Request received" will be used by any BFR if the

received Echo Request packet is not properly formatted.

When a receiver does not understand any TLV included in the Echo Request, the Return code will be set to "One or more of the TLVs was

not understood" carrying the respective TLVs.

When the received header BitString in the Echo Request packet contains

only its Bit-ID, "Replying BFR is the only BFER in header

BitString" is set in the reply.  This value implies that the receiver is

BFER, and the packet is not forwarded to any more neighbors.

When the received header BitString in the Echo Request packet contains

its Bit-ID in addition to other Bit-IDs, "Replying BFR is one of

the BFER in header BitString" is set in the reply.  This value implies that

the responder is a BFER, and the packet is further forwarded to one or

more neighbors.

Any transit BFR will send the Echo Reply with "Packet-Forward-

Success", if the TLV in the received Echo Request is understood and

the forwarding table has forwarding entries for the BitString.  This behvior is

demonstrated by a transit BFR during traceroute mode.

Kumar, et al.            Expires August 9, 2021                 [Page 7]

Internet-Draft                  BIER Ping                  February 2021

When Echo Request is received with multipath info for more than one

BFER, the Return Code is set to "Invalid Multipath Info Request".

If the BitString cannot be matched in the local forwarding table, the BFR

will use "No matching entry in forwarding table" in the reply.

If the BIER-MPLS label in the received Echo Request is not the one

assigned for SI in Original SI-BitString TLV, "Set-Identifier

Mismatch" is set in order to report the mismatch.

3.3.  BIER OAM TLV

This section defines various TLVs that can be used in BIER OAM

packet.  The TLVs (Type-Length-Value tuples) have the following

format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|               Type            |          Length               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

~                              Value                            ~

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

TLV Types are defined below; Length is the length of the Value field

in octets.  The Value field depends on the TLV Type.

3.3.1.  Original SI-BitString TLV

The Original SI-BitString TLV carries the set of BFER and carries the

same BitString that Initiator includes in the BIER header. This TLV has

the following format:

Kumar, et al.            Expires August 9, 2021                 [Page 8]

Internet-Draft                  BIER Ping                  February 2021

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Type = 1              |       Length = variable       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|    Set ID     | Sub-domain ID |BS Len|  Reserved              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                BitString  (first 32 bits)                     ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

~                                                               ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                BitString  (last 32 bits)                      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Set ID field is set to the value of the Set Identifier to which the BitString

belongs to.  This value is derived as defined in [RFC8279]

Sub-domain ID is set to the Sub-domain value to which BFER in

BitString belongs to.

BS Len is set based on the length of BitString as defined in

[RFC8296].

The BitString field carries the set of BFR-IDs that Initiator will

include in the BIER header.

An Initiator MUST include this TLV in the Echo Request packet.

3.3.2.  Target SI-BitString TLV

The Target SI-BitString TLV carries the set of BFER from which the

Initiator expects the reply from. This TLV has the following format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Type = 2              |       Length = variable       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|    Set ID     | Sub-domain ID |BS Len|  Reserved              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                BitString  (first 32 bits)                     ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

~                                                               ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                BitString  (last 32 bits)                      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Kumar, et al.            Expires August 9, 2021                 [Page 9]

Internet-Draft                  BIER Ping                  February 2021

Set ID field is set to the Set Identifier to which the BitString

belongs to.  This value is derived as defined in [RFC8279]

Sub-domain ID is set to the Sub-domain value to which BFER in

BitString belongs to.

BS Len is set based on the length of BitString as defined in

[RFC8296]

The BitString field carries the set of BFR-IDs of BFER(s) that

Initiator expects the response from.  The BitString in this TLV may

be different from the BitString in the BIER header and allows to control

the BFER responding to the Echo Request.  This TLV MUST be included

by Initiator in BIER OAM packet if the Downstream Mapping TLV

(section 3.3.4) is included.

3.3.3.  Incoming SI-BitString TLV

The Incoming SI-BitString TLV will be included by Responder BFR in

Reply message and copies the BitString from BIER header of incoming

Echo Request message.  This TLV has the following format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Type = 3              |       Length = variable       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|    Set ID     | Sub-domain ID |BS Len|  Reserved              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                BitString  (first 32 bits)                     ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

~                                                               ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                BitString  (last 32 bits)                      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Set ID field is set to the Set Identifier to which the BitString

belongs to.  This value is derived as defined in [RFC8279]

Sub-domain ID is set to the Sub-domain value to which BFER in

BitString belongs to.

BS Len is set based on the length of BitString as defined in

[RFC8296]

Kumar, et al.            Expires August 9, 2021                [Page 10]

Internet-Draft                  BIER Ping                  February 2021

The BitString field copies the BitString from the BIER header of the

incoming Echo Request.  A Responder BFR SHOULD include this TLV in

Echo Reply if the Echo Request is received with I flag set in

Downstream Mapping TLV.

An Initiator MUST NOT include this TLV in Echo Request.

3.3.4.  Downstream Mapping TLV

This TLV has the following format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Type = 4              |       Length = variable       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|               MTU             | Address Type  |     Flags     |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|               Downstream Address (4 or 16 octets)             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Downstream Interface Address (4 or 16 octets)         |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|        Sub-tlv Length         |                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+                               |

.                                                               .

.                      List of Sub-TLVs                         .

.                                                               .

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MTU

Set to MTU value of outgoing interface.

Address Type

The Address Type indicates the address type and length of the IP

address for the downstream interface.  The Address type is set to one

of the below:

Kumar, et al.            Expires August 9, 2021                [Page 11]

Internet-Draft                  BIER Ping                  February 2021

Type     Addr. Type       DA Length    DIA Length

-------  ---------------   ----------   ----------

1       IPv4 Numbered        4              4

2       IPv4 Unnumbered      4              4

3       IPv6 Numbered        16            16

4       IPv6 Unnumbered      16             4

DA Length - Downstream Address field Length

DIA Length - Downstream Interface Address field Length

Flags

The Flags field has the following format:

0 1 2 3 4 5 6 7

+-+-+-+-+-+-+-+-+

|     Rsvd    |I|

+-+-+-+-+-+-+-+-+

When I flag is set, the Responding BFR MUST include the Incoming SI-

BitString TLV in Echo Reply message.

Downstream Address and Downstream Interface Address

If the Address Type is 1, the Downstream Address MUST be set to

IPV4 BFR-Prefix of downstream BFR and Downstream Interface Address

is set to the downstream interface address.

If the Address Type is 2, the Downstream Address MUST be set to

IPV4 BFR-Prefix of downstream BFR and Downstream Interface Address

is set to the index assigned by upstream BFR to the interface.

If the Address Type is 3, the Downstream Address MUST be set to

IPV6 BFR-Prefix of downstream BFR and Downstream Interface Address

is set to the downstream interface address.

If the Address Type is 4, the Downstream Address MUST be set to

IPv6 BFR-Prefix of downstream BFR and Downstream Interface Address

is set to the index assigned by upstream BFR to the interface.

3.3.4.1.  Downstream Detailed Mapping Sub-TLVs

This section defines the optional Sub-TLVs that can be included in

Downstream Mapping TLV.

Kumar, et al.            Expires August 9, 2021                [Page 12]

Internet-Draft                  BIER Ping                  February 2021

Sub-TLV Type     Value

---------------  --------------

1         Multipath Entropy Data

2         Egress BitString

3.3.4.1.1.  Multipath Entropy Data

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|M|  Reserved     |                                             |

+-+-+-+-+-+-+-+-+-+                                             |

|                                                               |

|                  (Multipath Information)                      |

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

M Flag

This flag is set to 0 if all packets will be forwarded out through

the interface defined in the Downstream Mapping TLV.  When set to

1, Multipath Information will be defined by the Bit masked Entropy

data.

Multipath Information

Entropy Data encoded as defined in section 3.4

3.3.4.1.2.  Egress BitString

Responder BFR MAY include this Sub-TLV with the rewritten BitString

in the outgoing interface as defined in section 6.1 of [RFC8279]

0                   1                   2                   3

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|    Set ID     | Sub-domain ID |BS Len|  Reserved              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                BitString  (first 32 bits)                     ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

~                                                               ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                BitString  (last 32 bits)                      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Kumar, et al.            Expires August 9, 2021                [Page 13]

Internet-Draft                  BIER Ping                  February 2021

3.3.5.  Responder BFER TLV

The BFER replying to the request MAY include the Responder BFER TLV.

This TLV identifies the originator of BIER Echo Reply.  This TLV

has the following format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Type = 5              |            Length             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Reserved              |           BFR-ID              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

BFR-ID

The BFR-ID field carries the BFR-ID of replying BFER.  This TLV

MAY be included by Responding BFER in BIER Echo Reply packet.

3.3.6.  Responder BFR TLV

Any transit BFR replying to the request MAY include the Responder BFR

TLV.  This is used to identify the replying BFR without BFR-ID.  This

TLV has the following format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     TLV Type = 6              |       Length = variable       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Reserved              |          Address Type         |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

~                       BFR-Prefix (4 or 16 bytes)              ~

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Length

The Length field varies depending on the Address Type.

Address Type

Set to 1 for IPv4 or 2 for IPv6.

Kumar, et al.            Expires August 9, 2021                [Page 14]

Internet-Draft                  BIER Ping                  February 2021

BFR-Prefix

This field carries the local BFR-Prefix of the replying BFR.  This

TLV MAY be included by Responding BFR in the BIER Echo Reply packet.

3.3.7.  Upstream Interface TLV

The BFR replying to the request will include the Upstream Interface

TLV.  This TLV identifies the incoming interface and the BIER-

MPLS label in the incoming Echo Request.  This TLV has the following

format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     TLV Type = 7              |       Length = variable       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Reserved              |          Address Type         |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

~                 Upstream Address (4 or 16 bytes)              ~

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Length

The Length field varies depending on the Address Type.

Address Type

Set to 1 for IPv4 numbered, 2 for IPv4 Unnumbered 3 for IPv6

numbered or 4 for IPv6 Unnumbered.

Upstream Address

As defined in Section 3.3.4

3.3.8.  Reply-To TLV

The Initiator BFR MAY include Reply-To TLV in the Echo Request.  This

TLV is used by transit BFR or BFER when the reply mode is 2.  The IP

address will be used to generate the Echo Reply.  This TLV has the

following format:

Kumar, et al.            Expires August 9, 2021                [Page 15]

Internet-Draft                  BIER Ping                  February 2021

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     TLV Type = 8              |       Length = variable       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Reserved              |          Address Type         |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

~                    Reply-To Address (4 or 16 bytes)           ~

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Length

The Length field varies depending on the Address Type.

Address Type

Set to 1 for IPv4 or 2 for IPv6.

Reply-To Address

Set to any locally configured address to which the Echo reply

should be sent.

3.4.  Multipath Entropy Data Encoding

The size of the Entropy field in the BIER header is 20 bits, as defined in

section 2 of [RFC8296].  This encoding is similar to the Multipath Type 9 encoding

defined in Section 3.4.1.1.1 of [RFC8029].

4.  Procedures

This section describes aspects of Ping and traceroute operations.

4.1.  BIER OAM Processing

A BIER OAM packet MUST be sent to the BIER control plane for OAM

processing if one of the following conditions is true:

o  The receiving BFR is a BFER.

o  TTL of BIER-MPLS Label expired.

o  Router Alert label is present in the label stack.

Kumar, et al.            Expires August 9, 2021                [Page 16]

Internet-Draft                  BIER Ping                  February 2021

4.2.  Per BFER ECMP Discovery

As defined in [RFC8279], BIER follows the unicast forwarding path and

allows load balancing over ECMP paths between BFIR and BFER.  BIER

OAM MUST support ECMP path discovery between a BFIR and a given BFER

and MUST support path validation and failure detection of any

particular ECMP path between BFIR and BFER.

[RFC8296] proposes the BIER header with the Entropy field that can be

leveraged to exercise all ECMP paths.  The Initiator/BFIR will use

traceroute message to query each hop about the Entropy information

for each of the downstream paths.  To avoid complexity, it is suggested that

the ECMP query is performed per BFER by carrying required information

in BIER OAM message.

The Initiator MUST include Multipath Entropy Data Sub-TLV in

Downstream Mapping TLV.  It MUST also include the BFER in BitString

TLV to which the Multipath query is performed.

Any transit BFR will reply with Bit-masked Entropy for each

downstream path as defined in [RFC8029]

4.3.  Sending BIER Echo Request

The Initiator MUST set the Message Type as 1 and Return Code as 0.

The choice of the Sender's Handle and Sequence Number is a local matter

to the Initiator and SHOULD increment the Sequence number by 1 for

every subsequent Echo Request.  The QTF field is set to Initiator's

local timestamp format and TimeStamp Sent field is set to the time

that the Echo Request is sent.

The Initiator MUST include Original SI-BitString TLV.  The Initiator

MUST NOT include more than one Original SI-BitString TLV.  The

Initiator infers the Set Identifier value and Sub-domain ID value

from the respective BitString that will be included in the BIER header of

the packet and includes the values in "SI" and Sub-Domain ID fields

respectively.

In Ping mode, the Initiator MAY include Target SI-BitString TLV to

control the responding BFER(s) by listing all the BFERs from which

the Initiator expects a response.  In the traceroute mode, the Initiator

MAY include Target SI-Bitstring TLV to control the path trace towards

any specific BFER or set of BFERs.  The Initiator on receiving a

reply with Return code as "Replying BFR is the only BFER in header

Bitstring" or "Replying router is one of the BFER in header

Bitstring", SHOULD unset the respective BFR-id from Target SI-

BitString for any subsequent Echo Request.

Kumar, et al.            Expires August 9, 2021                [Page 17]

Internet-Draft                  BIER Ping                  February 2021

When the Reply mode is set to 2, the Initiator MUST include Reply-To

TLV (section 3.3.8) in the Echo Request.  The Initiator MUST also

listen to the UDP port defined in this TLV and process any segment

received with destination port as the value defined in the TLV and

sent to control plane for BIER OAM payload processing.

The Initiator MAY include Downstream Mapping TLV (section 3.3.4) in

the Echo Request to query additional information from transit BFRs

and BFERs.  In case of ECMP discovery, the Initiator MUST include the

Multipath Entropy Data Sub-TLV and SHOULD set the Target SI-BitString

TLV carrying a specific BFER ID.

The Initiator MUST encapsulate the OAM packet with BIER header and

MUST set the Proto as 5 and further encapsulates with BIER-MPLS

label.  In ping mode, the BIER-MPLS Label TTL MUST be set to 255.  In

traceroute mode, the BIER-MPLS Label TTL is set successively starting

from 1 and MUST stop sending the Echo Request if it receives a reply

with Return code as "Replying router is the only BFER in BIER header

Bitstring" from all BFER listed in Target SI-BitString TLV.

4.4.  Receiving BIER Echo Request

Sending a BIER OAM Echo Request to control plane for payload

processing is triggered as mentioned in section 4.1.

Any BFR on receiving Echo Request MUST perform the basic sanity

check.  Consider when a BFR cannot parse the OAM Dependent data payload

completely because the value in the OAM Message Length field is incorrect.  BFR MUST send

Echo Reply with Return Code set to "Malformed Echo Request received"

if the OAM Message Length is incorrect.  If the packet sanity check

is fine, it SHOULD initiate the below set of variables:

Reply-Flag

This flag is initially set to 1.

Interface-I

The incoming interface on which the Echo Request was received.

It may be used to validate the DDMAP info and to populate the

Upstream Interface TLV.

BIER-Label-L

The BIER-MPLS Label received as the top label of the Echo

Request.  It may be used to validate if the packet is traversing

the desired Set Identifier and sub-domain path.

Kumar, et al.            Expires August 9, 2021                [Page 18]

Internet-Draft                  BIER Ping                  February 2021

Header-H

The BIER header of the received Echo Request.  It may be used

to validate the DDMAP info and to populate the Incoming SI-

BitString TLV.  Also, it can be used to perform Entropy

calculation considering a different field in the header and reply

via Multipath Entropy Data Sub-TLV.

BFR MUST initialize the Best-return-code variable to the null value.

BFR will populate the Interface-I field with the identifier of the interface over which the Echo

Request is received, the top label in the MPLS stack of the received

Echo Request to BIER-Label-L, and the BIER header to BIER-Header.  If

the received Echo Request carries Target SI-BitString TLV, a BFR

SHOULD run boolean AND operation between BitString in Header-H and

BitString in Target SI-BitString TLV.  If the resulting BitString is

all-zero, reset Reply-Flag=0 and go to section 4.5.  Else:

o  If the BIER-Label-L does not correspond to the local label

assigned for {sub-domain, BitStringLen, SI} in Original SI-

BitString TLV, Set the Best-return-code to "Set-Identifier

Mismatch" and Go to section 4.5.

*  /* This detects any BIER-Label to {sub-domain, BitStringLen,

SI} synchronization problem in the upstream BFR causing any

unintended packet leak between sub-domains */

o  Set the Best-return-code to "One or more of the TLVs was not

understood" if any of the TLVs in the Echo Request message is not

understood.  Go to section 4.5.

o  If the BitString in Header-H does not match the BitString in

Egress BitString Sub-TLV of DDMAP TLV, set the Best-return-code to

"DDMAP Mismatch" and go to section 4.5.  When there are more than

one DDMAP TLV in the received Request packet, the Downstream

Address and Downstream Interface Address should be matched with

Interface-I to identify the right DDMAP TLV and then perform the

BitString match.

*  /* This detects any deviation between the BIER control plane and

BIER forwarding plane in the previous hop that may result in

loop or packet duplication.  */

o  Set the Best-return-code to "Invalid Multipath Info Request", when

the DDMAP TLV carries Multipath Entropy Data Sub-TLV, and if the

Target SI-BitString TLV in the received Echo Request carries more

than 1 BFER id.  Go to section 4.5.  Else, list the ECMP

downstream neighbors to reach BFR-id in Target SI-BitString TLV,

Kumar, et al.            Expires August 9, 2021                [Page 19]

Internet-Draft                  BIER Ping                  February 2021

calculate the Entropy considering the BitString in Header-H and

Multipath Entropy Data Sub-TLV from received Echo Request.  Store

the Data for each Downstream interface in a temporary variable.

Set the Best-return-code to 5 (Packet-Forward-Success) and goto

Section 4.5

*  /* This instructs to calculate the Entropy Data for each

downstream interface to reach the BFER in Target SI-BitString

TLV by considering the incoming BitString and Entropy Data.*/

o  Set the Best-return-code to "Replying router is the only BFER in

BIER header Bitstring", and go to section 4.5 if the responder is

BFER and there are no more bits in BIER header Bitstring left for

forwarding.

o  Set the Best-return-code to "Replying router is one of the BFER in

BIER header Bitstring", and include Downstream Mapping TLV, if the

responder is BFER and there are more bits in BitString left for

forwarding.  Also, include the Multipath information as defined in

Section 4.2 if the received Echo Request carries Multipath Entropy

Data Sub-TLV.  Go to section 4.5.

o  Set the Best-return-code to "No matching entry in forwarding

table", if the forwarding lookup defined in section 6.5 of

[RFC8279] does not match any entry for the received BitString in

BIER header.

*  /* This detects any missing BFR-id in the BIER forwarding

table.  It could be noted that it is difficult to detect such

missing BFR-id while sending the Request with more than one

BFR-id in BitString and so may need to include the BFER id that

is not responding to detect such failure.*/

o  Set the Best-return-code to "Packet-Forward-Success", and include

Downstream Mapping TLV.  Go to section 4.5

4.5.  Sending Echo Reply

If Reply-Flag=0, BFR MUST release the variables and MUST not send any

response to the Initiator.  If Reply-Flag=1, proceed as below:

The Responder BFR SHOULD include the BitString from Header-H to

Incoming SI-BitString TLV and include the Set ID, Sub-domain ID and

BS Len that corresponds to BIER-Label-L.  Responder BFR SHOULD

include the Upstream Interface TLV and populate the address from

Interface-I.

Kumar, et al.            Expires August 9, 2021                [Page 20]

Internet-Draft                  BIER Ping                  February 2021

When the Best-return-code is "Replying BFR is one of the BFER in

header Bitstring", it MUST include Responder BFER TLV.

If the received Echo Request had DDMAP with Multipath Entropy Data

Sub-TLV, Responder BFR MUST include DDMAP as defined in

Section 3.3.4 for each outgoing interface over which the packet

will be replicated and include the respective Multipath Entropy

Data Sub-TLV.  For each outgoing interface, respective Egress

BitString MUST be included in DDMAP TLV.

If the received Echo Request had DDMAP without Multipath Entropy

Data Sub-TLV, Responder BFR MUST include DDMAP as defined in

Section 3.3.4 for each outgoing interface over which the packet

will be replicated.  For each outgoing interface, respective

Egress BitString MUST be included in DDMAP TLV.

When the Best-return-code is "Replying BFR is the only BFER in header

Bitstring", it MUST include Responder BFER TLV.

The Responder MUST set the Message Type as 2 and Return Code as Best-

return-code.

The Echo Reply can be sent either as BIER-encapsulated or IP/UDP

encapsulated depending on the Reply mode in received Echo Request.

When the Reply mode in received Echo Request is set to 3, Responder

appends BIER header listing the BitString with BFIR ID (from Header-

H), set the Proto to 5 and set the BFIR as 0.  When the Reply mode in

received Echo Request is set to 2, Responder encapsulates with IP/UDP

header.  The UDP destination port MUST be set to TBD1, and the source port

MAY be set to TBD1 or other random local value.  The source IP is any

local address of the responder, and the destination IP is derived from

Reply-To TLV.

4.6.  Receiving Echo Reply

Upon receiving Echo Reply, the Initiator will use the Sender's Handle to

match with Echo Request sent.  If no match is found, the Initiator

MUST ignore the Echo Reply.

If receiving Echo Reply have Downstream Mapping, the Initiator SHOULD

copy the same to subsequent Echo Request(s).

If one of the Echo Reply is received with Return Code as "Replying

BFR is one of the BFER in header Bitstring", it SHOULD reset the BFR-

id of the responder from Target SI-BisString TLV in subsequent Echo

Request.

Kumar, et al.            Expires August 9, 2021                [Page 21]

Internet-Draft                  BIER Ping                  February 2021

/* This helps to avoid any BFR that is both BFER and also transit

BFR to continuously responding with Echo Reply.*/

5.  IANA Considerations

This document requests a UDP port TBD1 to be allocated by IANA for BIER

Echo.

This document requests IANA to create and manage of below-listed

registries and sub-registries:

5.1.  BIER OAM Registry

IANA is requested to create and maintain "BIER OAM Parameters"

registry.

5.2.  Message Types, Reply Modes, Return Codes

IANA is requested to create an "Message Type" sub-registry under "BIER

OAM Parameters" registry and assign the Message Types defined in

section 3.1

Also, IANA is requested to create "Echo Reply Mode" sub-registry under

"BIER OAM Parameters" registry and assign the Echo Reply Modes

defined in section 3.1

IANA is requested to create an "Echo Return Codes" sub-registry under

"BIER OAM Parameters" registry and assign the Return Codes defined in

section 3.2

5.3.  TLVs

The TLVs and Sub-TLVs defined in this document is not limited to Echo

Request or Reply message types and is applicable for other message

types.  The TLVs and Sub-TLVs requested by this document for IANA

consideration are the following:

Type        Sub-Type            Value Field

-------      --------            -----------

1                               Original SI-BitString

2                               Target SI-BitString

3                               Incoming SI-BitString

4                               Downstream Mapping

4              1                Multipath Entropy Data

4              2                Egress BitString

5                               Responder BFER

6                               Responder BFR

7                               Upstream Interface

Kumar, et al.            Expires August 9, 2021                [Page 22]

Internet-Draft                  BIER Ping                  February 2021

6.  Security Considerations

The security consideration for BIER Ping is similar to ICMP or LSP

Ping.  As like with ICMP or LSP ping, BFR may be exposed to Denial-of-

Service (DoS) attacks, and it is RECOMMENDED to regulate the BIER Ping

packet flow to the control plane.  A rate limiter SHOULD be applied to

avoid any attack.

As with ICMP or LSP Ping, a traceroute can be used to obtain network

information.  It is RECOMMENDED that the implementation checks the

integrity of BFIR of the Echo messages against any local secured list

before processing the message further

7.  Acknowledgement

The authors would like to thank Antoni Przygienda, Eric Rosen, Faisal

Iqbal Jeffrey (Zhaohui) Zhang and Shell Nakash for their review and

comments.

The authors would like to thank Mankamana Mishra for his thorough

review and comments.

8.  References

8.1.  Normative References

[RFC2119]  Bradner, S., "Key words for use in RFCs to Indicate

Requirement Levels", BCP 14, RFC 2119,

DOI 10.17487/RFC2119, March 1997,

<https://www.rfc-editor.org/info/rfc2119>.

[RFC5905]  Mills, D., Martin, J., Ed., Burbank, J., and W. Kasch,

"Network Time Protocol Version 4: Protocol and Algorithms

Specification", RFC 5905, DOI 10.17487/RFC5905, June 2010,

<https://www.rfc-editor.org/info/rfc5905>.

[RFC8029]  Kompella, K., Swallow, G., Pignataro, C., Ed., Kumar, N.,

Aldrin, S., and M. Chen, "Detecting Multiprotocol Label

Switched (MPLS) Data-Plane Failures", RFC 8029,

DOI 10.17487/RFC8029, March 2017,

<https://www.rfc-editor.org/info/rfc8029>.

[RFC8279]  Wijnands, IJ., Ed., Rosen, E., Ed., Dolganow, A.,

Przygienda, T., and S. Aldrin, "Multicast Using Bit Index

Explicit Replication (BIER)", RFC 8279,

DOI 10.17487/RFC8279, November 2017,

<https://www.rfc-editor.org/info/rfc8279>.

Kumar, et al.            Expires August 9, 2021                [Page 23]

Internet-Draft                  BIER Ping                  February 2021

[RFC8296]  Wijnands, IJ., Ed., Rosen, E., Ed., Dolganow, A.,

Tantsura, J., Aldrin, S., and I. Meilik, "Encapsulation

for Bit Index Explicit Replication (BIER) in MPLS and Non-

MPLS Networks", RFC 8296, DOI 10.17487/RFC8296, January

2018, <https://www.rfc-editor.org/info/rfc8296>.

8.2.  Informative References

[RFC0792]  Postel, J., "Internet Control Message Protocol", STD 5,

RFC 792, DOI 10.17487/RFC0792, September 1981,

<https://www.rfc-editor.org/info/rfc792>.

[RFC6291]  Andersson, L., van Helvoort, H., Bonica, R., Romascanu,

D., and S. Mansfield, "Guidelines for the Use of the "OAM"

Acronym in the IETF", BCP 161, RFC 6291,

DOI 10.17487/RFC6291, June 2011,

<https://www.rfc-editor.org/info/rfc6291>.

[RFC6424]  Bahadur, N., Kompella, K., and G. Swallow, "Mechanism for

Performing Label Switched Path Ping (LSP Ping) over MPLS

Tunnels", RFC 6424, DOI 10.17487/RFC6424, November 2011,

<https://www.rfc-editor.org/info/rfc6424>.

[RFC6425]  Saxena, S., Ed., Swallow, G., Ali, Z., Farrel, A.,

Yasukawa, S., and T. Nadeau, "Detecting Data-Plane

Failures in Point-to-Multipoint MPLS - Extensions to LSP

Ping", RFC 6425, DOI 10.17487/RFC6425, November 2011,

<https://www.rfc-editor.org/info/rfc6425>.

[RFC8444]  Psenak, P., Ed., Kumar, N., Wijnands, IJ., Dolganow, A.,

Przygienda, T., Zhang, J., and S. Aldrin, "OSPFv2

Extensions for Bit Index Explicit Replication (BIER)",

RFC 8444, DOI 10.17487/RFC8444, November 2018,

<https://www.rfc-editor.org/info/rfc8444>.

Authors' Addresses

Nagendra Kumar

Cisco Systems, Inc.

7200 Kit Creek Road

Research Triangle Park, NC  27709

US

Email: naikumar@cisco.com

Kumar, et al.            Expires August 9, 2021                [Page 24]

Internet-Draft                  BIER Ping                  February 2021

Carlos Pignataro

Cisco Systems, Inc.

7200 Kit Creek Road

Research Triangle Park, NC  27709-4987

US

Email: cpignata@cisco.com

Nobo Akiya

Big Switch Networks

Japan

Email: nobo.akiya.dev@gmail.com

Lianshu Zheng

Individual Contributor

China

Email: veronique_cheng@hotmail.com

Mach Chen

Huawei Technologies

Email: mach.chen@huawei.com

Greg Mirsky

Ericsson

Email: gregimirsky@gmail.com

Kumar, et al.            Expires August 9, 2021                [Page 25]

# Comments

So, it MAY not be considered as the sanity check failure? How it can be processed then?

So, it MAY not be considered as the sanity check failure? How it can be processed then?

Should we use the normative? E.g., “MUST be set”? Or remove “by default” and re-word to “When the Reply mode is set to 2 …”?

I think there must be normative form. Is it a MUST?

Normative?

Normative?

Is this a footnote or simply an informative text? If the latter, do we need to present it as comments?

This looks like the Editor’s Note. Should it be removed before the publication?