## Slide 1: Problem Statement and Requirement for CASM Coordinated Address Space Management draft-xie-ps-centralized-address-management-02 draft-kumar-casm-problem-and-use-cases-00
Chongfeng Xie, Qiong Sun (China Telecom)
Weiping Xu, Will Liu (Huawei)
Ian Farrer, Normen Kowalewski (Deutsche Telekom AG)
Ying Cheng (China Telecom)
Rakesh Kumar, Anil Lohiya (Juniper Networks)
Marc Blanchet (Viagenie)
Fioccola Giuseppe (Telecom Italia)
Declan Ma (ZDNS)
Notes: <number>

## Slide 2: Description
Organizations use IP Address Space Management (IPAM) tools to manage their IP address space, often with proprietary database and interfaces.
This work intends to evolve IPAM into standardized interfaces for coordinated management of IP addresses, including SDN/NFV networks and other forms of virtualization.
Use cases include dynamic allocation and release of IP addresses and prefixes based on usage (reallocation in case of no more in use) and/or user intent (for specific services).
Clarify the relationship vs DHCP?
Coordinated?
vs Anima?

## Slide 3: Use Cases List
Address pools configuration on BNGs / IPv6 transition devices
  DHCP server pool
  Static address configuration
  //DHCP v6 delegation
Address configuration API of IPAM
  NAT & CGN
  Public IP address pool
SDN controllers
//Tried to merge all the use cases in two drafts, may need to discuss, multicast was removed as it’s not widely used

## Slide 4: Use case 1 – sharing address among devices
BRAS
AAA
Client
Configured with IPv4/v6 address pools, and announce the corresponding routing into Internet
Access request
Authentication
Configured with user domain for subscribers
Allocate address from user domain address pools
Address allocation in broadband access users
Our problem:
  With address shortage problem, the remaining IPv4 address pools are usually quite scattered.
  It is complicated to manually configure all the address pools statically in BNGs (large MAN may have more than 100 BNGs).
  Sometimes, the address pools are needed to be transited from one BNG to another.
Address sharing among devices

## Slide 5: Use case 2 - sharing address among functions
Our problem
  For IPv6 transition technologies, e.g. DS-Lite, lw4over6, etc., they need to be configured with address pools as translated addresses.
  Different address pools are needed to be configured on each transition instance for HA support.
  The occupation of the address pools may vary during different transition periods.
DS-Li te/CGN
Configured with IPv4 address pools, and announce the corresponding routing into Internet
For HA support, different address pools are needed to configure in one CGN device
Client
DS-Li te/CGN
Access with private addr
Translate to public address
Access to a backup device
Translate to public address
Failover occurs
It is too complicated to configure all these address pools manually
Address sharing among functions

## Slide 6: Use case 3 - IPAM
Address configuration API of IPAM
MNS/OSS and IPAM perform address management on different levels of granularity

## Slide 7: Use case 4 - NAT & CGN //to be added later

## Slide 8: Use case 5-6 in draft-kumar-casm-problem-and-use-cases-00 to be added later

## Slide 9: Problem of current solution
Lack of common set of standard interfaces across IPAM system vendors
Address usually allocated with very little or no context
Lacks ability to annotate requests with user-defined attributes as private or public address // please help to explain
MAC address and network segment (VLAN) does not given enough information about user or usages // Please check whether we need layer 2
Lack of built-in multi-tenancy into interfaces // please add more details
Lack of information about address requester such as virtual or physical device
Lack of integration with name services such as DNS //suggest to remove as there is no use case
Lack of integration with DHCP server to get address records
Lack of integration with address translation services such as NAT44 and NAT64// suggest to add DS-lite as v6 transition

## Slide 10: Requirement
General operational requirements // This is about NBI, shall we add one use case?
  Multi-tenancy
  Authentication and Authorization
  Audit Logging
  Error notification
  Aggregated view
  Dynamic allocation and reclaiming
  Generic address assignment policies
Interface modeling requirements
  Functional attributes such as switch, router, firewall, server, end-point
  Form-factoral attributes such as physical, virtual
  Operational attributes such as management plane, control plane, data plane
  Network segment identifier, such as VLAN, VxLAN or other user-defined value
  Network segment type such as point-to-point, multi-point, loopback
  Addressing scope attributes such as private, public, VPN, unicast, multicast
  Extensible user-defined attributes
Functional requirements
  Address pools: Unicast(Private/Public v4 addresses, v6 addresses), Multicast
  Pool management: Address management, General management
Integration with other address services
  DHCP server, DNS server, NAT device, BNG device //suggest to discuss whether we put DNS here
Notes: China Unicom will present this page
Multi-tenancy: All interfaces exposed by CASM system must be multi-tenant capable. This is highly desirable for cloud based network management solutions. It may also be applicable for a service provider with different managed services use-case scenario.
Autentication and Authorization: All interfaces exposed by CASM system must support an authentication scheme. It also highly desriable to support operational restrictions on certain resources based on identity for security reasons.
Audit Logging: All CASM actvities must be logged for auditing or debugging purposes. The system must provide an interface to access these records.
Error notification: All interfaces exposed by CASM system must support error handling and user-defined error notification mechanism suh as alert or email. There may also be need to take corrective action for autonomus operation.
An integrated, centralized IP address management is desirable as it offers an aggregated view on all stages of the life cycle of IP address resources, from selection, allocation, assignment to reclaiming them into to free resources in an optimized and efficient way.
The approach needs to be much more dynamic and act on a much finer granularity than in the past, since address consumption in each device is changing over time, and resource usage can dynamically change over time based on actual user, service, traffic or session volume. A fast return of unused resources for reassignment is of high value.
IP address resource assignment policies have to be adaptable to a broad variety of usage scenarios and multiple types of network entities - physical and virtual. Examples are various types of network IP equipment, i.e., BNG, vBNG, CGN, FW, etc, which all need to be supported with resources - directly or indirectly - through the same IP address management server.
IP address management needs to be cable of handling IPv4 and IPv6 resources, including sub-netting, and prefixes in any valid configurable prefix length. All well defined and RFC covered address types should be administrable.
Overlapping pools of private addresses must be supported.
<number>

## Slide 11: Discussion
Do you have similar address management problem in your network ?
What’s the current approach for address management in your network ?
Is it useful to have a common address management specification?
Do you have same requirement in your network?
Do you have interests to work on this topic ?
Notes: <number>