## Slide 1: Architecture for CASM Coordinated Address Space Management draft-li-casm-address-pool-management-architecture-00 draft-kumar-casm-requirements-and-framework-00
Chen Li, Chongfeng Xie(China Telecom),
Jun Bi(Tsinghua University)
Weiping Xu(Huawei)
Rakesh Kumar, Anil Lohiya(Juniper)
Marc Blanchet(Viagenie)
Notes: <number>

## Slide 2: Overall Address Management Architecture
Coordinated Address Space Management System (CASM)
BNG,vBNG,C/U BNG
V6transition, firewall
DHCPv4 Server
DHCPv6 Server
CPE
DHCP, PPP,etc
CPE
DHCP, PPP,etc
CPE
IPv6 Prefixs Delegation
HOST
DHCP
3rd Party
OSS/BSS
ADMIN
Log Server
NAT
HOST
IP
Address Space Management & Control
…
What legacy mean?
Does “SDN” in the architecture draft means SDN controller?
Is the position right, up or down to the CASM System？

## Slide 3: Workflow for BNG use case
Address Space Management System
BNG
HOST
HOST
CPE
vBNG
HOST
HOST
CPE
C/U BNG
HOST
HOST
CPE
Specify:
  BNG initiates address pool request for desired sized of address.
  Management System allocates address pool and reply the BNG
  BNG issues an renew request if the lifetime is going to expire
  BNG keeps monitoring and reports the current usage of the current address pool
To manage the public IP address resource effectively and avoid the manual configuration mechanism
DHCP, PPP,etc
DHCP, PPP,etc
DHCP, PPP,etc

## Slide 4: Workflow for public IP address pool （NAT/CGN）use case
Address Space Management System
NAT
HOST
DHCP
HOST
HOST
CGN
HOST
DHCP
HOST
HOST
NAT
HOST
DHCP
HOST
HOST
Specify:
  Allocate the public IP address pools on NAT device
  Release the free public IP address pools
  Public IP address pool, port-set, translation policy configuration,

## Slide 5: Workflow for cloud enterprise use case
Address Space Management System
vDHCP
CPE
HOST
VM
vDHCP
Specify:
  Management System configure the IP address pool on the LAN side of CPE.
  Management System configure the IP address pool on the WAN side of CPE.
  Management System configure the IP address pool of VM in DC
To manage the public IP address resource effectively and avoid the manual configuration mechanism
Cloud enterprise
CPE
HOST
VM
Cloud enterprise
Notes: <number>

## Slide 6: Workflow for DHCPv4 use case
Address Space Management System
DHCPv4 Server
HOST
DHCP
HOST
HOST
DHCPv4 Server
HOST
DHCP
HOST
HOST
DHCPv4 Server
HOST
DHCP
HOST
HOST
Specify:
  An address Space management system used to initialize multiple address pools on DHCP servers for HOSTS
  Configure DHCP statically, if the DHCP server is ever replaced, the new server must be configured with the same old pool.

## Slide 7: Workflow for DHCPv6 delegation use case
Address Space Management System
DHCPv6 Server
CPE
DHCPv6 Server
DHCPv6 Server
Specify:
  Management System configure the IPv6 prefixs for CPE on DHCPv6 server
  The DHCPv6 Server then assign the corresponding IPv6 prefix to CPE.
IPv6 Prefixs Delegation
IPv6 Prefixs Delegation
IPv6 Prefixs Delegation
HOST
CPE
HOST
CPE
HOST

## Slide 8: Q&A
Where to place the SDN controller on the architecture?

## Slide 9: The following pages are backup slides

## Slide 10: Workflow for Static address configuration use case
Address Space Management System
Device
Device
Device
Specify:
  Address space management system configure address statically on devices without DHCP support.
The devices are lack of DHCP client functionality, or lack of DHCP server available in the network segment for whatever reason.
Without DHCP
Without DHCP
Without DHCP

## Slide 11: Workflow for multicast IP address pool use case
Address Space Management System
multicast content distributor
multicast content distributor
multicast content distributor
Specify:
this use case is not clear

## Slide 12: Detail procedure for BNG use case
Operators will configure remaining address pools centrally in the Address Pool Management Server.
1
The agent will initiate AddressPool reqeust to the APMS. APMS lookups the remaining address pool in its local database. It will then allocate a set of address pools to the agent.
2
If the lifetime of the address pool is going to expire, the agent should issue an AddressPoolRenew request to extend the lifetime.
3
The AddressPoolReport module keeps monitoring and reports the current usage of the current address pools.
4

## Slide 13: Detail procedure for BNG use case
Initial Address Pool Configuration
Address Pool Status Report

## Slide 14: Detail procedure for BNG use case
Address Pool Status Query
Address Pool Release