## Slide 1: draft-finn-detnet-bounded-latency Introduction
DetNet working group, IETF100, November, 2017
Norman Finn, Huawei

## Slide 2: Status. Abstract. Justification.
Individual draft. Incomplete.
Abstract: This document [provides] a model for DetNet to achieve bounded latency and zero congestion loss using existing and in-progress standards from IEEE 802 and RFCs from IETF.
  This goal is not achieved in this first version of the draft.
We have been talking a lot about packet replication, but DetNet’s primary features are bounded latency and zero congestion loss. These require an accurate, not approximate, computation of:
  The worst-case latency that a flow can experience; and
  The amount of buffer space required at each hop.

## Slide 3: Accurate numbers
Without accurate numbers for latency, DetNet is useless.
Without accurate numbers for buffer requirements, DetNet is too expensive to implement.
This hop’s buffer requirements depend strongly on the details of previous hops’ transmission selection algorithms.
So, accurate numbers require detailed descriptions and/or parameterization of queuing and transmission selection algorithms.
No single queuing and transmission selection algorithm will satisfy all of the DetNet use cases.

## Slide 4: What queuing and selection algorithms?
RFC 2963 “A Rate Adaptive Shaper for Differentiated Services” is being used, today, to implement DetNet-type services.
Several queuing and transmission selection algorithms are precisely defined in IEEE Std 802.1Q and its amendments, and are being used to implement DetNet-type services. Furthermore, 802.1Q defines exactly how these different 802.1Q methods interact with each other.
But, in IEEE Std 802.1Q, the definitions of the queueing and transmission selection algorithms are embedded in, and intimately tied to, the definition of a bridge – not a router or end system.

## Slide 5: Progress in IEEE 802.1 (this author’s opinion)
A project is under discussion* (≠ “started”!!) in IEEE 802.1 Time-Sensitive Networking Task Group to create a new document, “Quality of Service Provision for Non-Bridges”. This would specify how a device that is not a Bridge can apply the 802.1Q queuing and transmission selection algorithms. This would:
  Provide easy points of reference for IEEE, IETF, or other SDOs’ documents to call out 802.1Q queuing and transmission selection algorithms;
  Provide an entry to 802.1Q for implementers who want to build these queues, but do not care about the intricacies of bridges.
* The January 802.1 interim is authorized to prepare a Project Authorization Request to submit to the 802 Executive Committee at the March plenary.

## Slide 6: Whither draft-finn-detnet-bounded-latency?
It is the author’s intention that this draft eventually be a companion to the new 802.1 standard, defining at least one set of choices for 802.1 and/or IETF queuing definitions for implementing at least one class of DetNet service.
Whether the new 802.1 standard, or some development of draft-finn-detnet-bounded-latency, explains how to integrate RFC 2963 (or others) with bridging queues is To Be Determined.
Additional ideas / authors are welcome.

## Slide 7: Discussion