## Slide 1: DetNet Data Plane
DetNet Data Plane design team update
IETF 99, Prague, 2017

## Slide 2: Outline
Design team
Solution
Open issues
Next steps

## Slide 3: Design team
Members
  Jouni Korhonen (lead)
  Carlos Bernardos
  Loa Andersson
  Yuanlong Jiang
  Norm Finn
  Balazs Varga
  Janos Farkas
  Tal Mizrahi
  David Mozes

## Slide 4: Design team update cont’d
Weekly calls held...
Other stuff found at the mailing list:
  https://mailarchive.ietf.org/arch/search/?email_list=detnet-dp-dt

## Slide 5: Use cases – IEEE 802.1TSN over DetNet
(*) draft-dt-detnet-dp-sol-01
End Systems initiates / terminates IEEE802.1 TSN traffic..

## Slide 6: Use cases – PW-based native DetNet
(*) draft-dt-detnet-dp-sol-01
End Systems initiates / terminates PWs over MPLS..

## Slide 7: Use case – Native IPv6-based DetNet
End Systems initiates / terminates IPv6 packets with DetNet “support”

## Slide 8: Solution basics
Leverages RFC6073 Multi-Segment PseudoWires or IPv6.
Designed to work with existing control planes
  E.g. LDP, RSVP-TE, SR (for MPLS PWs) and centralized controller.
  Small updates are inevitable, though.
  Control plane for native IPv6 has not been discussed too much yet.
Maximize the reuse of existing solutions and implementations:
  Extend only where needed & mandatory for solution to work.
  No new functionality unless really necessary.

## Slide 9: Hard issues to get agreement
Unified encapsulation for all types of traffic..
  End result was – two encapsulations.
  Native IPv6 and MPLS PWs.
DetNet flow identification:
  A PW Label for MPLS PWs. There is no “dedicated” DetNet label per se.
  A flow label for Native IPv6.
Service protection:
  Packet Replication and Elimination for Redundancy (PREF).
  Also need to differentiate between DetNet compound and member flows..

## Slide 10: Packet formats with MPLS PWs
DetNet data plane encapsulation:
  Always has a PW label.
  Always has a CW.
Topology/service “S-label” for overlays to connect only desired set of PE nodes:
  Exposes PW label only when needed.
  A node can be treated as a P node or a PE node within an overlay.
(*) draft-dt-detnet-dp-sol-01

## Slide 11: Packet formats with Native IPv6
DetNet native IPv6 data plane encapsulation:
  Always has a DetNet DstOpt for “control word”.
  Always has a Flow Label set to Flow-ID.
For explicit routes DstOpt works well for unicast flows e.g., with Segment Routing.
(*) draft-dt-detnet-dp-sol-01

## Slide 12: Packet formats cont’d
IPv6 makes use of Destination Options – new option needed.
Required for packet Replication and Elimination Function (PREF).
PW Control Word is the same as for Ethernet over MPLS (RFC4448).
Required for packet Replication and Elimination Function (PREF).
(*) draft-dt-detnet-dp-sol-01

## Slide 13: Flow identification..
Integral part of DetNet flow processing. Flow identification has two key aspects (MPLS PSN example):
  At the forwarding and queuing level:
    Flow identification implicitly part of FEC and encoded into label(s) and TC bits.
    May identify an aggregate of DetNet flows or individual flows (e.g., a FEC per flow).
  As part of the Packet Replication and Elimination Function:
    Flow lookup based on the PW Label and accompanied with the CW SeqNum to detect whether a packet has already be seen.
    Done within the PseudoWire (extended forwarder) function.
    Note: replication is basically a reuse of 1+1 protection mechanism.

## Slide 14: Open issues
Few topics are still under work:
  Interworking between MPLS and IPv6 DetNet flows/transports.
Control plane is another topic… out of scope for this I-D. However...
  The design team did consider it as well to some extent.
  Controlling PREF function, resource reservations, etc…
Multicast DetNet flows:
  The design team did not discuss this thoroughly..
Relay and Edge node processing clarifications for native IPv6.
  E.g. whether PREF can be done in anywhere else than in end hosts and edge nodes.
Management and control considerations..

## Slide 15: Next steps..
Call for adoption as a WG Item!!
  We acknowledge there is plenty of work to do.. but the current draft should work as a good basis for the final solution.