## Slide 1: DetNet Data Plane
draft-dt-detnet-dp-sol-01
DetNet Data Plane design team update
IETF 99, Prague, 2017

## Slide 2: Outline
Design team
Solution
Open issues
Next steps

## Slide 3: Design team
Members
  Jouni Korhonen (lead)
  Carlos Bernardos
  Loa Andersson
  Yuanlong Jiang
  Norm Finn
  Balazs Varga
  Janos Farkas
  Tal Mizrahi
  David Mozes

## Slide 4: Design team update cont’d
Weekly calls held...
Other stuff found at the mailing list:
  https://mailarchive.ietf.org/arch/search/?email_list=detnet-dp-dt

## Slide 5: Use case – IEEE 802.1TSN over DetNet
End Systems initiates / terminates IEEE802.1 TSN traffic..
With MPLS PSN this is an MS-PW T-PE with DetNet extensions i.e.,
DA-T-PE..
With MPLS PSN this is an MS-PW S-PE with DetNet extensions i.e., DA-S-PE..
(*) draft-dt-detnet-dp-sol-01

## Slide 6: Use case – PW-based DetNet
End Systems initiates / terminates PWs over MPLS..
With MPLS PSN this is an MS-PW S-PE with DetNet extensions i.e., DA-S-PE..
(*) draft-dt-detnet-dp-sol-01

## Slide 7: Use case – Native IPv6-based DetNet
End Systems initiates / terminates IPv6 packets with DetNet “support”
(*) draft-dt-detnet-dp-sol-01

## Slide 8: Mixing use cases..
Combining “IEEE 802.1TSN over DetNet” and “PW-based native DetNet” use cases is rather straight forward:
  The PW encapsulation/de-capsulation either takes place in an end station or an edge node.
  However, interworking function still required at the edge node between 802.1TSN and PW e.g., when it comes to sequence numbers etc.
Combining PW-based and “native IPv6” use cases:
  Interworking needs some more tinkering. Probably trying to cover all possible combinations makes no sense (e.g., non-DetNet aware end station talks IPv6 to native IPv6 DetNet-aware end station over 802.1TSN interconnect..)

## Slide 9: Solution basics
Uses PseudoWires (with MPLS PSN) and IPv6 as the data plane encapsulation solutions.
Designed to work with existing control planes
  E.g. LDP, RSVP-TE, SR (for MPLS PWs) and centralized controller.
  Small updates are inevitable, though.
  Control plane for native IPv6 has not been discussed too much yet.
Maximize the reuse of existing solutions and implementations:
  Extend only where needed & mandatory for solution to work.
  No new functionality unless really necessary.

## Slide 10: Hard issues to get agreement
Unified encapsulation for all types of traffic..
  End result was – two encapsulations.
  Native IPv6 and MPLS PWs.
DetNet flow identification:
  A PW Label for MPLS PWs. There is no “dedicated” DetNet label per se.
  A flow label for Native IPv6.
Service protection:
  Packet Replication and Elimination for Redundancy (PREF).
  Also need to differentiate between DetNet compound and member flows..

## Slide 11: Packet formats with MPLS PWs encapsulation
DetNet flow:
  Flow-ID -> PW label.
  SeqNum -> CW.
S-Label:
  A DetNet node to DetNet node "service" label that is used between DA-*-PE devices (see slide 5).
T-Label:
  Used to identify the LSP used to transport a DetNet flow across an MPLS PSN, e.g., a hop-by-hop label used between LSRs.
(*) draft-dt-detnet-dp-sol-01

## Slide 12: Packet formats with Native IPv6 encapsulation
DetNet flow:
  Flow-ID -> Flow Label.
  SeqNum -> DetNet DstOpt.
For explicit routes DstOpt works well for unicast flows e.g., with Segment Routing.
(*) draft-dt-detnet-dp-sol-01

## Slide 13: Packet formats cont’d
IPv6 makes use of Destination Options – new option needed.
Required for packet Replication and Elimination Function (PREF).
PW Control Word is the same as for Ethernet over MPLS (RFC4448).
Required for packet Replication and Elimination Function (PREF).
(*) draft-dt-detnet-dp-sol-01

## Slide 14: Flow identification..
Integral part of DetNet flow processing. Flow identification has two key aspects (MPLS PSN example):
  At the forwarding and queuing level:
    Flow identification implicitly part of FEC and encoded into label(s) and TC bits.
    May identify an aggregate of DetNet flows or individual flows (e.g., a FEC per flow).
  As part of the Packet Replication and Elimination Function:
    Flow lookup based on the PW Label and accompanied with the CW SeqNum to detect whether a packet has already be seen.
    Done within the PseudoWire (extended forwarder) function.
    Note: replication is basically a reuse of 1+1 protection mechanism.

## Slide 15: Other data plane considerations
Class of Service:
  CoS for DetNet flows with PWs (and MPLS PSN) encapsulation rely on RFC3270 described DiffServ architecture.
  CoS for DetNet flows with IPv6 encapsulation rely on DiffServ DSCP code points and related mechanisms.
  Plus some other considerations.
Quality of Service:
  A baseline set of QoS capabilities for DetNet flows carried in PWs and MPLS can provided by MPLS with Traffic Engineering (MPLS-TE) and the related control planes..
  IPv6 should leverage the underlying network layer such as 802.1TSN.
Cross-DetNet flow resource aggregation:
  The data plane implications of aggregation are independent for MPLS/PW and IP encapsulated DetNet flows, and should leverage existing work e.g., hierarchical LSPs.

## Slide 16: Other data plane considerations cont’d
Bidirectional traffic:
  How bidirectional traffic between two end stations are handled (e.g., associated & co-routed bidirectional flows in a case of LSP), fate sharing, ensuring the same path, etc.
Layer 2 addressing and QoS Considerations:
  Background: how baseline TSN standards identify TSN streams (e.g. DetNet flows), use VLAN tags, multicast destination addresses, etc..
Interworking between PW- and IPv6-based encapsulations
  Currently TBD. See slides 8 and 17.

## Slide 17: Time Synchronization
A full section added with time-synchronization related considerations within DetNet deployments..

## Slide 18: Open issues
Few topics are still under work:
  Interworking between MPLS and IPv6 DetNet flows/transports.
Control plane is another topic… out of scope for this I-D. However...
  The design team did consider it as well to some extent.
  Controlling PREF function, resource reservations, etc…
Multicast destined DetNet flows:
  The data plane assumes p2p transport connectivity within the DetNet domain.
Relay and Edge node processing clarifications for native IPv6.
  E.g. whether PREF can be done in anywhere else than in end hosts and edge nodes.
Management and control considerations..

## Slide 19: Next steps..
Call for adoption as a WG Item!!
  We acknowledge there is plenty of work to do.. but the current draft should work as a good basis for the final solution.