## Slide 1: I2RS RIB Route Example
Sue Hares

## Slide 2: I2RS RIB Example
Attempt to match Andy slides with I2RS RIB model (8/31/2015)
Boiled down to IPv4 route
  128.2/16 with nexthop 1 – added by netconf config
  128.2/16 with nexthop 2 – added by I2RS RIB
  DDOS attack causes you to overwrite NETCONF config with I2RS RIB route

## Slide 3: Current Datastores
candidate
running
startup
config true;
config false;
operational data
All operational data exists alongside config=true but there is no datastore defined for config=false data nodes

## Slide 4: Current Datastores (Ext. 1)
candidate
running
startup
config true;
config false;
operational data
actual config
intended config
Conceptual intended and actual values are determined by the server as an implementation detail

## Slide 5: Route
grouping route {
description
“The common attribute used for all routes;”
uses route-prefix;
container nexthop {
uses nexthop;
}
container route-statistics {
leaf route-state {
type route-state-def;
config false; /* operational state */
}
leaf route-installed state {
type route-installed-state def;
config false;
}
leaf route-reason {
type route-reason-def;
config false;
}
}
container router-attributes {
uses router-attributes;
}
container route-vendor-attributes
uses route-vendor attributes;
}
module i2rs-rib { …
container routing-instance {
…
list rib-list {
…
list route-list {
key “route-index”;
uses route;
}
} }
operational data
Extensions

## Slide 6: Route
module i2rs-rib { …. container routing-instance { …
list rib-list { ….
list route-list {
key “route-index”;
leaf route-index {
type uint64;
mandatory true;
}
leaf route-type {
type route-type-def;
mandatory true;
}
Container match {
choice rib-route-type {….
leaf destination-ip-v4-prefix {
type inet:ipv4-prefix;
mandatory true;
}
}
}
leaf nexthop-id {
type uint32;
mandatory true;
}
leaf next-hopo-ipv4-address {
type inet:ipv4-prefix;
mandatory true
}
} }
Index for route direct reference without prefix match; Main key.
Type: ipv4, ipv6, mpls, mac, interface
Type: v4 prefix match
Index for nexthop direct index without match
IPv4 prefix
container route-statistics {
leaf route-installed state {
type route-installed-state def;
config false;
}
}
Defined as:
Installed, uninstalled

## Slide 7: Thermostat Model Equivalent
Route 128.1/16
config true;
config false;
Route 128.1/16
nexthop 1
Route-installed-state Installed
Scheduler
Client
actual config
intended config

## Slide 8: Route + Ephemeral Route
Route 128.2/16
nexthop id 1
config true;
config false;
Scheduler
Client
actual config
intended config
Add IPS
Route
ephemeral datastore
running datastore
Route 128.2/16 is not deleted by add IPS Route the desired config is over-ridden
Route 128.2/16
nexthop id 2
Route 128.1/16 nexthop 1
Route-installed-state Installed

## Slide 9: Route + Ephemeral Route
Route 128.2/16
nexthop id 1
config true;
config false;
Scheduler
Client
actual config
intended config
Add IPS
Route
ephemeral datastore
running datastore
Diagnostics test the DDOS response by altering the
Route installed in RIB
Could keep the first
Route as “not installed”
if implementation desired
Route 128.2/16
nexthop id 2
Route 128.1/16 nexthop 2
Route-installed-state Installed
Route 128.1/16 nexthop 1
Route-installed-state Not installed
DDOS
Attack
Route 128.2/16
nexthop id 2

## Slide 10: RESTCONF Example
RESTCONF Running Datastore Edit
PUT /restconf/data/i2rs-rib/instance=1/rib=IPv4/route=128.1/next-hop
{ “next-hop”:1}
RESTCONF Ephemeral Datastore Edit of config=true
PUT /restconf/data/i2rs-rib/instance=1/rib=IPv4/route=128.1/next-hop?datastore=ephemeral
{ “next-hop”:2 }
RESTCONF Ephemeral Datastore Edit of config=false
PUT /restconf/data/i2rs-rib/instance=1/rib=IPv4/route=128.1/next-hop=2/route-installed-state/datastore=ephemeral
{ “route-installed-state”: Installed }

## Slide 11: Issues
Did I replicate Andy’s example? Did I get the RESTCONF syntax right?
config=false should have some reflection on the true state of the route in the FIB
  Having installed and uninstalled route makes sense for DDOS case, but it blow up the RIB size by those number
  Implementations could immediately clean uninstalled routes out.
Does Andy’s example mean that I2RS RIB and the Routing RIB need to be aligned?
  Right now the two are in the same general area, but not aligned.
  Could do this if it helped make deployments easier.
Not sure where ephemeral false would go?
Can another client query for a list of what routes come from the I2RS RIB for the IPv4 RIB?

## Slide 12: Summary
Both config=true and config=false nodes can be edited in the ephemeral datastore
  this datastore overrides normal intended config and actual config (implementation details)
Edit and validation rules for ephemeral datastore can be different than for the running datastore
  Actual rules TBD but cannot reference data that is “less stable” than the current context
  Want to minimize performance overhead; maybe even provide mode where YANG validation rules are skipped

## Slide 13: From I2RS Yang module to short ROUTE
Backup on creating the shorten route

## Slide 14
grouping route {
description
“The common attribute
used for all routes;”
uses route-prefix;
container nexthop {
uses nexthop;
}
….
}
grouping route-prefix {
description “common
attributes use for all routes”;
leaf route-index {
type uint64;
mandatory true;
}
leaf route-type {
type route-type-def;
mandatory true;
}
container match {
choice rib-route-type {
… ipv4
… ipv6
… mpls
… mac
}
}
case ipv4 {
description
“match on destination IP
address in header”;
container ipv4 {
leaf ipv4-route-type {
type ip-route-type def;
mandatory true;
}
choice ip-route-type {
case destination-ipv4-address {
leaf destination-ipv4-prefix {
type inet:ipv4-prefix
mandatory true;
}
case destination-source-ipv4-address
…..
}
}
module i2rs-rib { …
container routing-instance {
…
list rib-list {
…
list route-list {
key “route-index”;
uses route;
}
} }
grouping nexthop {
leaf nexthop-id {
mandatory true;
type uint32;
}
choice next-hop-type {
case next-hop base {
list nexthop-chain {
key “nexthop-chain-id”;
uses nexthop-chain-member;
}
}
}

## Slide 15: Route info
grouping route {
description
“The common attribute
used for all routes;”
uses route-prefix;
container nexthop {
uses nexthop;
}
….
}
grouping route-prefix {
description “common
attributes use for all routes”;
leaf route-index {
type uint64;
mandatory true;
}
leaf route-type {
type route-type-def;
mandatory true;
}
container match {
choice route-type {
… ipv4
… ipv6
… mpls
… mac
}
}
case ipv4 {
description
“match on destination IP
address in header”;
container ipv4 {
leaf ipv4-route-type {
type ip-route-type def;
mandatory true;
}
choice ip-route-type {
case destination-ipv4-address {
leaf destination-ipv4-prefix {
type inet:ipv4-prefix
mandatory true;
}
case destination-source-ipv4-address
…..
}
}
module i2rs-rib { …
container routing-instance {
…
list rib-list {
…
list route-list {
key “route-index”;
leaf route-index {
type uint64;
mandatory true;
}
leaf route-type {
type route-type-def;
mandatory true;
}
leaf destination-ip-v4-prefix {
type inet:ipv4-prefix;
mandatory true;
}
left nexthop-id {
type uint32;
mandatory true;
}
leaf next-hop-ipv4-address {
type inet:ipv4-address
mandatory true
}
} }
grouping nexthop {
leaf nexthop-id {
mandatory true;
type uint32;
}
choice next-hop-type {
case next-hop base {
list nexthop-chain {
key “nexthop-chain-id”;
uses nexthop-chain-member;
}
}
}
IPv4
Route