## Slide 1: IETF YANG routing models VRF centric vs Protocol centric

## Slide 2: Vendor implementations of routing config
Two flavors :
  VRF centric :
    All the configuration of the routing protocol is contained within the associated instance
  Protocol centric :
    All the configuration of the routing-protocol is contained within the « default-routing-instance » including containers for « VRF » specific configurations
Routing-instance VRF1
protocol isis {}
protocol ospf {}
protocol ldp {}
!
protocol isis {
instance VRF1 {}
instance VRF2 {}
}
protocol ospf {
instance VRF1 {}
instance VRF2 {}
}
Routing-instance VRF2
protocol isis {}
protocol ospf {}
protocol ldp {}
!
Typically CISCO config-like
Brocade,HP,Huawei …
Typically Juniper/ALU config-like

## Slide 3: Vendor implementations of routing config : VRF centric example
protocols isis {
level 1 {
authentication-key TOTO;
}
interface ge-0/4/0 level 1 metric 10;
}
Routing-instances VRF1 {
protocols isis {
level 1 disable;
interface xe-0/3/0;
}
}
Routing-instances VRF2 {
protocols isis {
level 2 wide-metrics-only:
level 1 disable;
interface xe-0/2/0;
}
}

## Slide 4: Vendor implementations of routing config : protocol centric example
router ospf 10
router-id 11.11.11.11
vrf VRF1
router-id 11.11.11.11
area 0
interface Gig1/0
!
vrf VRF2
router-id 11.11.11.11
area 1
interface Gig2/0
!
!
!