## Slide 1: Delay Management: a brief history
Fred Baker

## Slide 2: Where did Adaptive Queue Management come from? Early work…
1984, RFC 896, Nagle: “Congestion control in IP/TCP internetworks”
1985, RFC 970, Nagle: “On Packet Switches with Infinite Storage”
1988, SIGCOMM ‘88, Jacobson: “Congestion avoidance and control”
1989, CACM, Demers, Keshav, Shenker: “Analysis and Simulation of a Fair Queuing Algorithm”
1990, SIGCOMM ‘90, Mankin: “Random drop congestion control”
1993, IEEE/ACM Transactions on Networking, Jacobsen and Floyd, “Random early detection gateways for congestion avoidance”
1993, IEEE/ACM Transactions on Networking, Parekh and Gallagher, “A generalized processor sharing approach to flow control in integrated services networks”
2006, A good overview: http://www.pollere.net/Pdfdocs/QrantJul06.pdf

## Slide 3: IETF work on congestion control
Work in the IETF probably started with RFC 1633, which defined a few terms:
  Elastic Applications (and traffic): applications that adapt flow rate to network behavior (which comes down to TCP, its successors, and assigns)
  Real Time Applications (and traffic): Traffic that doesn’t adapt but cannot be filtered out as an attack (nominally voice and video)
The next steps were involved with fixing TCP implementations.
  Vern Paxson tested many implementations, and named and shamed bad ones
  Outcome: TCP implementations were standardized and generally improved
A lot of work has happened since: 177 RFCs that describe TCP options, capabilities, and algorithms
  Notably RFC 5681 “TCP Congestion Control”, which describes the Unix BSD TCP Reno.
  Led primarily by Sally Floyd, Mark Allman, Greg Shepherd, and others

## Slide 4: IETF Quality of Service Architectures
Integrated Services
  Protocol: RSVP
  Premise: ask network to set aside bandwidth for Real Time services
  Not widely deployed, as service providers saw it as a vehicle for infrastructure attacks
Differentiated Services
  Protocol: DSCP (IPv4) or Traffic Class (IPv6) defined to allow traffic classification
  Premise:
    Let originators classify traffic (except that ISPs override that)
    Let networks decide how they wanted to treat different classes of traffic
  Thought hard about configuring queuing systems, queue disciplines, and drop disciplines, and standard service structures (https://tools.ietf.org/html/rfc4594 “Configuration Guidelines for DiffServ Service Classes. Babiarz, Chan, Baker. August 2006.)
  Concept heavily used in MPLS
  IP DSCP used within networks, but not across network boundaries
  But see https://tools.ietf.org/html/rfc8100
    Diffserv-Interconnection Classes and Practice. R. Geib, Ed., D. Black

## Slide 5: Academic and Open Source work
There are a number of projects one could identify, but I’ll mention:
  Adaptive RED (ARED) (implemented in Linux)
  Flow RED (https://pdos.csail.mit.edu/~rtm/papers/fred.pdf)
  Codel (also published in RFC 8290)
  Proportional Integral Controller Enhanced (PIE, also RFC 8033)