Network Working Group                                          G. Mirsky

Internet-Draft                                                J. Halpern

Intended status: Standards Track                                Ericsson

Expires: 5 September 2022                                         X. Min

ZTE Corp.

A. Clemm

J. Strassner

Futurewei

J. Francois

Inria

L. Han

China Mobile

4 March 2022

Precision Availability Metrics for SLO-Governed End-to-End Services

draft-mhmcsfh-ippm-pam-00

Abstract

This document defines a set of metrics for networking services with

performance requirements expressed as Service Level Objectives (SLO).

These metrics, referred to as Precision Availability Metrics (PAM),

can be used to assess the service levels that are being delivered.

PAM can be used to control how a service is provided in order to meet its SLO as

and consequently to assess and identify any service distortion. .

Status of This Memo

This Internet-Draft is submitted in full conformance with the

provisions of BCP 78 and BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF).  Note that other groups may also distribute

working documents as Internet-Drafts.  The list of current Internet-

Drafts is at https://datatracker.ietf.org/drafts/current/.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

This Internet-Draft will expire on 5 September 2022.

Mirsky, et al.          Expires 5 September 2022                [Page 1]

Internet-Draft              PAM for Multi-SLO                 March 2022

Copyright Notice

Copyright (c) 2022 IETF Trust and the persons identified as the

document authors.  All rights reserved.

This document is subject to BCP 78 and the IETF Trust's Legal

Provisions Relating to IETF Documents (https://trustee.ietf.org/

license-info) in effect on the date of publication of this document.

Please review these documents carefully, as they describe your rights

and restrictions with respect to this document.  Code Components

extracted from this document must include Revised BSD License text as

described in Section 4.e of the Trust Legal Provisions and are

provided without warranty as described in the Revised BSD License.

Table of Contents

1.  Introduction  . . . . . . . . . . . . . . . . . . . . . . . .   2

2.  Conventions used in this document . . . . . . . . . . . . . .   4

2.1.  Terminology and Acronyms  . . . . . . . . . . . . . . . .   4

3.  Performance Availability Metrics  . . . . . . . . . . . . . .   4

3.1.  Preliminaries . . . . . . . . . . . . . . . . . . . . . .   5

3.2.  Derived Performance Availability Metrics  . . . . . . . .   6

3.3.  Network Availability in Performance Availability

Metrics . . . . . . . . . . . . . . . . . . . . . . . . .   7

4.  Statistical SLO . . . . . . . . . . . . . . . . . . . . . . .   7

5.  Availability of Anything-as-a-Service . . . . . . . . . . . .   8

6.  Other PAM Benefits  . . . . . . . . . . . . . . . . . . . . .  10

7.  Discussion Items  . . . . . . . . . . . . . . . . . . . . . .  10

8.  IANA Considerations . . . . . . . . . . . . . . . . . . . . .  11

9.  Security Considerations . . . . . . . . . . . . . . . . . . .  11

10. Acknowledgments . . . . . . . . . . . . . . . . . . . . . . .  11

11. References  . . . . . . . . . . . . . . . . . . . . . . . . .  11

11.1.  Informative References . . . . . . . . . . . . . . . . .  12

Authors' Addresses  . . . . . . . . . . . . . . . . . . . . . . .  12

1.  Introduction

Network operators and network users often need to assess the quality

with which network services are being produced and delivered.  In particular in

cases where service level guarantees are given and service level

objectives (SLOs) are defined, it is essential to provide a measure

of the degree with which actual service levels that are delivered

comply with SLOs that were agreed, typically in agreements.  Examples of service levels

include service latency and packet loss.  Simple examples of SLOs

associated with such service levels would be target values for the

maximum end-to-end latency or maximum packet loss ratio that would be

deemed acceptable.

Mirsky, et al.          Expires 5 September 2022                [Page 2]

Internet-Draft              PAM for Multi-SLO                 March 2022

To express the perceived quality of delivered networking services versus their

SLOs, a set of metrics are needed to

characterize the quality of the service being provided.  Of concern

is not so much the absolute service level (for example, actual

latency experienced), but whether the service is provided in

accordance with the contracted, and eventually negotiated, service levels.  For instance, this include whether

the latency that is experienced falls within an acceptable range

that has been contracted for the service.  The specific quality

depends on the SLO that is in effect.    A non-conformance to an SLO might result in

degradation of the quality of experience for gamers up to

jeopardizing the safety of a large area.  However, as those

applications represent significant business opportunities, they

demand dependable technical solutions.

The same service level may be deemed acceptable for one

application, while unacceptable for another, depending on the needs

of the application.  Hence it is not sufficient to simply measure

service levels per se over time, but to assess the quality of the

service being provided with the applicable SLO in mind.  However, there are no metrics in place that can be used to account

for the quality with which services are delivered relative to their

SLOs, and whether their SLOs are being met on at all times.

Such metrics and the instrumentation to support them are essential

for a number of purposes, including monitoring (to ensure that

networking services are performing according to their objectives) as

well as accounting (to maintain a record of service levels delivered,

important for monetization of such services as well as for triaging

of problems).

The current state-of-the-art of metrics available today includes, for

example, interface metrics, useful to obtain data on traffic volume

and behavior that can be observed at an interface [RFC2863] and

[RFC8343], but agnostic of actual end-to-end service levels and not

specific to distinct flows.  Flow records [RFC7011] and [RFC7012]

maintain statistics about flows, including flow volume and flow

duration, but again, contain very little information about end-to-end

service levels, let alone whether the service levels delivered to

meet their targets, i.e., their associated SLOs.

This specification introduces a new set of metrics, Precision

Availability Metrics (PAM), aimed at capturing end-to-end service

levels for a flow, specifically the degree to which flows comply with

the SLOs that are in effect.

The term "availability" reflects that a service which is characterized by its SLOs is considered

Mirsky, et al.          Expires 5 September 2022                [Page 3]

Internet-Draft              PAM for Multi-SLO                 March 2022

unavailable whenever those SLOs are violated, even if basic

connectivity is still working.

"Precision" refers to that

services whose end-to-end service levels are governed by SLOs, and

which must therefore be precisely delivered according to the

associated quality and performance requirements.  It should be noted

that "precision" refers to what is being assessed, not to the

mechanism used to measure it; in other words, it does not refer to

the precision of the mechanism with which actual service levels are

measured.  The specification and implementation of methods that

provide for accurate measurements is a separate topic independent of

the definition of the metrics in which the results of such

measurements would be expressed.

[Ed.note: It should be noted that at this point, the set of metrics

proposed here is intended as a "starter set" that is intended to

spark further discussion.  Other metrics are certainly conceivable;

we expect that the list of metrics will evolve as part of the Working

Group discussions.]

2.  Conventions & Terminology

2.1.  Terminology and Acronyms

[Ed.Note: needs updating.]

PAM Precision Availability Metric

OAM Operations, Administration, and Maintenance

EI Errored Interval

EIR Errored Interval Ratio

SEI Severely Errored Interval

SEIR Severely Errored Interval Ratio

EFI Error-Free Interval

3.  Performance Availability Metrics

Mirsky, et al.          Expires 5 September 2022                [Page 4]

Internet-Draft              PAM for Multi-SLO                 March 2022

3.1.  Introducing Error Intervals

When analyzing the availability metrics of a service flow between two

nodes, we need to select a time interval as the unit of PAM.  In

[ITU.G.826], a time interval of one second is used.  That is

reasonable, but some services may require different granularity.  For

that reason, the time interval in PAM is viewed as a variable

parameter though constant for a particular measurement session.

Further, for the purpose of PAM, each time interval, e.g., second or

decamillisecond, is classified either as Errored Interval (EI),

Severely Errored Interval (SEI), or Error-Free Interval (EFI).  These

are defined as follows:

*  EI is a time interval during which at least one of the

performance parameters degraded below its pre-defined optimal

level threshold or a defect was detected.

*  SEI is a time interval during which at least one of the

performance parameters degraded below its pre-defined critical

threshold or a defect was detected.

*  Consequently, EFI is a time interval during which all

performance objectives are at or above their respective pre-

defined optimal levels and no defect has been detected. In such interval, there is no negative deviation of the experienced service vs. the expected service.

In this document, the defect is

interpreted as the state of inability to communicate between a

particular set of nodes.  It is important to note that it is being

defined as a state, and thus, it has conditions that define entry

into it and exit out of it.  Also, the state of defect exists only in

connection to the particular group of nodes in the network, not the

network as a domain.

From these defections, a set of basic metrics can be defined that

count the numbers of time intervals that fall into each category:

*  EI count.

*  SEI count.

*  EFI count.

Mirsky, et al.          Expires 5 September 2022                [Page 5]

Internet-Draft              PAM for Multi-SLO                 March 2022

3.2.  Derived Performance Availability Metrics

A set of metrics can be created based on PAM introduced in Section 3.

In this document, these metrics are referred to as derived PAM.  Some

of these metrics are modeled after Mean Time Between Failure (MTBF)

metrics - a "failure" in this context referring to a failure to

deliver a packet according to its SLO.

*  Time since the last errored interval (e.g., since last errored ms,

since last errored second).  (This parameter is suitable for the

monitoring of the current health.)  [Ed. note: Need a definition

of "current health".  Is there an alternative to "current"?  Past

health?]

*  Packets since the last errored packet.  (This parameter is

suitable for the monitoring of the current health.)

*  Mean time between EIs (e.g., between errored milliseconds, errored

seconds) is the arithmetic mean of time between consecutive EIs.

*  Mean packets between EIs is the arithmetic mean of the number of

SLO-compliant packets between consecutive EIs.  (Another variation

of "MTBF" in a service setting.)

An analogous set of metrics can be produced for SEI:

*  Time since the last SEI (e.g., since last errored ms, since last

errored second).  (This parameter is suitable for the monitoring

of the current health.)

*  Mean time between SEIs (e.g., between severely errored

milliseconds, severely errored seconds) is the arithmetic mean of

time between consecutive SEIs.

*  Mean packets between SEIs is the arithmetic mean of the number of

SLO-compliant packets between consecutive SEIs.  (Another

variation of "MTBF" in a service setting.)

Determining the period in which the path is currently PAM-wise is

helpful.  But because switching between periods requires ten

consecutive intervals, shorter conditions may not be adequately

reflected.  Two additional PAMs can be used, and they are defined as

follows:

*  errored interval ratio (EIR) is the ratio of EI to the total

number of time unit intervals in a time of the availability

periods during a fixed measurement interval.

Mirsky, et al.          Expires 5 September 2022                [Page 6]

Internet-Draft              PAM for Multi-SLO                 March 2022

*  severely errored interval ratio (SESR) - is the ratio of SEIs to

the total number of time unit intervals in a time of the

availability periods during a fixed measurement interval.

3.3.  Network Availability in Performance Availability Metrics

EI, SEI, and EFI characterize the

communication between two nodes relative to the level of required and

acceptable performance and when the performance level degrades below an

acceptable level.  The former condition in this document referred to

as network availability.  The latter - network unavailability.  Based

on the definitions, SEI is the one time interval of network

unavailability while EI and EFI present an interval of network

availability.  But since the conditions of the network are

everchanging periods of network availability and unavailability need

to be defined with duration larger than one time interval to reduce

the number of state changes while correctly reflecting the network

condition.  The method to determine the state of the network in terms

of PAM is described below:

*  If ten consecutive SEIs been detected, then the PAM state of the

network is determined as unavailability, and the beginning of that

period of unavailability state is at the start of the first SEI in

the sequence of the consecutive SEIs.

*  Similarly, ten consecutive non-SEIs, i.e., either EIs or EFIs,

indicate that the network is in the availability period, i.e.,

available.  The start of that period is at the beginning of the

first non-SEI.

*  Resulting from these two definitions, a sequence of less than ten

consecutive SEIs or non-SEIs does not change the PAM state of the

network.  For example, if the PAM state is determined as

unavailability, a sequence of seven EFIs is not viewed as an

availability period.

4.  Statistical SLO

It should be noted that certain Service Level Agreements (SLAs) may be

statistical, requiring the service levels of packets in a flow to

adhere to specific distributions.  For example, an SLA might state

that any given SLO applies only to a certain percentage of packets,

allowing for a certain level of, for example, packet loss and/or

exceeding packet delay threshold take place.  Each such event, in

that case, does not necessarily constitute an SLO violation.

However, it is still useful to maintain those statistics, as the

number of out-of-SLO packets still matters when looked at in

proportion to the total number of packets.

Mirsky, et al.          Expires 5 September 2022                [Page 7]

Internet-Draft              PAM for Multi-SLO                 March 2022

Along that vein, an SLA might establish an SLO of, say, end-to-end

latency to not exceed 20 ms for 99% of packets, to not exceed 25ms for

99.999% of packets, and to never exceed 30ms for anything beyond.  In

that case, any individual packet missing the 20 ms latency target

cannot be considered an SLO violation in itself, but compliance with

the SLO may need to be assessed after the fact.

To support statistical SLAs more directly, it is feasible to support

additional metrics, such as metrics that represent histograms for

service level parameters with buckets corresponding to individual

service level objectives.  For the example just given, a histogram

for a given flow could be maintained with three buckets: one

containing the count of packets within 20ms, a second with a count of

packets between 20 and 25ms (or simply all within 25ms), a third with

a count of packets between 25 and 30ms (or merely all packets within

30ms, and a fourth with a count of anything beyond (or simply a total

count).  Of course, the number of buckets and the boundaries between

those buckets should correspond to the needs of the application

respectively SLA, i.e., to the specific guarantees and SLOs that were

provided.  The definition of histogram metrics is for further study.

5.  Availability of Anything-as-a-Service

Anything as a service (XaaS) describes a general category of services

related to cloud computing and remote access.  These services include

the vast number of products, tools, and technologies that are

delivered to users as a service over the Internet.  In this document,

the availability of XaaS is viewed as the ability to access the

service over a period of time with pre-defined performance

objectives.  Among the advantages of the XaaS model are:

*  Improving the expense model by purchasing services from providers

on a subscription basis rather than buying individual products,

e.g., software, hardware, servers, security, infrastructure, and

install them on-site, and then link everything together to create

networks.

*  Speeding new apps and business processes by quickly adapting to

changing market conditions with new applications or solutions.

*  Shifting IT resources to specialized higher-value projects that

use the core expertise of the company.

But XaaS model also has potential challenges:

*  Possible downtime resulting from issues of internet reliability,

resilience, provisioning, and managing the infrastructure

resources.

Mirsky, et al.          Expires 5 September 2022                [Page 8]

Internet-Draft              PAM for Multi-SLO                 March 2022

*  Performance issues caused by depleted resources like bandwidth,

computing power, inefficiencies of virtualized environments,

ongoing management and security of multi-cloud services.

*  Complexity impacts enterprise IT team that must remain in the

process of the continued learning of the provided services.

The framework and metrics of the PAM defined in Section 3 allow a

provider of XaaS and their customers to quantify, measure, monitor

for conformance what is often referred to as an ephemeral -

availability of the service to be delivered.  There are other

definitions and methods of expressing availability.  For example,

[HighAvailability-WP] uses the following equation:

Availability Average = MTBF/(MTBF + MTRR),

where:

MTBF (Mean Time Between Failures) - mean time between

individual component failures.  For example, a hard drive

malfunction or hypervisor reboot.

MTTR (Mean Time To Repair) - refers to how long it takes to fix

the broken component or the application to come back online,

While this approach estimates the expected availability of a XaaS,

the PAM reflects near-real-time availability of a service as

experienced by a user.  It also provides valuable data for more

accurate and realistic MTBF and MTTR in the particular environment,

and simplifies comparison of different solutions that may use

redundant servers (web and database), load balancers.

In another field of communication, mobile voice and data services,

the definition of service availability is understood as "the

probability of successful service reception: a given area is declared

"in-coverage" if the service in that area is available with a pre-

specified minimum rate of success.  Service availability has the

advantage of being more easily understandable for consumers and is

expressed as a percentage of the number of attempts to access a given

service."  [BEREC-CP].  The definition of the availability used in

the PAM throughout this document is close to the quoted above.  It

might be considered as the extension that allows regulators,

operators, and consumers to compare not only the rate of successfully

establishing a connection but the quality of the connection during

its lifetime.

Mirsky, et al.          Expires 5 September 2022                [Page 9]

Internet-Draft              PAM for Multi-SLO                 March 2022

6.  Other PAM Benefits

PAM provides a number of benefits with other, more

conventional performance metrics.  Without PAM, it would be possible

to conduct ongoing measurements of service levels and maintain a

time-series of service level records, then assess compliance with

specific SLOs after the fact.  However, doing so would require the

collection of vast amounts of data that would need to be generated,

exported, transmitted, collected, and stored.  In addition, extensive

postprocessing would be required to compare that data against SLOs

and analyze its compliance.  Being able to perform these tasks at

scale and in real-time would present significant additional

challenges.

Adding PAM allows for a more compact expression of service level

compliance.  In that sense, PAM does not simply represent raw data

but expresses actionable information.  In conjunction with proper

instrumentation, PAM can thus help avoid expensive postprocessing.

7.  Discussion Items

The following items require further discussion:

*  Terminology - "Errored" vs. "Violated".  The key metrics defined

in this draft refer to intervals during which violations of

objectives for service level parameters occur as "errored".  The

term "errored" was chosen in continuity with the concept of

"errored seconds", often used in transmission systems.  However,

"violated" may be a more accurate term, as the metrics defined

here are not "errors" in an absolute sense, but relative to a set

of defined objectives.

*  Metrics.  The foundational metrics defined in this draft refer to

errored/violated intervals.  In addition, counts of errors/

violations related to individual packets may also need to be

maintained.  Metrics referring to violated/errored packets, i.e.

packets that on an individual basis miss a performance objective

may be added in a later revision of this document.

The following is a list of items for which further discussion is

needed as to whether they should be included in the scope of this

specification:

*  A YANG data model.

*  A set of IPFIX Information Elements.

*  Statistical metrics: e.g., histograms/buckets.

Mirsky, et al.          Expires 5 September 2022               [Page 10]

Internet-Draft              PAM for Multi-SLO                 March 2022

*  Policies regarding the definition of "errored" and "severely

errored" time interval.

*  Additional second-order metrics, such as "longest disruption of

service time" (measuring consecutive time units with SEIs).

8.  IANA Considerations

TBA

9.  Security Considerations

Instrumentation for metrics that are used to assess compliance with

SLOs constitute an attractive target for an attacker.  By interfering

with the maintaining of such metrics, services could be falsely

identified as complying (when they are not) or vice-versa flagged as

being non-compliant (when indeed they are).  While this document does

not specify how networks should be instrumented to maintain the

identified metrics.  Such instrumentation needs to be adequately

secured to ensure accurate measurements and prohibit tampering with

metrics being kept.

Where metrics are being defined relative to an SLO, the configuration

of those SLOs needs to be adequately secured.  Likewise, where SLOs

can be adjusted, the correlation between any metrics instance and a

particular SLO must be clear.  The same service levels that

constitute SLO violations for one flow that should be maintained as

part of the "errored time units" and related metrics, may be

perfectly compliant for another flow.  In cases when it is impossible

to tie together SLOs and PAM properly, it will be preferable to

merely maintain statistics about service levels delivered (for

example, overall histograms of end-to-end latency) without assessing

which constitutes violations.

By the same token, where the definition of what constitutes a

"severe" or a "significant" error depends on policy or context.  The

configuration of such policy or context needs to be specially

secured.  Also, the configuration of this policy must be bound to the

metrics being maintained.  This way, it will be clear which policy

was in effect when those metrics were being assessed.  An attacker

that can tamper with such policies will render the corresponding

metrics useless (in the best case) or misleading (in the worst case).

10.  Acknowledgments

TBA

11.  References

Mirsky, et al.          Expires 5 September 2022               [Page 11]

Internet-Draft              PAM for Multi-SLO                 March 2022

11.1.  Informative References

[BEREC-CP] Body of European Regulators for Electronic Communications,

"BEREC Common Position on information to consumers on

mobile coverage", Common Approaches/Positions BoR (18)

237, June 2018, <https://berec.europa.eu/eng/document_regi

ster/subject_matter/berec/regulatory_best_practices/

common_approaches_positions/8315-berec-common-position-on-

information-to-consumers-on-mobile-coverage>.

[HighAvailability-WP]

Avi Freedman, Server Central, "High Availability in Cloud

and Dedicated Infrastructure", <https://www.deft.com/wp-

content/uploads/pdf/SCTG-High-Availability-White-Paper-

Part-2.pdf>.

[ITU.G.826]

ITU-T, "End-to-end error performance parameters and

objectives for international, constant bit-rate digital

paths and connections", ITU-T G.826, December 2002.

[RFC2863]  McCloghrie, K. and F. Kastenholz, "The Interfaces Group

MIB", RFC 2863, DOI 10.17487/RFC2863, June 2000,

<https://www.rfc-editor.org/info/rfc2863>.

[RFC7011]  Claise, B., Ed., Trammell, B., Ed., and P. Aitken,

"Specification of the IP Flow Information Export (IPFIX)

Protocol for the Exchange of Flow Information", STD 77,

RFC 7011, DOI 10.17487/RFC7011, September 2013,

<https://www.rfc-editor.org/info/rfc7011>.

[RFC7012]  Claise, B., Ed. and B. Trammell, Ed., "Information Model

for IP Flow Information Export (IPFIX)", RFC 7012,

DOI 10.17487/RFC7012, September 2013,

<https://www.rfc-editor.org/info/rfc7012>.

[RFC8343]  Bjorklund, M., "A YANG Data Model for Interface

Management", RFC 8343, DOI 10.17487/RFC8343, March 2018,

<https://www.rfc-editor.org/info/rfc8343>.

Authors' Addresses

Greg Mirsky

Ericsson

Email: gregimirsky@gmail.com

Mirsky, et al.          Expires 5 September 2022               [Page 12]

Internet-Draft              PAM for Multi-SLO                 March 2022

Joel Halpern

Ericsson

Email: joel.halpern@ericsson.com

Xiao Min

ZTE Corp.

Email: xiao.min2@zte.com.cn

Alexander Clemm

Futurewei

2330 Central Expressway

Santa Clara,  CA 95050

United States of America

Email: ludwig@clemm.org

John Strassner

Futurewei

2330 Central Expressway

Santa Clara,  CA 95050

United States of America

Email: strazpdj@gmail.com

Jerome Francois

Inria

615 Rue du Jardin Botanique

54600 Villers-les-Nancy

France

Email: jerome.francois@inria.fr

Liuyan Han

China Mobile

32 XuanWuMenXi Street

Beijing

100053

China

Email: hanliuyan@chinamobile.com

Mirsky, et al.          Expires 5 September 2022               [Page 13]

# Comments

There are several views of a service. Here is a figure I’m used to include to cover these matters.

Means to assess that what is delivered is not deviating from what is delivered are important, but the same means may also be used internally to check the deviation from what is engineered vs target service, etc.

To be defined.

This is too vague, unless the ends are called out.

I would use « One-way or two-way » here.

To insist on the need to customize service targets.

of what?

It seems that you assume an SLO is necessarily related to traffic performance. If so, please call that out explicitly in the text.

Not sure to follow the reasoning here.

This is subjective. I would just remove such mentions.

standard?

You may add a reference to rfc7297#section-3.4.

For the loss parameter, this would be the other way around.

How is this set ?

How is this set ?

You may need to discuss why a count metric is useful here.

I see that this can be sued to assess the instability of the service if *EI periods are observed.

Not sure this one is needed.

I would aslo mention percentiles here.

After reading this section, I’m not sure what is the purpose of this section.

That is ?

I’m not sure this document should argue in favor or against the model.

This is subjective/speculative in nature. I suggest to focus on technical matters.

This is more about marketing :-)

Is this specific to these services?

Idem as above