Network Working Group                                           F. Maino

Internet-Draft                                                V. Ermagan

Intended status: Standards Track                           Cisco Systems

Expires: June 2, 2019                                        A. Cabellos

Universitat Politecnica de Catalunya

D. Saucez

INRIA

November 29, 2018

LISP-Security (LISP-SEC)

draft-ietf-lisp-sec-17

Abstract

This memo specifies LISP-SEC, a set of security mechanisms that

provides origin authentication, integrity and anti-replay protection

to LISP's EID-to-RLOC mapping data conveyed via mapping lookup

process.  LISP-SEC also enables verification of authorization on EID-

prefix claims in Map-Reply messages.

Requirements Language

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT",

"SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this

document are to be interpreted as described in BCP14 [RFC2119][RFC8174] when, and only when, they appear in all capitals, as shown here.

Status of This Memo

This Internet-Draft is submitted in full conformance with the

provisions of BCP 78 and BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF).  Note that other groups may also distribute

working documents as Internet-Drafts.  The list of current Internet-

Drafts is at http://datatracker.ietf.org/drafts/current/.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

This Internet-Draft will expire on June 2, 2019.

Maino, et al.             Expires June 2, 2019                  [Page 1]

Internet-Draft                  LISP-SEC                   November 2018

Copyright Notice

Copyright (c) 2018 IETF Trust and the persons identified as the

document authors.  All rights reserved.

This document is subject to BCP 78 and the IETF Trust's Legal

Provisions Relating to IETF Documents

(http://trustee.ietf.org/license-info) in effect on the date of

publication of this document.  Please review these documents

carefully, as they describe your rights and restrictions with respect

to this document.  Code Components extracted from this document must

include Simplified BSD License text as described in Section 4.e of

the Trust Legal Provisions and are provided without warranty as

described in the Simplified BSD License.

Table of Contents

1.  Introduction  . . . . . . . . . . . . . . . . . . . . . . . .   3

2.  Definition of Terms . . . . . . . . . . . . . . . . . . . . .   3

3.  LISP-SEC Threat Model . . . . . . . . . . . . . . . . . . . .   4

4.  Protocol Operations . . . . . . . . . . . . . . . . . . . . .   5

5.  LISP-SEC Control Messages Details . . . . . . . . . . . . . .   7

5.1.  Encapsulated Control Message LISP-SEC Extensions  . . . .   7

5.2.  Map-Reply LISP-SEC Extensions . . . . . . . . . . . . . .   9

5.3.  Map-Register LISP-SEC Extentions  . . . . . . . . . . . .  11

5.4.  ITR Processing  . . . . . . . . . . . . . . . . . . . . .  11

5.4.1.  Map-Reply Record Validation . . . . . . . . . . . . .  13

5.4.2.  PITR Processing . . . . . . . . . . . . . . . . . . .  14

5.5.  Encrypting and Decrypting an OTK  . . . . . . . . . . . .  14

5.6.  Map-Resolver Processing . . . . . . . . . . . . . . . . .  15

5.7.  Map-Server Processing . . . . . . . . . . . . . . . . . .  15

5.7.1.  Map-Server Processing in Proxy mode . . . . . . . . .  16

5.8.  ETR Processing  . . . . . . . . . . . . . . . . . . . . .  16

6.  Security Considerations . . . . . . . . . . . . . . . . . . .  17

6.1.  Mapping System Security . . . . . . . . . . . . . . . . .  17

6.2.  Random Number Generation  . . . . . . . . . . . . . . . .  17

6.3.  Map-Server and ETR Colocation . . . . . . . . . . . . . .  17

6.4.  Deploying LISP-SEC  . . . . . . . . . . . . . . . . . . .  18

6.5.  Shared Keys Provisioning  . . . . . . . . . . . . . . . .  18

6.6.  Replay Attacks  . . . . . . . . . . . . . . . . . . . . .  18

6.7.  Message Privacy . . . . . . . . . . . . . . . . . . . . .  19

6.8.  Denial of Service and Distributed Denial of Service

Attacks . . . . . . . . . . . . . . . . . . . . . . . . .  19

7.  IANA Considerations . . . . . . . . . . . . . . . . . . . . .  19

7.1.  ECM AD Type Registry  . . . . . . . . . . . . . . . . . .  19

7.2.  Map-Reply AD Type Registry  . . . . . . . . . . . . . . .  19

7.3.  HMAC Functions  . . . . . . . . . . . . . . . . . . . . .  20

7.4.  Key Wrap Functions  . . . . . . . . . . . . . . . . . . .  20

Maino, et al.             Expires June 2, 2019                  [Page 2]

Internet-Draft                  LISP-SEC                   November 2018

7.5.  Key Derivation Functions  . . . . . . . . . . . . . . . .  21

8.  Acknowledgements  . . . . . . . . . . . . . . . . . . . . . .  21

9.  Normative References  . . . . . . . . . . . . . . . . . . . .  21

Authors' Addresses  . . . . . . . . . . . . . . . . . . . . . . .  23

1.  Introduction

The Locator/ID Separation Protocol

[I-D.ietf-lisp-rfc6830bis] [I-D.ietf-lisp-rfc6833bis] is a network-

layer-based protocol that enables separation of IP addresses into two

new numbering spaces: Endpoint Identifiers (EIDs) and Routing

Locators (RLOCs).  EID-to-RLOC mappings are stored in a database, the

LISP Mapping System, and made available via the Map-Request/Map-Reply

lookup process.  If these EID-to-RLOC mappings, carried through Map-

Reply messages, are transmitted without integrity protection, an

adversary can manipulate them and hijack the communication,

impersonate the requested EID, or mount Denial of Service or

Distributed Denial of Service attacks.  Also, if the Map-Reply

message is transported unauthenticated, an adversarial LISP entity

can overclaim an EID-prefix and maliciously redirect traffic directed

to a large number of hosts.  The LISP-SEC threat model, described in

Section 3, is built on top of the LISP threat model defined in

[RFC7835], that includes a detailed description of "overclaiming"

attack.

This memo specifies LISP-SEC, a set of security mechanisms that

provides origin authentication, integrity and anti-replay protection

to LISP's EID-to-RLOC mapping data conveyed via mapping lookup

process.  LISP-SEC also enables verification of authorization on EID-

prefix claims in Map-Reply messages, ensuring that the sender of a

Map-Reply that provides the location for a given EID-prefix is

entitled to do so according to the EID prefix registered in the

associated Map-Server.  Map-Register security, including the right

for a LISP entity to register an EID-prefix or to claim presence at

an RLOC, is out of the scope of LISP-SEC.  Additional security

considerations are described in Section 6.

2.  Definition of Terms

One-Time Key (OTK): An ephemeral randomly generated key that must

be used for a single Map-Request/Map-Reply exchange.

ITR One-Time Key (ITR-OTK): The One-Time Key generated at the Ingress Tunnel Router (ITR).

MS One-Time Key (MS-OTK): The One-Time Key generated at the Map-

Server.

Maino, et al.             Expires June 2, 2019                  [Page 3]

Internet-Draft                  LISP-SEC                   November 2018

Authentication Data (AD): Metadata that is included either in a

LISP Encapsulated Control Message (ECM) header, as defined in

Section 6.1.8 of [I-D.ietf-lisp-rfc6833bis], or in a Map-Reply

message to support confidentiality, integrity protection, and

verification of EID-prefix authorization.

OTK Authentication Data (OTK-AD): The portion of ECM

Authentication Data that contains a One-Time Key.

EID Authentication Data (EID-AD): The portion of ECM and Map-Reply

Authentication Data used for verification of EID-prefix

authorization.

Packet Authentication Data (PKT-AD): The portion of Map-Reply

Authentication Data used to protect the integrity of the Map-Reply

message.

For definitions of other terms, notably Map-Request, Map-Reply,

Ingress Tunnel Router (ITR), Egress Tunnel Router (ETR), Map-Server

(MS), and Map-Resolver (MR) please consult the LISP specification

[I-D.ietf-lisp-rfc6833bis].

3.  LISP-SEC Threat Model

LISP-SEC addresses the control plane threats, described in sections

3.7 and 3.8 of [RFC7835], that target EID-to-RLOC mappings, including

manipulations of Map-Request and Map-Reply messages, and malicious

ETR EID prefix overclaiming.

LISP-SEC makes two main assumptions:

(1) the LISP mapping system is expected to deliver a Map-Request

message to their intended destination ETR as identified by the EID,

and (2) no man-in-the-middle (MITM) attack can be mounted within the

LISP Mapping System.  How the Mapping System is protected from MITM

attacks depends from the particular Mapping Systems used, and is out

of the scope of this memo.  Furthermore, while LISP-SEC enables

detection of EID prefix overclaiming attacks, it assumes that Map-

Servers can verify the EID prefix authorization at time of

registration.

According to the threat model described in [RFC7835] LISP-SEC assumes

that any kind of attack, including MITM attacks, can be mounted in

the access network, outside of the boundaries of the LISP mapping

system.  An on-path attacker, outside of the LISP mapping system can,

for example, hijack Map-Request and Map-Reply messages, spoofing the

identity of a LISP node.  Another example of on-path attack, called

overclaiming attack, can be mounted by a malicious Egress Tunnel

Router (ETR), by overclaiming the EID-prefixes for which it is

Maino, et al.             Expires June 2, 2019                  [Page 4]

Internet-Draft                  LISP-SEC                   November 2018

authoritative.  In this way the ETR can maliciously redirect traffic

directed to a large number of hosts.

4.  Protocol Operations

The goal of the security mechanisms defined in

[I-D.ietf-lisp-rfc6833bis] is to prevent unauthorized insertion of

mapping data by providing origin authentication and integrity

protection for the Map-Register, and by using the nonce to detect

unsolicited Map-Reply sent by off-path attackers.

LISP-SEC builds on top of the security mechanisms defined in

[I-D.ietf-lisp-rfc6833bis] to address the threats described in

Section 3 by leveraging the trust relationships existing among the

LISP entities participating to the exchange of the Map-Request/Map-

Reply messages.  Those trust relationships are used to securely

distribute a One-Time Key (OTK) that provides origin authentication,

integrity and anti-replay protection to mapping data conveyed via the

mapping lookup process, and that effectively prevent overclaiming

attacks.  The processing of security parameters during the Map-

Request/Map-Reply exchange is as follows:

o  The ITR-OTK is generated and stored at the ITR, and securely

transported to the Map-Server.

o  The Map-Server uses the ITR-OTK to compute a Keyed-Hashing for

Message Authentication (HMAC) [RFC2104] that protects the

integrity of the mapping data known to the Map-Server to prevent

overclaiming attacks.  The Map-Server also derives a new OTK, the

MS-OTK, that is passed to the ETR, by applying a Key Derivation

Function (KDF) (e.g., [RFC5869]) to the ITR-OTK.

o  The ETR uses the MS-OTK to compute an HMAC that protects the

integrity of the Map-Reply sent to the ITR.

o  Finally, the ITR uses the stored ITR-OTK to verify the integrity

of the mapping data provided by both the Map-Server and the ETR,

and to verify that no overclaiming attacks were mounted along the

path between the Map-Server and the ITR.

Section 5 provides the detailed description of the LISP-SEC control

messages and their processing, while the rest of this section

describes the flow of LISP protocol operations at each entity involved in

the Map-Request/Map-Reply exchange:

o  The ITR, upon needing to transmit a Map-Request message, generates

and stores an OTK (ITR-OTK).  This ITR-OTK is included into the

Encapsulated Control Message (ECM) that contains the Map-Request

Maino, et al.             Expires June 2, 2019                  [Page 5]

Internet-Draft                  LISP-SEC                   November 2018

sent to the Map-Resolver.  To provide confidentiality to the ITR-

OTK over the path between the ITR and its Map-Resolver, the ITR-

OTK SHOULD be encrypted using a preconfigured key shared between

the ITR and the Map-Resolver, similar to the key shared between

the ETR and the Map-Server in order to secure ETR registration

[I-D.ietf-lisp-rfc6833bis].

o  The Map-Resolver decapsulates the ECM message, decrypts the ITR-

OTK, if needed, and forwards through the Mapping System the

received Map-Request and the ITR-OTK, as part of a new ECM

message.  As described in Section 5.6, the LISP Mapping System

delivers the ECM to the appropriate Map-Server, as identified by

the EID destination address of the Map-Request.

o  The Map-Server is configured with the location mappings and policy

information for the ETR responsible for the EID destination

address.  Using this preconfigured information, the Map-Server,

after the decapsulation of the ECM message, finds the longest

match EID-prefix that covers the requested EID in the received

Map-Request.  The Map-Server adds this EID-prefix, together with

an HMAC computed using the ITR-OTK, to a new Encapsulated Control

Message that contains the received Map-Request.

o  If the Map-Server is acting in proxy mode, as specified in

[I-D.ietf-lisp-rfc6833bis], the ETR is not involved in the

generation of the Map-Reply.  In this case the Map-Server

generates the Map-Reply on behalf of the ETR as described below.

o  The Map-Server derives a new OTK, the MS-OTK, by applying a Key

Derivation Function (KDF) to the ITR-OTK.  This MS-OTK is included

in the Encapsulated Control Message that the Map-Server uses to

forward the Map-Request to the ETR.  To provide MS-OTK

confidentiality over the path between the Map-Server and the ETR,

the MS-OTK SHOULD be encrypted using the key shared between the

ETR and the Map-Server in order to secure ETR registration

[I-D.ietf-lisp-rfc6833bis].

o  The ETR, upon receiving the ECM encapsulated Map-Request from the

Map-Server, decrypts the MS-OTK, if needed, and originates a

Map-Reply that contains the EID-to-RLOC mapping

information as specified in [I-D.ietf-lisp-rfc6833bis].

o  The ETR computes an HMAC over this Map-Reply, keyed with

MS-OTK to protect the integrity of the whole Map-Reply.  The ETR

also copies the EID-prefix authorization data that the Map-Server

included in the ECM encapsulated Map-Request into the Map-Reply

message.  The ETR then sends this complete Map-Reply message to

the requesting ITR.

Maino, et al.             Expires June 2, 2019                  [Page 6]

Internet-Draft                  LISP-SEC                   November 2018

o  The ITR, upon receiving the Map-Reply, uses the locally stored

ITR-OTK to verify the integrity of the EID-prefix authorization

data included in the Map-Reply by the Map-Server.  The ITR

computes the MS-OTK by applying the same KDF used by the Map-

Server, and verifies the integrity of the Map-Reply.  If the

integrity checks fail, the Map-Reply MUST be discarded.  Also, if

the EID-prefixes claimed by the ETR in the Map-Reply are not equal

or more specific than the EID-prefix authorization data inserted

by the Map-Server, the ITR MUST discard the Map-Reply.

5.  LISP-SEC Control Messages Details

LISP-SEC metadata associated with a Map-Request is transported within

the Encapsulated Control Message that contains the Map-Request.

LISP-SEC metadata associated with the Map-Reply is transported within

the Map-Reply itself.

5.1.  Encapsulated Control Message LISP-SEC Extensions

LISP-SEC uses the ECM defined in

[I-D.ietf-lisp-rfc6833bis] with S-bit set to 1 to

indicate that the LISP header includes Authentication Data (AD).  The

format of the LISP-SEC ECM Authentication Data is defined in Figure x.  OTK-AD stands for One-Time Key Authentication Data

and EID-AD stands for EID Authentication Data.

Maino, et al.             Expires June 2, 2019                  [Page 7]

Internet-Draft                  LISP-SEC                   November 2018

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  ECM AD Type  |V|  Unassigned   |        Requested HMAC ID      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+\

|              OTK Length       |       OTK Encryption ID       | |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |

|                       One-Time-Key Preamble ...               | |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+OTK-AD

|                   ... One-Time-Key Preamble                   | |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |

~                      One-Time Key (128 bits)                  ~/

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ <---+

|           EID-AD Length       |           KDF ID              |     |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+     |

| Record Count  |    Reserved   |         EID HMAC ID           |EID-AD

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+\    |

|   Unassigned    | EID mask-len  |           EID-AFI             | |   |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ Rec |

~                          EID-prefix ...                       ~ |   |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+/    |

~                            EID HMAC                           ~     |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ <---+

Figure X: LISP-SEC ECM Authentication Data

ECM AD Type: 1 (LISP-SEC Authentication Data).  See Section 7.

V: Key Version bit.  This bit is toggled when the sender switches

to a new OTK wrapping key

Unassigned: Set to 0 on transmission and ignored on receipt.

Requested HMAC ID: The HMAC algorithm requested by the ITR.  See

Section 5.4 for details.

OTK Length: The length (in bytes) of the OTK Authentication Data

(OTK-AD), that contains the OTK Preamble and the OTK.

OTK Encryption ID: The identifier of the key wrapping algorithm

used to encrypt the One-Time-Key. When a 128-bit OTK is sent

unencrypted by the Map-Resolver, the OTK Encryption ID is set to

NULL_KEY_WRAP_128.  See Section 5.5 for more details.

One-Time-Key Preamble: set to 0 if the OTK is not encrypted.  When

the OTK is encrypted, this field carries additional metadata

resulting from the key wrapping operation.  When a 128-bit OTK is

Maino, et al.             Expires June 2, 2019                  [Page 8]

Internet-Draft                  LISP-SEC                   November 2018

sent unencrypted by Map-Resolver, the OTK Preamble is set to

0x0000000000000000 (64 bits).  See Section 5.5 for details.

One-Time-Key: the OTK encrypted (or not) as specified by OTK

Encryption ID.  See Section 5.5 for details.

EID-AD Length: length (in bytes) of the EID Authentication Data

(EID-AD).  The ITR MUST set EID-AD Length to 4 bytes, as it only

fills the KDF ID field, and all the remaining fields part of the

EID-AD are not present.  An EID-AD MAY contain multiple EID-

records.  Each EID-record is 4-byte long plus the length of the

AFI-encoded EID-prefix.

KDF ID: Identifier of the Key Derivation Function used to derive

the MS-OTK.  The ITR MAY use this field to indicate the

recommended KDF algorithm, according to local policy.  The Map-

Server can overwrite the KDF ID if it does not support the KDF ID

recommended by the ITR.  See Section 5.4 for more details.

Record Count: The number of records in this Map-Request message.

A record is comprised of the portion of the packet that is labeled

'Rec' above and occurs the number of times equal to Record Count.

Unassigned: Set to 0 on transmission and ignored on receipt.

EID HMAC ID: Identifier of the HMAC algorithm used to protect the

integrity of the EID-AD.  This field is filled by Map-Server that

computed the EID-prefix HMAC.  See Section 5.4 for more details.

EID mask-len: Mask length for EID-prefix.

EID-AFI: Address family of EID-prefix according to [RFC5226]

EID-prefix: The Map-Server uses this field to specify the EID-

prefix that the destination ETR is authoritative for, and is the

longest match for the requested EID.

EID HMAC: HMAC of the EID-AD computed and inserted by Map-Server.

Before computing the HMAC operation the EID HMAC field MUST be set

to 0.  The HMAC MUST cover the entire EID-AD.

5.2.  Map-Reply LISP-SEC Extensions

LISP-SEC uses the Map-Reply defined in [I-D.ietf-lisp-rfc6833bis],

with S-bit set to 1 to indicate that the Map-Reply

message includes Authentication Data (AD).  The format of the LISP-

SEC Map-Reply Authentication Data is defined in Figure ...

Maino, et al.             Expires June 2, 2019                  [Page 9]

Internet-Draft                  LISP-SEC                   November 2018

PKT-AD is the Packet Authentication Data that covers the Map-Reply

payload.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  MR AD Type   |                 Unassigned                      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ <---+

|           EID-AD Length       |           KDF ID              |     |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+     |

| Record Count  |    Reserved   |         EID HMAC ID           |EID-AD

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+\    |

|   Unassigned    | EID mask-len  |           EID-AFI             | |   |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ Rec |

~                          EID-prefix ...                       ~ |   |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+/    |

~                            EID HMAC                           ~     |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ <---+

|         PKT-AD Length         |         PKT HMAC ID           |\

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |

~                            PKT HMAC                           ~PKT-AD

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+/

Figure y: LISP-SEC Map-Reply Authentication Data

MR AD Type: 1 (LISP-SEC Authentication Data).  See Section 7.

EID-AD Length: length (in bytes) of the EID-AD.  An EID-AD MAY

contain multiple EID-records.  Each EID-record is 4-byte long plus

the length of the AFI-encoded EID-prefix.

KDF ID: Identifier of the Key Derivation Function used to derive

MS-OTK.  See Section 5.7 for more details.

Record Count: The number of records in this Map-Reply message.  A

record is comprised of the portion of the packet that is labeled

'Rec' above and occurs the number of times equal to Record Count.

Unassigned: Set to 0 on transmission and ignored on receipt.

EID HMAC ID: Identifier of the HMAC algorithm used to protect the

integrity of the EID-AD.  See Section 5.7 for more details.

EID mask-len: Mask length for EID-prefix.

EID-AFI: Address family of EID-prefix according to [RFC5226].

Maino, et al.             Expires June 2, 2019                 [Page 10]

Internet-Draft                  LISP-SEC                   November 2018

EID-prefix: This field contains an EID-prefix that the destination

ETR is authoritative for, and is the longest match for the

requested EID.

EID HMAC: HMAC of the EID-AD, as computed by the Map-Server.

Before computing the HMAC operation the EID HMAC field MUST be set

to 0.  The HMAC covers the entire EID-AD.

PKT-AD Length: length (in bytes) of the Packet Authentication Data

(PKT-AD).

PKT HMAC ID: Identifier of the HMAC algorithm used to protect the

integrity of the Map-Reply.

PKT HMAC: HMAC of the whole Map-Reply packet, including the LISP-

SEC Authentication Data.  The scope of the authentication goes

from the Map-Reply Type field to the PKT HMAC field included.

Before computing the HMAC operation the PKT HMAC field MUST be set

to 0.  See Section 5.8 for more details.

5.3.  Map-Register LISP-SEC Extensions

This memo is allocating one of the bits marked as Unassigned in the

Map-Register message defined in Section 6.1.6 of

[I-D.ietf-lisp-rfc6833bis].  More precisely, the second bit after the

Type field in a Map-Register message is allocated as the S-bit.  The

S-bit indicates to the Map-Server that the registering ETR is LISP-

SEC enabled.

An ETR that supports LISP-SEC MUST set the S-bit in its

Map-Register messages.

5.4.  ITR Processing

Upon creating a Map-Request, the ITR generates a random ITR-OTK that

is stored locally, together with the nonce generated as specified in

[I-D.ietf-lisp-rfc6833bis].

The Map-Request MUST be encapsulated in an ECM, with the S-bit set to

1, to indicate the presence of Authentication Data.  If the ITR and

the Map-Resolver are configured with a shared key, the ITR-OTK

confidentiality SHOULD be protected by wrapping the ITR-OTK with the

algorithm specified by the OTK Encryption ID field.  See Section 5.5

for further details on OTK encryption.

The Requested HMAC ID field contains the suggested HMAC algorithm to

be used by the Map-Server and the ETR to protect the integrity of the

ECM Authentication data and of the Map-Reply.

Maino, et al.             Expires June 2, 2019                 [Page 11]

Internet-Draft                  LISP-SEC                   November 2018

The KDF ID field specifies the suggested key derivation function to

be used by the Map-Server to derive the MS-OTK.  A KDF Value of NONE

(0), MAY be used to specify that the ITR has no preferred KDF ID.

The EID-AD length is set to 4 bytes, since the Authentication Data

does not contain EID-prefix Authentication Data, and the EID-AD

contains only the KDF ID field.

In response to an encapsulated Map-Request that has the S-bit set, an

ITR MUST receive a Map-Reply with the S-bit set, that includes an

EID-AD and a PKT-AD.  If the Map-Reply does not include both ADs, the

ITR MUST discard it.  In response to an encapsulated Map-Request with

S-bit set to 0, the ITR expects a Map-Reply with S-bit set to 0, and

the ITR SHOULD discard the Map-Reply if the S-bit is set.

Upon receiving a Map-Reply, the ITR must verify the integrity of both

the EID-AD and the PKT-AD, and MUST discard the Map-Reply if one of

the integrity checks fails.  After processing the Map-Reply, the ITR

must discard the <nonce,ITK-OTK> pair associated to the Map-Reply

The integrity of the EID-AD is verified using the locally stored ITR-

OTK for this exchange to re-compute the HMAC of the EID-AD using the algorithm

specified in the EID HMAC ID field.  If the EID HMAC ID field does

not match the Requested HMAC ID the ITR SHOULD discard the Map-Reply

and send, at the first opportunity it needs to, a new Map-Request

with a different Requested HMAC ID field, according to ITR's local

policy.  The scope of the HMAC operation covers the entire EID-AD,

from the EID-AD Length field to the EID HMAC field, which must be set

to 0 before the computation of the HMAC.

ITR MUST set the EID HMAC ID field to 0 before computing the HMAC.

To verify the integrity of the PKT-AD, first the MS-OTK is derived

from the locally stored ITR-OTK using the algorithm specified in the

KDF ID field.  This is because the PKT-AD is generated by the ETR

using the MS-OTK.  If the KDF ID in the Map-Reply does not match the

KDF ID requested in the Map-Request, the ITR SHOULD discard the Map-

Reply and send, at the first opportunity it needs to, a new Map-

Request with a different KDF ID, according to ITR's local policy.

The derived MS-OTK is then used to re-compute the HMAC of the PKT-AD

using the Algorithm specified in the PKT HMAC ID field.  If the PKT

HMAC ID field does not match the Requested HMAC ID the ITR SHOULD

discard the Map-Reply and send, at the first opportunity it needs to,

a new Map-Request with a different Requested HMAC ID according to

ITR's local policy or until all HMAC IDs supported by the ITR have

been attempted.

Maino, et al.             Expires June 2, 2019                 [Page 12]

Internet-Draft                  LISP-SEC                   November 2018

Each individual Map-Reply EID-record is considered valid only if: (1)

both EID-AD and PKT-AD are valid, and (2) the intersection of the

EID-prefix in the Map-Reply EID-record with one of the EID-prefixes

contained in the EID-AD is not empty.  After identifying the Map-

Reply record as valid, the ITR sets the EID-prefix in the Map-Reply

record to the value of the intersection set computed before, and adds

the Map-Reply EID-record to its EID-to-RLOC cache, as described in

[I-D.ietf-lisp-rfc6833bis].  An example of Map-Reply record

validation is provided in Section 5.4.1.

The ITR SHOULD send SMR triggered Map-Requests over the mapping

system in order to receive a secure Map-Reply.  If an ITR accepts

piggybacked Map-Replies, it SHOULD also send a Map-Request over the

mapping system in order to verify the piggybacked Map-Reply with a

secure Map-Reply.

5.4.1.  Map-Reply Record Validation

The payload of a Map-Reply may contain multiple EID-records.  The

whole Map-Reply is signed by the ETR, with the PKT HMAC, to provide

integrity protection and origin authentication to the EID-prefix

records claimed by the ETR.  The Authentication Data field of a Map-

Reply may contain multiple EID-records in the EID-AD.  The EID-AD is

signed by the Map-Server, with the EID HMAC, to provide integrity

protection and origin authentication to the EID-prefix records

inserted by the Map-Server.

Upon receiving a Map-Reply with the S-bit set, the ITR first checks

the validity of both the EID HMAC and of the PKT-AD HMAC.  If either

one of the HMACs is not valid, a log action MUST be taken and the

Map-Reply MUST NOT be processed any further.  If both HMACs are

valid, the ITR proceeds with validating each individual EID-record

claimed by the ETR by computing the intersection of each one of the

EID-prefix contained in the payload of the Map-Reply with each one of

the EID-prefixes contained in the EID-AD.  An EID-record is valid

only if at least one of the intersections is not the empty set.

For instance, the Map-Reply payload contains 3 mapping record EID-

prefixes:

2001:db8:102::/48

2001:db8: 103::/48

2001:db8: 200::/40

The EID-AD contains two EID-prefixes:

Maino, et al.             Expires June 2, 2019                 [Page 13]

Internet-Draft                  LISP-SEC                   November 2018

2001:db8:0103::/48

2001:db8:0203::/48

The EID-record with EID-prefix 2001:db8:0102::/48 is not eligible to

be used by the ITR since it is not included in any of the EID-ADs

signed by the Map-Server.  A log action MUST be taken.

The EID-record with EID-prefix 2001:db8:0103::/48 is eligible to be

used by the ITR because it matches the second EID-prefix contained in

the EID-AD.

The EID-record with EID-prefix 2001:db8:0200::/40 is not eligible to

be used by the ITR since it is not included in any of the EID-ADs

signed by the Map-Server.  A log action MUST be taken.  In this last

example the ETR is trying to over claim the EID-prefix

2001:db8:0200::/40, but the Map-Server authorized only

2001:db8:0203::/48, hence the EID-record is discarded.

5.4.2.  PITR Processing

The processing performed by a PITR is equivalent to the processing of

an ITR.  However, if the PITR is directly connected to a Mapping

System such as LISP+ALT [RFC6836], the PITR performs the functions of

both the ITR and the Map-Resolver forwarding the Map-Request

encapsulated in an ECM header that includes the Authentication Data

fields as described in Section 5.6.

5.5.  Encrypting and Decrypting an OTK

MS-OTK confidentiality is REQUIRED in the path between the Map-Server

and the ETR, the MS-OTK SHOULD be encrypted using the preconfigured

key shared between the Map-Server and the ETR for the purpose of

securing ETR registration [I-D.ietf-lisp-rfc6833bis].  Similarly, if

ITR-OTK confidentiality is required in the path between the ITR and

the Map-Resolver, the ITR-OTK SHOULD be encrypted with a key shared

between the ITR and the Map-Resolver.

The OTK is encrypted using the algorithm specified in the OTK

Encryption ID field.  When the AES Key Wrap algorithm is used to

encrypt a 128-bit OTK, according to [RFC3394], the AES Key Wrap

Initialization Value MUST be set to 0xA6A6A6A6A6A6A6A6 (64 bits).

The output of the AES Key Wrap operation is 192-bit long.  The most

significant 64-bit are copied in the One-Time Key Preamble field,

while the 128 less significant bits are copied in the One-Time Key

field of the LISP-SEC Authentication Data.

Maino, et al.             Expires June 2, 2019                 [Page 14]

Internet-Draft                  LISP-SEC                   November 2018

When decrypting an encrypted OTK the receiver MUST verify that the

Initialization Value resulting from the AES Key Wrap decryption

operation is equal to 0xA6A6A6A6A6A6A6A6.  If this verification fails

the receiver MUST discard the entire message.

When a 128-bit OTK is sent unencrypted the OTK Encryption ID is set

to NULL_KEY_WRAP_128, and the OTK Preamble is set to

0x0000000000000000 (64 bits).

5.6.  Map-Resolver Processing

Upon receiving an encapsulated Map-Request with the S-bit set, the

Map-Resolver decapsulates the ECM message.  The ITR-OTK, if

encrypted, is decrypted as specified in Section 5.5.

Protecting the confidentiality of the ITR-OTK and, in general, the

security of how the Map-Request is handed by the Map-Resolver to the

Map-Server, is specific to the particular Mapping System used, and

outside of the scope of this memo.

In Mapping Systems where the Map-Server is compliant with

[I-D.ietf-lisp-rfc6833bis], the Map-Resolver originates a new ECM

header with the S-bit set, that contains the unencrypted ITR-OTK, as

specified in Section 5.5, and the other data derived from the ECM

Authentication Data of the received encapsulated Map-Request.

The Map-Resolver then forwards to the Map-Server the received Map-

Request, encapsulated in the new ECM header that includes the newly

computed Authentication Data fields.

5.7.  Map-Server Processing

Upon receiving an ECM encapsulated Map-Request with the S-bit set,

the Map-Server process the Map-Request according to the value of the

S-bit contained in the Map-Register sent by the ETR during

registration.

If the S-bit contained in the Map-Register was clear the Map-Server

decapsulates the ECM and generates a new ECM encapsulated Map-Request

that does not contain an ECM Authentication Data, as specified in

[I-D.ietf-lisp-rfc6833bis].  The Map-Server does not perform any

further LISP-SEC processing, and the Map-Reply will not be protected.

If the S-bit contained in the Map-Register was set the Map-Server

decapsulates the ECM and generates a new ECM Authentication Data.

The Authentication Data includes the OTK-AD and the EID-AD, that

contains EID-prefix authorization information, that are ultimately

sent to the requesting ITR.

Maino, et al.             Expires June 2, 2019                 [Page 15]

Internet-Draft                  LISP-SEC                   November 2018

The Map-Server updates the OTK-AD by deriving a new OTK (MS-OTK) from

the ITR-OTK received with the Map-Request.  MS-OTK is derived

applying the key derivation function specified in the KDF ID field.

If the algorithm specified in the KDF ID field is not supported, the

Map-Server uses a different algorithm to derive the key and updates

the KDF ID field accordingly.

The Map-Server and the ETR MUST be configured with a shared key for

mapping registration according to [I-D.ietf-lisp-rfc6833bis].  If MS-

OTK confidentiality is required, then the MS-OTK SHOULD be encrypted,

by wrapping the MS-OTK with the algorithm specified by the OTK

Encryption ID field as specified in Section 5.5.

The Map-Server includes in the EID-AD the longest match registered

EID-prefix for the destination EID, and an HMAC of this EID-prefix.

The HMAC is keyed with the ITR-OTK contained in the received ECM

Authentication Data, and the HMAC algorithm is chosen according to

the Requested HMAC ID field.  If The Map-Server does not support this

algorithm, the Map-Server uses a different algorithm and specifies it

in the EID HMAC ID field.  The scope of the HMAC operation covers the

entire EID-AD, from the EID-AD Length field to the EID HMAC field,

which must be set to 0 before the computation.

The Map-Server then forwards the updated ECM encapsulated Map-

Request, that contains the OTK-AD, the EID-AD, and the received Map-

Request to an authoritative ETR as specified in

[I-D.ietf-lisp-rfc6833bis].

5.7.1.  Map-Server Processing in Proxy mode

If the Map-Server is in proxy mode, it generates a Map-Reply, as

specified in [I-D.ietf-lisp-rfc6833bis], with the S-bit set to 1.

The Map-Reply includes the Authentication Data that contains the EID-

AD, computed as specified in Section 5.7, as well as the PKT-AD

computed as specified in Section 5.8.

5.8.  ETR Processing

Upon receiving an ECM encapsulated Map-Request with the S-bit set,

the ETR decapsulates the ECM message.  The OTK field, if encrypted,

is decrypted as specified in Section 5.5 to obtain the unencrypted

MS-OTK.

The ETR then generates a Map-Reply as specified in

[I-D.ietf-lisp-rfc6833bis] and includes the Authentication Data that

contains the EID-AD, as received in the encapsulated Map-Request, as

well as the PKT-AD.

Maino, et al.             Expires June 2, 2019                 [Page 16]

Internet-Draft                  LISP-SEC                   November 2018

The EID-AD is copied from the Authentication Data of the received

encapsulated Map-Request.

The PKT-AD contains the HMAC of the whole Map-Reply packet, keyed

with the MS-OTK and computed using the HMAC algorithm specified in

the Requested HMAC ID field of the received encapsulated Map-Request.

If the ETR does not support the Requested HMAC ID, it uses a

different algorithm and updates the PKT HMAC ID field accordingly.

The scope of the HMAC operation covers the entire PKT-AD, from the

Map-Reply Type field to the PKT HMAC field, which must be set to 0

before the computation.

Finally the ETR sends the Map-Reply to the requesting ITR as

specified in [I-D.ietf-lisp-rfc6833bis].

6.  Security Considerations

6.1.  Mapping System Security

The LISP-SEC threat model described in Section 3, assumes that the

LISP Mapping System is working properly and eventually delivers Map-

Request messages to a Map-Server that is authoritative for the

requested EID.

It is assumed that the Mapping System ensures the confidentiality of

the OTK, and the integrity of the Map-Reply data.  However, how the

LISP Mapping System is secured is out of the scope of this document.

Similarly, Map-Register security, including the right for a LISP

entity to register an EID-prefix or to claim presence at an RLOC, is

out of the scope of LISP-SEC.

6.2.  Random Number Generation

The ITR-OTK MUST be generated by a properly seeded pseudo-random (or

strong random) source.  See [RFC4086] for advice on generating

security-sensitive random data

6.3.  Map-Server and ETR Colocation

If the Map-Server and the ETR are colocated, LISP-SEC does not

provide protection from overclaiming attacks mounted by the ETR.

However, in this particular case, since the ETR is within the trust

boundaries of the Map-Server, ETR's overclaiming attacks are not

included in the threat model.

Maino, et al.             Expires June 2, 2019                 [Page 17]

Internet-Draft                  LISP-SEC                   November 2018

6.4.  Deploying LISP-SEC

This memo is written according to [RFC2119].  Specifically, the use

of the key word SHOULD "or the adjective 'RECOMMENDED', mean that

there may exist valid reasons in particular circumstances to ignore a

particular item, but the full implications must be understood and

carefully weighed before choosing a different course".

Those deploying LISP-SEC according to this memo, should carefully

weight how the LISP-SEC threat model applies to their particular use

case or deployment.  If they decide to ignore a particular

recommendation, they should make sure the risk associated with the

corresponding threats is well understood.

As an example, in certain closed and controlled deployments, it is

possible that the threat associated with a MiTM between the xTR and

the Mapping System is very low, and after carfeul consideration it

may be decided to allow a NULL key wrapping algorithm while carrying

the OTKs between the xTR and the Mapping System.

As an example at the other end of the spectrum, in certain other

deployments, attackers may be very sophisticated, and force the

deployers to enforce very strict policies in term of HMAC algorithms

accepted by an ITR.

Similar considerations apply to the entire LISP-SEC threat model, and

should guide the deployers and implementors whenever they encounter

the key word SHOULD across this memo.

6.5.  Shared Keys Provisioning

Provisioning of the keys shared between the ITR and the Map-Resolver

as well as between the ETR and the Map-Server should be performed via

an orchestration infrastructure and it is out of the scope of this

draft.  It is recommended that both shared keys are refreshed at

periodical intervals to address key aging or attackers gaining

unauthorized access to the shared keys.  Shared keys should be

unpredictable random values.

6.6.  Replay Attacks

An attacker can capture a valid Map-Request and/or Map-Reply and

replay it, however once the ITR receives the original Map-Reply the

<nonce,ITR-OTK> pair stored at the ITR will be discarded.  If a

replayed Map-Reply arrives at the ITR, there is no <nonce,ITR-OTK>

that matches the incoming Map-Reply and will be discarded.

Maino, et al.             Expires June 2, 2019                 [Page 18]

Internet-Draft                  LISP-SEC                   November 2018

In case of replayed Map-Request, the Map-Server, Map-Resolver and ETR

will have to do a LISP-SEC computation.  This is equivalent to a

valid LISP-SEC computation and an attacker does not obtain any

benefit.

6.7.  Message Privacy

DTLS [RFC6347] SHOULD be used to provide communication privacy and to

prevent eavesdropping, tampering, or message forgery to the messages

exchanged between the ITR, Map-Resolver, Map-Server, and ETR.

6.8.  Denial of Service and Distributed Denial of Service Attacks

LISP-SEC mitigates the risks of Denial of Service and Distributed

Denial of Service attacks by protecting the integrity and

authenticating the origin of the Map-Request/Map-Reply messages, and

by preventing malicious ETRs from overclaiming EID prefixes that

could re-direct traffic directed to a potentially large number of

hosts.

7.  IANA Considerations

7.1.  ECM AD Type Registry

IANA is requested to create the "ECM Authentication Data Type"

registry with values 0-255, for use in the ECM LISP-SEC Extensions

Section 5.1.  The registry MUST be initially populated with the

following values:

Name                     Value        Defined In

-------------------------------------------------

Reserved                 0             This memo

LISP-SEC-ECM-EXT         1             This memo

HMAC Functions

Values 2-255 are unassigned.  They are to be assigned according to

the "Specification Required" policy defined in [RFC5226].

7.2.  Map-Reply AD Type Registry

IANA is requested to create the "Map-Reply Authentication Data Type"

registry with values 0-255, for use in the Map-Reply LISP-SEC

Extensions Section 5.2.  The registry MUST be initially populated

with the following values:

Maino, et al.             Expires June 2, 2019                 [Page 19]

Internet-Draft                  LISP-SEC                   November 2018

Name                     Value        Defined In

-------------------------------------------------

Reserved                 0             This memo

LISP-SEC-MR-EXT          1             This memo

HMAC Functions

Values 2-255 are unassigned.  They are to be assigned according to

the "Specification Required" policy defined in [RFC5226].

7.3.  HMAC Functions

IANA is requested to create the "LISP-SEC Authentication Data HMAC

ID" registry with values 0-65535 for use as Requested HMAC ID, EID

HMAC ID, and PKT HMAC ID in the LISP-SEC Authentication Data:

Name                     Number        Defined In

-------------------------------------------------

NONE                     0             This memo

AUTH-HMAC-SHA-1-96       1             [RFC2104]

AUTH-HMAC-SHA-256-128    2             [RFC6234]

HMAC Functions

Values 3-65535 are unassigned.  They are to be assigned according to

the "Specification Required" policy defined in [RFC5226].

AUTH-HMAC-SHA-1-96 MUST be supported, AUTH-HMAC-SHA-256-128 SHOULD be

supported.

7.4.  Key Wrap Functions

IANA is requested to create the "LISP-SEC Authentication Data Key

Wrap ID" registry with values 0-65535 for use as OTK key wrap

algorithms ID in the LISP-SEC Authentication Data:

Name                     Number        Defined In

-------------------------------------------------

Reserved                 0             This memo

NULL-KEY-WRAP-128        1             This memo

AES-KEY-WRAP-128         2             [RFC3394]

Key Wrap Functions

Maino, et al.             Expires June 2, 2019                 [Page 20]

Internet-Draft                  LISP-SEC                   November 2018

Values 3-65535 are unassigned.  They are to be assigned according to

the "Specification Required" policy defined in [RFC5226].

NULL-KEY-WRAP-128, and AES-KEY-WRAP-128 MUST be supported.

NULL-KEY-WRAP-128 is used to carry an unencrypted 128-bit OTK, with a

64-bit preamble set to 0x0000000000000000 (64 bits).

7.5.  Key Derivation Functions

IANA is requested to create the "LISP-SEC Authentication Data Key

Derivation Function ID" registry with values 0-65535 for use as KDF

ID in the LISP-SEC Authentication Data:

Name                     Number        Defined In

-------------------------------------------------

NONE                     0             This memo

HKDF-SHA1-128            1             [RFC5869]

Key Derivation Functions

Values 2-65535 are unassigned.  They are to be assigned according to

the "Specification Required" policy defined in [RFC5226].

HKDF-SHA1-128 MUST be supported

8.  Acknowledgements

The authors would like to acknowledge Pere Monclus, Dave Meyer, Dino

Farinacci, Brian Weis, David McGrew, Darrel Lewis and Landon Curt

Noll for their valuable suggestions provided during the preparation

of this document.

9.  Normative References

[I-D.ietf-lisp-rfc6830bis]

Farinacci, D., Fuller, V., Meyer, D., Lewis, D., and A.

Cabellos-Aparicio, "The Locator/ID Separation Protocol

(LISP)", draft-ietf-lisp-rfc6830bis-26 (work in progress),

November 2018.

[I-D.ietf-lisp-rfc6833bis]

Fuller, V., Farinacci, D., and A. Cabellos-Aparicio,

"Locator/ID Separation Protocol (LISP) Control-Plane",

draft-ietf-lisp-rfc6833bis-22 (work in progress), November

2018.

Maino, et al.             Expires June 2, 2019                 [Page 21]

Internet-Draft                  LISP-SEC                   November 2018

[RFC2104]  Krawczyk, H., Bellare, M., and R. Canetti, "HMAC: Keyed-

Hashing for Message Authentication", RFC 2104,

DOI 10.17487/RFC2104, February 1997, <https://www.rfc-

editor.org/info/rfc2104>.

[RFC2119]  Bradner, S., "Key words for use in RFCs to Indicate

Requirement Levels", BCP 14, RFC 2119,

DOI 10.17487/RFC2119, March 1997, <https://www.rfc-

editor.org/info/rfc2119>.

[RFC3394]  Schaad, J. and R. Housley, "Advanced Encryption Standard

(AES) Key Wrap Algorithm", RFC 3394, DOI 10.17487/RFC3394,

September 2002, <https://www.rfc-editor.org/info/rfc3394>.

[RFC4086]  Eastlake 3rd, D., Schiller, J., and S. Crocker,

"Randomness Requirements for Security", BCP 106, RFC 4086,

DOI 10.17487/RFC4086, June 2005, <https://www.rfc-

editor.org/info/rfc4086>.

[RFC5226]  Narten, T. and H. Alvestrand, "Guidelines for Writing an

IANA Considerations Section in RFCs", RFC 5226,

DOI 10.17487/RFC5226, May 2008, <https://www.rfc-

editor.org/info/rfc5226>.

[RFC5869]  Krawczyk, H. and P. Eronen, "HMAC-based Extract-and-Expand

Key Derivation Function (HKDF)", RFC 5869,

DOI 10.17487/RFC5869, May 2010, <https://www.rfc-

editor.org/info/rfc5869>.

[RFC6234]  Eastlake 3rd, D. and T. Hansen, "US Secure Hash Algorithms

(SHA and SHA-based HMAC and HKDF)", RFC 6234,

DOI 10.17487/RFC6234, May 2011, <https://www.rfc-

editor.org/info/rfc6234>.

[RFC6347]  Rescorla, E. and N. Modadugu, "Datagram Transport Layer

Security Version 1.2", RFC 6347, DOI 10.17487/RFC6347,

January 2012, <https://www.rfc-editor.org/info/rfc6347>.

[RFC6836]  Fuller, V., Farinacci, D., Meyer, D., and D. Lewis,

"Locator/ID Separation Protocol Alternative Logical

Topology (LISP+ALT)", RFC 6836, DOI 10.17487/RFC6836,

January 2013, <https://www.rfc-editor.org/info/rfc6836>.

[RFC7835]  Saucez, D., Iannone, L., and O. Bonaventure, "Locator/ID

Separation Protocol (LISP) Threat Analysis", RFC 7835,

DOI 10.17487/RFC7835, April 2016, <https://www.rfc-

editor.org/info/rfc7835>.

Maino, et al.             Expires June 2, 2019                 [Page 22]

Internet-Draft                  LISP-SEC                   November 2018

Authors' Addresses

Fabio Maino

Cisco Systems

170 Tasman Drive

San Jose, California  95134

USA

Email: fmaino@cisco.com

Vina Ermagan

Cisco Systems

170 Tasman Drive

San Jose, California  95134

USA

Email: vermagan@cisco.com

Albert Cabellos

Universitat Politecnica de Catalunya

c/ Jordi Girona s/n

Barcelona  08034

Spain

Email: acabello@ac.upc.edu

Damien Saucez

INRIA

2004 route des Lucioles - BP 93

Sophia Antipolis

France

Email: damien.saucez@inria.fr

Maino, et al.             Expires June 2, 2019                 [Page 23]

# Comments

Accepted

You may indicate that intercepting a Map-Register would lead to a similar attack, but authentication means already described in 6833bis are sufficient (?) to detect such attack.

Accepted, addressed together with the next comment.

It can be useful to motivate the scope

Added reference to 6833bis

Accepted

There is no such section in the 6833bis.

Removed reference to section.

Which access network?

LISP may be deployed in DCs, for example. What would be access network, then?

Removed ‘access network’

accepted

Providing samples of such « secure distribution» would be useful.

Accepted. Added reference to section 5.5.

Any recommendation about key generation (e.g., rfc4086) ?

Rejected. Consideration on OTK randomness are in section 6.2

I guess this is done for each for each Map-Request/Map-Reply exchange. Please update the text accordingly.

Accepted. Specified that a new OTK is generated per each Map-request

Accepted

Accepted

What are the implications if this SHOULD is not followed? Wouldn’t the ITR-OTK be then available for misuse?

Accepted in principle. New text specifies that OTK encryption is a MUST, and how unencrypted OTK is allowed only when DTLS is enabled.

You may recall why this exchange is “secure” under the threat model described above.

Accepted in principle, adding a reference to the threat model section

where ?

Accepted by adding reference to Proxy section

Idem as Med8.

Accepted. Addressed as in Med8

Specified that the next two steps, when in proxy mode, are skipped.,

where ?

Removed standard as per the next 2 cmments

How this is ensured ?

Accepted. Mentioned that KDF is psecified in the Map-Reply

Already introduced above

All comments accepted.

Accepted

Accepted

Accepted

Accepted

Instead of pointing to that section, it is helpful to have more description about this field here.

How the ITR sets this value when multiple hmacs are supported ?

Accepted

Accepted

Accepted

Accepted, Changed to 8060 (LCAF)

This RFC is about IANA considerations. Why is it listed here?

Accepted

Accepted both the following 2 comments

Accepted all cooments related to Figure

Accepted

Accepted. Changed to 8060 (LCAF)

I fail to see why this is cited. Please check

Accepted

Accepted

Accepted

Please check this.

Accepted

It is not easy to follow the operations. I suggest to organize the text as follows:

- Generating Map-Request by an ITR

- Processing Map-Request by a Map-Resolver

- Processing ECM by an ETR

…

- Processing Map-Reply by an ITR

Accepted in principle

Maybe mention this is stored for the duration of the exchange.

Accepted

Accepted

It may be worth to mention that, absent consistent configuration of involved entities, extra delays will be experienced to resolve a mapping.

You may consider adding some text to indicate the mandatory-to-support IDs.

Unless configured otherwise, these IDs MUST be used in the sec extension messages.

Accepted

Accepted in all the IPv6 examples that follows

leading zeros must be removed as per RFC5952

Accepted in principle

to be mentionned earlier in the document

Accepted

To be moved  to teh core text.

Accepted

Should be mentioned in the text earlier.

Accepted

Why this one is normative ?

Accepted. Moved to informative