## Slide 1: LISP Multi-AS Backbones
Victor Moreno (vimoreno@cisco.com)
LISP-WG IETF 111 July 2021

## Slide 2: Agenda
Uberlay and GB-LISP Recap
Multi-AS Federation Requirements
Next steps

## Slide 3: Ground Based LISP (GBL) - Reference Topology
AOC - ATS Region X
Radio Region 1
Radio Region 2
Interworking Region (LISP RLOC Space)
A-R
AC-R
A-R
handover
Multi-link / Handover
AC-R
AC-R
A/G-R
A/G-R
G/G-R
LISP MS/MR
IPv6 ICAO Net X
IPv6 ICAO Net Y
A/G-R: Air/Ground Router (LISP XTR)
G/G-R: Ground/Ground Router (LISP XTR)
ATS-E: ATS End-system
AC-R: Access Ground Router
A-R: Airborne Router
A-E: Airborne End-system
SP-A
SP-C
SP-B

## Slide 4: ICAO Federated Network
The International Civil Aviation Organization (ICAO) Aeronautical Telecommunications Network (ATN) is run by a consortium of different providers.
  This network must support mobility and multi-homing across the different providers
The Uberlay model has been proposed as a way to architect this mixed environment.
The providers require a mechanism to peer with each other without requiring an intermediary organization to run the Uberlay for them.
  A federated Uberlay Mapping System amongst the providers is desirable.
  Peering agreements must be enforced

## Slide 5: ICAO – Existing peering agreements
CSP A
CSP B
CSP C
Radio Region
Radio Region
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC/ATC
AOC/ATC
Underlay Inter AS EBGP
Underlay ASBR
CSP = Communication Service Provider
A/G-R
A/G-R
G/G-R
G/G-R
AOC/ATC
AOC/ATC
A/G-R
A/G-R
G/G-R
G/G-R
AOC/ATC
AOC/ATC
EBGP
EBGP
EBGP

## Slide 6: ICAO – Uberlay Structure
CSP A
CSP B
CSP C
Radio Region
Radio Region
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC/ATC
AOC/ATC
Underlay Inter AS EBGP
EBGP
Underlay ASBR
CSP = Communication Service Provider
EBGP
A/G-R
A/G-R
G/G-R
G/G-R
AOC/ATC
AOC/ATC
A/G-R
A/G-R
G/G-R
G/G-R
AOC/ATC
AOC/ATC
EBGP
Uberlay
Site-Overlays (west)
Site-Overlays (east)
RTR-E
RTR-E
RTR-E
RTR-W
RTR-W
RTR-W

## Slide 7: ICAO – Uberlay Mapping System Federation
CSP A
CSP B
CSP C
Radio Region
Radio Region
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC/ATC
AOC/ATC
Inter & Intra CSP Federation
EBGP
Underlay ASBR
CSP = Communication Service Provider
EBGP
A/G-R
A/G-R
G/G-R
G/G-R
AOC/ATC
AOC/ATC
A/G-R
A/G-R
G/G-R
G/G-R
AOC/ATC
AOC/ATC
EBGP
Uberlay
Site-Overlays (west)
Site-Overlays (east)
RTR-E
RTR-E
RTR-E
RTR-W
RTR-W
RTR-W
CSP A
CSP B
CSP C
Mapping System Federation

## Slide 8: Multi-AS Uberlay - Federation
Underlay-AS-A
Underlay-AS-B
Underlay-AS-C
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-C
XTR-A
XTR-B1
MS-A
MS-C
MS-B
XTR-B2
Each MS/MR services the XTRs in its AS
As hosts move, their EIDs must be registered to the MS in the AS they are connected to
EID related Peering agreements across ASs must be enforced
MS = MS+MR in all diagrams
EBGP
Underlay Inter AS EBGP
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 9: Peering agreements and policies
Underlay-AS-A
Underlay-AS-B
Underlay-AS-C
LISP MS/MR
Border Router
LISP MS Federation
Underlay ASBR
XTR-C
XTR-A
XTR-B1
MS-A
MS-C
MS-B
XTR-B2
Policies Based on peering Agreements
  Transit: EID-prefixes allowed/denied in certain ASs
  Ingress: Preferable terms via a particular AS_PATH
MS = MS+MR in all diagrams
EBGP
Underlay Inter AS EBGP
Peering Agreements
Refer to EID prefixes
Terms of Service
Govern use of all resources in the AS (Over & Under)
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 10: Multi-AS Uberlay – Scenarios
LISP MS/MR
Border Router
Underlay ASBR
Paths:
  Multi-AS Transit
  Direct
  Transit
  Intra-AS
MS = MS+MR
Underlay-AS-A
Underlay-AS-B
Underlay-AS-C
XTR-C2
XTR-A
XTR-B1
MS-A
MS-C-West
MS-B
XTR-B2
Underlay Inter AS EBGP
MS-C-East
XTR-C1
Underlay-AS-D
Underlay-AS-E
XTR-D
MS-D
MS-E
XTR-E
1
2
3
4
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 11: Summary of Requirements
Scope overlay resources (XTRs, MS/MRs) per Underlay-AS
  Intra-AS scopes are a secondary requirement
Federation without intermediaries
Scope EID state per AS or intra-AS region
Support intra and inter-AS connectivity
Support EID mobility across ASs
Support EID multi-homing
Enforce policies derived from peering agreements (match on EID enforce in the underlay)
Support different path scenarios: Transit, Direct, Intra-AS
Should not require RTRs at AS-Borders

## Slide 12: Next steps
Firm up requirements definition: draft-moreno-lisp-multi-as
Explore applicability of DDT, document as deployment
Explore alternative approaches if necessary

## Slide 14: Background Information

## Slide 15: Drivers for Re-homing EIDs across CSP Uberlay Map Systems
Resiliency and survivability. A problem in one CSP should not impact aircraft connected to other CSPs
Latency. Minimize RTT of signaling
Authority assignment. CSPs must be able to autonomously render and assure services, service levels and the enforcement of policies
Accountability and Audit. CSPs are accountable for all communications of connected devices and must be able to show complete Audit logs
Trust. Limited across CSPs, governments and other stakeholders
Notes: ATC, AOC, Drones all in different IP address spaces. These will all be subject to policies (regional and cross CSP constraints).
Mention the inclusion of DSCP/Port and other numbers
Policy Context Prefix, Application, Radio Link

## Slide 16: Requirements for a Federated Mapping System
EIDs should be in full control of the SP they attach to.
The Federated Mapping System in the Uberlay should support the peering agreements by different mechanisms (e.g. engineered paths, etc.)
Each SP should be autonomous in defining and enforcing policy for EIDs connected to their network. The policy includes constraints derived from peering agreements.
An EID (aircraft) may multi-home to 2 or more provider networks. So policies would likely need to be enforced at a flow level (Src+Dest RLOCs rather than a Pure Destination EID level)

## Slide 17: Options to Consider
Cache Referral System / DDT
New Mobility enhancements for a Federated Mapping System
LISP De-cent
Others …
Document as its own draft? Or part of the Uberlay draft?

## Slide 18: Concerns
Avoid replicating the underlay BGP peering topology in the overlay
The policy applied must be consistent with the underlay peering agreements
Mobility of EID registrations between Administrative Domains may be a hard requirement. This would mean moving the point of authority in the MS federation (ruling out a few of the existing mechanisms)

## Slide 19: ICAO – Use Case 1: Air Traffic Control
Radio Region
Radio Region
CSP A-West
CSP A-East
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
ANSP A
ANSP B
RTR-W
RTR-E
Mapping System Federation
EBGP
Underlay ASBR
Air Traffic Control (ATC) communications are Regional, but cross-CSPs
A dedicated IP address for ATC (ATC-EID) has been proposed.
Policy: maintain the ATC EIDs local to the region, all CSPs involved must be updated
Uberlay
CSP B-West
CSP B-East

## Slide 20: ICAO – Use Case 2: Airline Operation Control
Radio Region
Radio Region
CSP A
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC Airline 1
AOC Airline 2
RTR-W
RTR-E
Mapping System Federation
Underlay ASBR
Airline Operation Control (AOC) communications may traverse CSPs, often an Airline will work with a single global CSP
A dedicated IP address for AOC (AOC-EID) has been proposed.
Policy: Maintain authority @ connecting CSP’s Uberlay Mapping System
  Registrations, Access Control, Accountability
  Path preferences expressed by aircraft, rendered by CSPs
Uberlay

## Slide 21: ICAO – Use Case 3: Multi-link
Radio Region
Radio Region
CSP B
G/G-R
A/G-R
LISP MS/MR
Border Router
AOC/ATC
RTR-B
CSP C
A/G-R
G/G-R
AOC/ATC
RTR-C
EBGP
Underlay ASBR
Mapping System Federation
Uberlay
Aircraft connects to more than one CSP
Aircraft sends communication preferences to A/G-Rs (A/G Interface) per GB-LISP
  Mappings are registered with matching Priorities and Weights
  Aircraft signals whether it is leaving a link or adding new links
RTRs register the separate Aircraft mappings in the different Uberlay Map Servers
Federated MS must merge the mappings for the aircraft
  Map-Notifications
  LISP-decent updates
  Others?
  Discuss whether there is a need for a site or region identifier
MS-U-C
MS-U-B

## Slide 22: ICAO – Use Case 4 – Path Preference
Radio Region
Radio Region
CSP A
CSP B
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC
AOC/ATC
RTR-W
RTR-E
CSP C
A/G-R
G/G-R
AOC/ATC
RTR-S
Mapping System Federation
EBGP
EBGP
EBGP
Underlay ASBR
Uberlay
Some policies may dictate path restrictions
  Aircraft/Airline preferences
  CSP peering agreements
These (x)EID/Application level policies must be enforceable in the Uberlay

## Slide 23: Ground Based LISP (GBL) – Behavior (1)
AOC - ATS Region X
Radio Region 1
Radio Region 2
Interworking Region (LISP RLOC Space)
A-R
AC-R
AC-R
A/G-R1
A/G-R2
G/G-R
LISP MS/MR
IPv6 ICAO Net X
Aircraft attaches to one or more A/G Networks
A/G Network advertises reachability of the aircraft delegated prefix (EID)
Mapping Server maintains RLOC-EID mapping
Each AGR has RLOC address
Aircraft preference and link QoS can be signalled over A/G Network
Radio Region 3
AC-R
A/G-R3
GGR needs to query which RLOC(s) serve destination EID
Traffic tunnelled over Internetwork
EID | RLOC
Y | AGR1 – Priority 1, 50% AGR2 – Priority 1, 50%
Map-cache:
Y via
AGR2(50) & AGR1(50)

## Slide 24: Ground Based LISP (GBL) – Behavior (2)
AOC - ATS Region X
Radio Region 1
Radio Region 2
Interworking Region (LISP RLOC Space)
A-R
AC-R
AC-R
A/G-R1
A/G-R2
G/G-R
LISP MS/MR
IPv6 ICAO Net X
Aircraft attaches to one or more A/G Networks
A/G Network advertises reachability of the aircraft delegated prefix (EID)
Each AGR has RLOC address
Aircraft preference and link QoS can be signalled over A/G Network
Radio Region 3
AC-R
A/G-R3
Traffic tunnelled over Internetwork
Route optimised for served ground users
Map-cache:
Y via
AGR2(50) & AGR1(50)
EID | RLOC
Y | AGR1 – Priority 1, 50% AGR2 – Priority 1, 50%
EID | RLOC
Y | AGR1 – Priority 1, 50% AGR2 – Priority 2, 50% AGR3 – Priority 1, 50%
Map-cache:
Y via
AGR3(50) & AGR1(50)

## Slide 25: Per Application Path Preference
AOC - ATS Region X
Radio Region 1
Radio Region 2
Interworking Region (LISP RLOC Space)
A-R
AC-R
A-R
AC-R
AC-R
A/G-R1
A/G-R2
G/G-R
LISP MS/MR
IPv6 ICAO Net X
IPv6 ICAO Net Y
Air-to-ground path decided on Aircraft Router
Ground-to-air path governed by Aircraft defined metrics
Exception routing for certain Apps based on DSCP
A-R Advertises Preference and Quality Metric
(e.g. Route Solicitation)
Metric registered as priority/weight for ICAO Net-Y
Choose A/G-R based on priority/weight
Metric is Propagated
EID (IP, DSCP) | RLOC
Y, Green | AGR1 – P2 AGR2 – P1
Y, Red | AGR1 – P1 AGR2 – P2
Notes: Demand based: Context aware map replies: In the context of AOC (low cost) vs. in the context ATS

## Slide 26: Session Establishment and Subscription
AOC - ATS Region X
Radio Region 1
Radio Region 2
Interworking Region (LISP RLOC Space)
A-R
AC-R
A-R
AC-R
AC-R
A/G-R 1
A/G-R 2
G/G-R X
LISP MS/MR
IPv6 ICAO Net X
IPv6 ICAO Net Y
Map-reply
G/G-R-X is subscribed to NetY
Map-request + subscribe
Forwarding path before Map Resolution is complete

## Slide 27: Optimized Multi-link mobility (1)
AOC - ATS Region X
Radio Region 1
Radio Region 2
Interworking Region (LISP RLOC Space)
A-R
AC-R
A-R
AC-R
AC-R
A/G-R 1
A/G-R 2
G/G-R X
LISP MS/MR
IPv6 ICAO Net X
IPv6 ICAO Net Y
Forwarding path via best metric
Better metric pushed to subscribers
Regional Peers are notified
Only subscribers and regional peers are updated
Map-Notify Subscribers
G/G-R-X is subscribed to NetY
Advertise Net-Y with better metric
Map-Notify Regional Peers

## Slide 28: Optimized Multi-link mobility (2)
AOC - ATS Region X
Radio Region 1
Radio Region 2
Interworking Region (LISP RLOC Space)
A-R
A-R
IPv6 ICAO Net X
IPv6 ICAO Net Y
Traffic redirect complete
Signaled only relevant Routers
Seamless Convergence (direct subscriber cache update)
Direct Connectivity (no anchor points)
G/G-R-X is subscribed to NetY
A/G-R 1
A/G-R 2
G/G-R X
LISP MS/MR
AC-R
AC-R
AC-R

## Slide 29: ICAO – Existing peering agreements
Radio Region
Radio Region
CSP A
CSP B
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC/ATC
AOC/ATC
CSP C
Underlay Inter AS EBGP
EBGP
EBGP
EBGP
Underlay ASBR
CSP = Communication Service Provider

## Slide 30: ICAO – Uberlay Structure
Radio Region
Radio Region
CSP A
CSP B
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC/ATC
AOC/ATC
RTR-W
RTR-E
CSP C
A/G-R
G/G-R
AOC/ATC
RTR-S
Underlay Inter AS EBGP
Uberlay LISP MS Federation
EBGP
EBGP
EBGP
Underlay ASBR
Uberlay
Site-Overlay
Site-Overlay
Site-Overlay

## Slide 31: ICAO – Uberlay Mapping System Federation
Radio Region
Radio Region
CSP A
CSP B
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC/ATC
AOC/ATC
RTR-W
RTR-E
CSP C
A/G-R
G/G-R
AOC/ATC
RTR-S
Mapping System Federation
Underlay Inter AS EBGP
Uberlay LISP MS Federation
EBGP
EBGP
EBGP
Underlay ASBR