| MIPSHOP WG | Gabor Bajko |
| --- | --- |
| Internet Draft | Nokia |
| Intended Status: Standards Track | Subir Das |
| Expires: August 1, 2008 | Telcordia |
|  | February 1, 2008 |

Dynamic Host Configuration Protocol (DHCPv4 and DHCPv6) Options for Mobility Server (MoS) discovery

draft-bajko-mos-dhcp-options-02

Status of this Memo

By submitting this Internet-Draft, each author represents that any applicable patent or other IPR claims of which he or she is aware have been or will be disclosed, and any of which he or she becomes aware will be disclosed, in accordance with Section 6 of BCP 79.

Internet-Drafts are working documents of the Internet Engineering Task Force (IETF), its areas, and its working groups. Note that other groups may also distribute working documents as Internet-Drafts.

Internet-Drafts are draft documents valid for a maximum of six months and may be updated, replaced, or obsoleted by other documents at any time. It is inappropriate to use Internet-Drafts as reference material or to cite them other than as "work in progress."

The list of current Internet-Drafts can be accessed at http://www.ietf.org/ietf/1id-abstracts.txt.

The list of Internet-Draft Shadow Directories can be accessed at http://www.ietf.org/shadow.html.

This Internet-Draft will expire on August 1, 2008.

Copyright Notice

Copyright (C) The IETF Trust (2008).

Abstract

This document defines a number of Dynamic Host Configuration Protocol (DHCP-for-IPv4 and DHCP-for-IPv6) options that contain a list of domain names or IP addresses that can be mapped to servers providing IEEE 802.21 type of Mobility Services. These Mobility Services are used to assist an MN in handover preparation (network discovery) and handover decision (network selection). The services addressed by this document are the Media Independent Handover Services defined in [1].

Conventions used in this document

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD", "SHOULD NOT", "RECOMMENDED",  "MAY", and "OPTIONAL" in this document are to be interpreted as described in RFC-2119 [].

Terminology and abbreviations used in this document

Mobility Services: comprises of a set of different services provided by the network to mobile nodes to facilitate handover preparation and handover decision.

Mobility Server: a network node providing Mobility Support Services.

MIH: Media Independent Handover, as defined in [1].

MIH Service: IS, ES or CS type of service, as defined in [1].

Table of Content

1. Introduction ...................................................2

2. DHCPv4 Options for MoS Discovery................................3

2.1 Domain Name List .........................................4

2.2 IPv4 Address List ........................................5

3. DHCPv6 Options for MoS Discovery................................5

3.1 MoS Identifier Option.....................................6

3.2 IPv6 Relay Agent MoS Option...............................7

3.3 MoS Information Option                                    8

4. Option Usage                                                   10

4.1 Usage of DHCPv4 Options for MoS Discovery                10

4.2 Usage of DHCPv6 Options for MoS Discovery                11

5. Security Considerations .......................................11

6. IANA Considerations ...........................................11

7. Acknowledgements ..............................................12

8. Normative References ..........................................12

9. Informative References ........................................12

10. Author's Addresses ...........................................12

1. Introduction

IEEE 802.21 [1] defines three distinct service types to facilitate link layer handovers across heterogeneous technologies:

a) Information Services (IS)

IS provides a unified framework to the higher layer entities across the heterogeneous network environment to facilitate discovery and selection of multiple types of networks existing within a geographical area, with the objective to help the higher layer mobility protocols to acquire a global view of the heterogeneous networks and perform seamless handover across these networks.

b) Event Services (ES)

Events may indicate changes in state and transmission behavior of the physical, data link and logical link layers, or predict state changes of these layers. The Event Service may also be used to indicate management actions or command status on the part of the network or some management entity.

c) Command Services (CS)

The command service enables higher layers to control the physical, data link, and logical link layers. The higher layers may control the reconfiguration or selection of an appropriate link through a set of handover commands.

In IEEE terminology these services are called Media Independent Handover (MIH) services.

While these services may be co-located, the different pattern and type of information they provide does not necessitate the co-location.

An MN may make use of any of these MIH service types separately or any combination of them.

It is anticipated that a Mobility Server will not necessarily host all three of these MIH services together, thus there is a need to discover the MIH services types separately.

This document defines three dhcp options for DHCPv4 and DHCPv6, one for each of the services defined in [1], namely IS, ES and CS. The options would allow an MN to locate a Mobility Server which hosts the desired MIH service type (IS, ES or CS) the MN is looking for. This is one of the possible solutions for locating a server providing Mobility Services; manual configuration is an example of another.

2. DHCPv4 Options for MoS Discovery

This section describes three options for DHCPv4.

The DHCPv4 options for MoS discovery carry either a 32-bit (binary) IPv4 address or, preferably, a DNS [RFC1035] fully-qualified domain name to be used by the MN to locate a server hosting either an IS, an ES or a CS service.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|OPTION_code|    Length     |      enc      |  ...

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

...   Mos Server (domain name or IP address list)

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Option code: IPv4 MoS option codes assigned by IANA (tbd), separate ones for IS (IPv4-IS), for ES (IPv4-ES) and CS (IPv4-CS).

Length: indicates the total number of octets in the option following the 'Length' field, including the encoding byte

enc: one byte indicating the encoding type of the next field

The options have two encodings, specified by the encoding byte ('enc') that follows the code byte. If the encoding byte has the value 0, it is followed by a list of domain names, as described below (Section 2.1). If the encoding byte has the value 1, it is followed by one or more IPv4 addresses (Section 2.2). All implementations MUST support both encodings. The 'Length' field indicates the total number of octets in the option following the 'Length' field, including the encoding byte.

A DHCP server MUST NOT mix the two encodings in the same DHCP message, even if it sends two different instances of the same option. Attempts to do so would result in incorrect client behavior as DHCP processing rules call for the concatenation of multiple instances of an option into a single option prior to processing the option [7].

The code for the MIH IS option is XXX. The code for the MIH ES option is YYY. The code for the MIH CS option is ZZZ.

2.1 Domain Name List

If the 'enc' byte has a value of 0, the encoding byte is followed by a sequence of labels, encoded according to Section 3.1 of [RFC1035], quoted below:

Domain names in messages are expressed in terms of a sequence of labels. Each label is represented as a one octet length field followed by that number of octets.  Since every domain name ends with the null label of the root, a domain name is terminated by a length byte of zero. The high order two bits of every length octet must be zero, and the remaining six bits of the length field limit the label to 63 octets or less. To simplify implementations, the total length of a domain name (i.e., label octets and label length octets) is restricted to 255 octets or less.

[RFC1035] encoding was chosen to accommodate future internationalized domain name mechanisms.

The minimum length for this encoding is 3.

The option MAY contain multiple domain names, but these SHOULD refer to different NAPTR records, rather than different A records. The client MUST try the records in the order listed, applying the mechanism described in [8] for each. The client only resolves the subsequent domain names if attempts to contact the first one failed or yielded no common transport protocols between the MN and the server.

Use of multiple domain names is not meant to replace NAPTR and SRV records, but rather to allow a single DHCP server to indicate MIH servers operated by multiple providers.

Clients MUST support compression according to the encoding in Section 4.1.4 of "Domain Names - Implementation And Specification" [RFC1035].

Since the domain names are supposed to be different domains, compression will likely have little effect, however.

If the length of the domain list exceeds the maximum permissible within a single option (254 octets), then the domain list MUST be represented in the DHCP message as specified in [7].

The DHCP option for this encoding has the following format:

Code  Len   enc   DNS name of MoS server

+-----+-----+-----+-----+-----+-----+-----+-----+--

| XXX |  n  |  0  |  s1 |  s2 |  s3 |  s4 | s5  |  ...

+-----+-----+-----+-----+-----+-----+-----+-----+--

As an example, consider the case where the server wants to offer two MIH IS servers, "example.com" and "example.net".  These would be encoded as follows:

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+

|XXX|27 | 0 | 7 |'e'|'x'|'a'|'m'|'p'|'l'|'e'| 3 |'c'|'o'|'m'| 0 |

+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+

+---+---+---+---+---+---+---+---+---+---+---+---+---+

| 7 |'e'|'x'|'a'|'m'|'p'|'l'|'e'| 3 |'n'|'e'|'t'| 0 |

+---+---+---+---+---+---+---+---+---+---+---+---+---+

2.2 IPv4 Address List

If the 'enc' byte has a value of 1, the encoding byte is followed by a list of IPv4 addresses indicating appropriate MIH servers available to the MN. Servers MUST be listed in order of preference.

Its minimum length is 5, and the length MUST be a multiple of 4 plus one. The DHCP option for this encoding has the following format:

Code   Len   enc  IPv4 Address 1          IPv4 Address 2

+-----+-----+-----+-----+-----+-----+-----+-----+--

| XXX |  n  |  1  | a1  | a2  | a3  | a4  | a1  |  ...

+-----+-----+-----+-----+-----+-----+-----+-----+--

3. DHCPv6 Options for MoS discovery

This section introduces new DHCPv6 options used for MoS discovery.

The MN can not specify the network (local or home) where it wants the MoS address from. Whether the MN receives an MoS address from local or home network will depend on the actual network deployment:

a) In a split scenario, where the network access authentication is independent of the home network authentication, the MN will discover the MoS in the local (visited) network.

b) In an integrated scenario, where the network access authentication is performed by the home network, the address of the MoS from the home network may be sent (via AAA protocols) to the visited network during the authentication procedure and provisioned to the MN.

The DHCPv6 options defined in this section together with the procedures defined in section 4 can support both scenarios.

3.1 MoS Identifier Option

This option is included in the Information-request message and used to request a specific MoS-type address from a DHCP server.

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|       OPTION IPv6-MoS         |           option-len          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|   MoS-type    |                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

option-code

OPTION_IPv6-MoS (TBD)

option-len

2 + length of the Home Network Identifier field

MoS-Type

The type of Mobility Services the MN is looking for,

i.e. IS, ES or CS or a combination of these:

1    IS service

2    ES service

3    both IS and ES services

4    CS service

5    IS and CS services

6    ES and CS services

7    IS, ES and CS services

3.2 IPv6 Relay Agent MoS Option

This option carries the home network information which was transferred to the NAS from AAAH by using [I-D.ietf-mip6-radius-MoS, TBD]. The DHCP relay agent sends this option to the DHCP server in the Relay-forward Message.

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     OPTION_IPv6-MoS-RELAY     |           option-len          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

.                             sub-options                       .

.                                                               .

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

option-code

OPTION_IPv6-MoS-RELAY (TBD).

option-len

The length of sub-options

sub-options

A series of IPv6 Relay Agent sub-options.

3.2.1. IPv6 Relay Agent Sub-option

This sub-option carries the MoS information to the DHCP server.

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|          sub-opt-code         |        sub-opt-len            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|   MoS Type    |                                               |

+-+-+-+-+-+-+-+-+        MoS Information                        .

.                                                               .

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

sub-opt-code

A 16-bit unsigned integer for the type of the following

MoS Information field. Possible values are:

1    MoS IP address list

2    MoS FQDN list

sub-opt-len

1 + The length of MoS Information field.

MoS type

The type of MoS services the server supports. Valid

values:

1    IS service

2    ES service

3    both IS and ES services

4    CS service

5    IS and CS services

6    ES and CS services

7    IS, ES and CS services

MoS Information

An MoS IP address or MoS FQDN to be provided to a mobile node according to the sub-opt-code.

When the sub-opt-code is set to 1, the MoS Information field MUST contain the 128-bit IPv6 address of the MoS.

When the sub-opt-code is set to 2, the MoS Information field MUST contain the FQDN of the MoS as described in Section 8 of [RFC3315].

Multiple sub-options may exist in a IPv6 Relay Agent option to carry more than one MoS Information (IPv6 address or FQDN).

3.3 MoS Information Option

This option is included in the Reply message and used to carry MoS information to the mobile node in the form of one or more of MoS IP address(es) or MoS FQDN(s).

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|      OPTION_IPv6-MoSINF       |           option-len          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

.                          sub-options                          .

.                                                               .

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

option-code

OPTION_IPv6-MoSINF (TBD).

option-len

length of sub-options

sub-options

A series of MoS  Information sub-options.

3.3.1 MoS Information Sub-option

This sub-option carries the assigned MoS information to the DHCP client.

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|          sub-opt-code         |          sub-opt-len          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|   MoS Type    |                                               |

+-+-+-+-+-+-+-+-+                                               +

.                     MoS Information                           .

.                                                               .

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

sub-opt-code

A 16-bit unsigned integer for the type of the following

MoS Information field. Possible values are:

1    MoS IP address

2    MoS FQDN

sub-opt-len

2 + length of MoS Information field.

MoS type

An 8 bit integer specifying the type of MoS services the

server supports. Valid values are:

0    NULL

1    IS service

2    ES service

3    both IS and ES services

4    CS services

5    IS and CS services

6    ES and CS services

7    IS, ES and CS services

MoS Information

An MoS IP address or MoS FQDN to be provided to a mobile

node according to the sub-opt-code.

The sub-opt-code, sub-opt-len and MoS Information fields are set in the same manner as those of an IPv6 Relay Agent sub-option.

4. Option Usage

4.1 Usage of DHCPv4 Options for MoS Discovery

The requesting and sending of the proposed DHCPv4 options follow the rules for DHCP options in [RFC2131].

4.1.1 Mobile Node behavior

The mobile node may perform the MoS information discovery procedure either during initial association with a network or when the mobility service is required. It may also try to perform the MoS information discovery when it lacks the network information for MoS or needs to change the  MoS for some reasons, for instance, to recover from the single point of failure of the existing MoS

In order to acquire the MoS information, the mobile node MUST send a REQUEST message to a unicast server address. In this message the mobile node (DHCP client) MUST include the Option Code for the MoS Discovery option in the OPTION_code.

4.1.2 DHCP Server behavior

When the DHCP server receives the REQUEST message with the MoS Discovery option in the OPTION_code, the DHCP server MUST follow the [RFC2131] logic to construct a REPLY message with the MoS Discovery option. The reply message may contain IP address or the FQDN of the MoS Server.

In case that the server cannot find any MoS information, it MUST return the MoS Discovery option by setting the MoS Server address 0.0.0.0 with 'enc' 1.

4.2 DHCPv6 Options for MoS discovery

The requesting and sending of the proposed DHCPv6 options follow the rules for DHCP options in [RFC3315].

4.2.1 Mobile node behavior

The mobile node may perform the MoS information discovery procedure either during initial association with a network or when the mobility service is required. It may also try to perform the MoS information discovery when it lacks the network information for MoS or needs to change the  MoS for some reasons, for instance, to recover from the single point of failure of the existing MoS

In order to acquire the MoS address, the mobile node MUST send an Information-request message to the All_DHCP_Relay_Agents_and_Servers multicast address. In this message the mobile node (DHCP client) MUST include the Option Code for the MoS Discovery option in the OPTION_ORO.

4.2.2 DHCP Relay Agent behavior

Upon receiving the Information-request from the mobile node, the DHCP relay agent MUST forward the message to the DHCP server as per [RFC3315].

If the relay agent determines that the AAAV/NAS has passed MoS information for this mobile node and has available MoS information for it, the relay agent MUST include the MoS information in the MIP6 Relay Agent option, and attach this option in the Relay-forward message.

In case the relay agent does not maintain any MoS information for the requesting mobile node, it simply forwards the received message to the DHCP server according to the [RFC3315].

Upon receiving a Relay-reply message from the DHCPv6 server, the relay agent MUST follow the guidelines defined in [RFC3315]. The relay agent extracts the Reply message from the Relay Message option in the Relay-reply message and relays it to the mobile node.

4.2.3 DHCP Server behavior

When the DHCP server receives an Information-request message with MoS Identifier Option, the DHCP server MUST follow the procedures defined in [RFC3315] to construct a REPLY message with the MoS Information Option containing the MoS Information.

When the DHCP Server receives the Information-request message with the MoS Identifier option in the Relay-forward message, it looks for a MIP6 Relay Agent Option containing MoS Information. The Information-request message may not include the MIP6 Relay Agent option in case there was no MoS information available to the mobile node at the NAS / DHCP Relay Agent.

The DHCP server MUST follow the following logic to construct a Reply message with the MoS Information option, and include the Reply message in the payload of a Relay Message option of Relay-reply message:

If the DHCP server has the requested MoS information, it MUST include the information in the MoS Information option. The server can provide the matching information extracted from the MIP6 Relay Agent option or from the information preconfigured locally according to the policy.

5. Security Considerations

The security considerations in [RFC2131] apply. If an adversary manages to modify the response from a DHCP server or insert its own response, an MN could be led to contact a rogue Mobility Server, possibly one that then would provide wrong information, event or command for handover.

It is recommended to use either DHCP authentication option described in [RFC3118] where available, or rely upon link layer security. This will also protect the denial of service attacks to DHCP servers. [RFC3118] provides mechanisms for both entity authentication and message authentication.

6. IANA Considerations

This document registers the following dhcpv4 options with IANA:

IPv4-IS

IPv4-ES

IPv4-CS

This document also registers the following dhcpv6 options with IANA:

IPv6-MoSINF

IPv6-MoS

This document also registers the following dhcpv6 Relay options with IANA:

IPv6-MoS-RELAY

7. Acknowledgements

Acknowledgements to the DT members.

8. Normative References

[1] IEEE 802.21 Standard for Local and Metropolitan Area Networks: Media Independent Handover Services

[RFC2131] Droms, R., "Dynamic Host Configuration Protocol", RFC 2131, March 1997.

[RFC1035] Mockapetris, P., "Domain names - implementation and specification", STD 13, RFC 1035, November 1987.

[7] Lemon, T. and S. Cheshire, "Encoding Long DHCP Options", RFC3396, November 2002.

[RFC3118] Authentication for DHCP Messages, Droms et al, June 2001

[RFC3315] Dynamic Host Configuration Protocol for IPv6 (DHCPv6), Droms et al, July 2003

9. Informative References

[8] Bajko, G. " Locating Mobility Servers", draft-bajko-mos-dns-discovery-00.txt

10. Author's Addresses

Gabor Bajko

Nokia

gabor.bajko@nokia.com

Subir Das

Telcordia

subir@research.telcordia.com

Full Copyright Statement

Copyright (C) The IETF Trust (2007).

This document is subject to the rights, licenses and restrictions contained in BCP 78, and except as set forth therein, the authors retain all their rights.

This document and the information contained herein are provided on an "AS IS" basis and THE CONTRIBUTOR, THE ORGANIZATION HE/SHE REPRESENTS OR IS SPONSORED BY (IF ANY), THE INTERNET SOCIETY, THE IETF TRUST AND THE INTERNET ENGINEERING TASK FORCE DISCLAIM ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

Intellectual Property

The IETF takes no position regarding the validity or scope of any Intellectual Property Rights or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; nor does it represent that it has made any independent effort to identify any such rights.  Information on the procedures with respect to rights in RFC documents can be found in BCP 78 and BCP 79.

Copies of IPR disclosures made to the IETF Secretariat and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this specification can be obtained from the IETF on-line IPR repository at http://www.ietf.org/ipr.

The IETF invites any interested party to bring to its attention any copyrights, patents or patent applications, or other proprietary rights that may cover technology that may be required to implement this standard.  Please address the information to the IETF at ietf-ipr@ietf.org.

Acknowledgment

Funding for the RFC Editor function is provided by the IETF Administrative Support Activity (IASA).