MPLS Working Group                                             G. Mirsky

Internet-Draft                                                S. Ruffini

Intended status: Standards Track                                 E. Gray

Expires: August 15, 2016                                        Ericsson

J. Drake

Juniper Networks

S. Bryant

Cisco Systems

A. Vainshtein

ECI Telecom

February 12, 2016

Residence Time Measurement in MPLS network

draft-ietf-mpls-residence-time-03

Abstract

This document specifies G-ACh based Residence Time Measurement and

how it can be used by time synchronization protocols being

transported over MPLS domain.

Residence time is the variable part of propagation delay of timing

and synchronization messages and knowing what this delay is for each

message allows for a more accurate determination of the delay to be

taken into account in applying the value included in a PTP event

message.

Status of This Memo

This Internet-Draft is submitted in full conformance with the

provisions of BCP 78 and BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF).  Note that other groups may also distribute

working documents as Internet-Drafts.  The list of current Internet-

Drafts is at http://datatracker.ietf.org/drafts/current/.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

This Internet-Draft will expire on August 15, 2016.

Mirsky, et al.           Expires August 15, 2016                [Page 1]

Internet-Draft         Residence Time Measurement          February 2016

Copyright Notice

Copyright (c) 2016 IETF Trust and the persons identified as the

document authors.  All rights reserved.

This document is subject to BCP 78 and the IETF Trust's Legal

Provisions Relating to IETF Documents

(http://trustee.ietf.org/license-info) in effect on the date of

publication of this document.  Please review these documents

carefully, as they describe your rights and restrictions with respect

to this document.  Code Components extracted from this document must

include Simplified BSD License text as described in Section 4.e of

the Trust Legal Provisions and are provided without warranty as

described in the Simplified BSD License.

Table of Contents

1.  Introduction  . . . . . . . . . . . . . . . . . . . . . . . .   3

1.1.  Conventions used in this document . . . . . . . . . . . .   3

1.1.1.  Terminology . . . . . . . . . . . . . . . . . . . . .   3

1.1.2.  Requirements Language . . . . . . . . . . . . . . . .   4

2.  Residence Time Measurement  . . . . . . . . . . . . . . . . .   4

3.  G-ACh for Residence Time Measurement  . . . . . . . . . . . .   5

3.1.  PTP Packet Sub-TLV  . . . . . . . . . . . . . . . . . . .   6

4.  Control Plane Theory of Operation . . . . . . . . . . . . . .   7

4.1.  RTM Capability  . . . . . . . . . . . . . . . . . . . . .   7

4.2.  RTM Capability Sub-TLV  . . . . . . . . . . . . . . . . .   8

4.3.  RTM Capability Advertisement in OSPFv2  . . . . . . . . .   9

4.4.  RTM Capability Advertisement in OSPFv3  . . . . . . . . .   9

4.5.  RTM Capability Advertisement in IS-IS . . . . . . . . . .   9

4.6.  RSVP-TE Control Plane Operation to Support RTM  . . . . .  10

4.7.  RTM_SET Sub-object  . . . . . . . . . . . . . . . . . . .  11

4.7.1.  RSSO Sub-TLVs . . . . . . . . . . . . . . . . . . . .  12

5.  Data Plane Theory of Operation  . . . . . . . . . . . . . . .  15

6.  Applicable PTP Scenarios  . . . . . . . . . . . . . . . . . .  15

7.  One-step Clock and Two-step Clock Modes . . . . . . . . . . .  16

8.  IANA Considerations . . . . . . . . . . . . . . . . . . . . .  18

8.1.  New RTM G-ACh . . . . . . . . . . . . . . . . . . . . . .  18

8.2.  New RTM TLV Registry  . . . . . . . . . . . . . . . . . .  18

8.3.  New RTM Sub-TLV Registry  . . . . . . . . . . . . . . . .  19

8.4.  RTM Capability sub-TLV in OSPFv2  . . . . . . . . . . . .  19

8.5.  RTM Capability sub-TLV in OSPFv3  . . . . . . . . . . . .  20

8.6.  IS-IS RTM Application ID  . . . . . . . . . . . . . . . .  20

8.7.  RTM_SET Sub-object RSVP Type and sub-TLVs . . . . . . . .  20

9.  Security Considerations . . . . . . . . . . . . . . . . . . .  21

10. Acknowledgements  . . . . . . . . . . . . . . . . . . . . . .  22

11. References  . . . . . . . . . . . . . . . . . . . . . . . . .  22

11.1.  Normative References . . . . . . . . . . . . . . . . . .  22

Mirsky, et al.           Expires August 15, 2016                [Page 2]

Internet-Draft         Residence Time Measurement          February 2016

11.2.  Informative References . . . . . . . . . . . . . . . . .  23

Authors' Addresses  . . . . . . . . . . . . . . . . . . . . . . .  24

1.  Introduction

Time synchronization protocols, Network Time Protocol version 4

(NTPv4) [RFC5905] and Precision Time Protocol (PTP) Version 2

[IEEE.1588.2008] can be used to synchronize clocks across network

domain.  Measurement of the time a PTP event message spends

traversing a node (using precise times of receipt at an ingress

interface and transmission at an egress interface), called Residence

Time, is one of on-path support types defined in [IEEE.1588.2008] and

can be used to improve the accuracy of clock synchronization.  This

document defines new Generalized Associated Channel (G-ACh) that can

be used in Multi-Protocol Label Switching (MPLS) network to measure

Residence Time over Label Switched Path (LSP).  Mechanisms for

transport of time synchronization protocol packets over MPLS are out

of scope in this document.

Though it is possible to use RTM over LSPs instantiated using LDP

such scenarios are outside the scope of this document.  The scope of

this document is on Traffic Engineered LSPs because the LSP's path

can be either explicitly specified or, at the minimum, can be

determined when signaling.  Such LSP can be instantiated either by

using RSVP-TE [RFC3209] or Path Computation Element [RFC4655].  The

PCE-based scenario is for further study and is outside the scope of

this document.

[I-D.ietf-tictoc-1588overmpls] describes alternative method of on-

path support for timing distribution protocols.  Comparison of

proposed solutions is outside the scope of this document.

1.1.  Conventions used in this document

1.1.1.  Terminology

MPLS: Multi-Protocol Label Switching

ACH: Associated Channel

TTL: Time-to-Live

G-ACh: Generic Associated Channel

GAL: Generic Associated Channel Label

NTP: Network Time Protocol

Mirsky, et al.           Expires August 15, 2016                [Page 3]

Internet-Draft         Residence Time Measurement          February 2016

ppm: parts per million

PTP: Precision Time Protocol

LSP: Label Switched Path

LSR: Label Switching Router

OAM: Operations, Administration, and Maintenance

RRO: Record Route Object

RSSO: RTM Set Sub-object

RTM: Residence Time Measurement

IGP: Internal Gateway Protocol

1.1.2.  Requirements Language

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT",

"SHOULD", "SHOULD NOT", "RECOMMENDED", "NOT RECOMMENDED", "MAY", and

"OPTIONAL" in this document are to be interpreted as described in

[RFC2119].

2.  Residence Time Measurement

Packet Loss and Delay Measurement for MPLS Networks [RFC6374] can be

used to measure one-way or two-way end-to-end propagation delay over

LSP or PW.  But these metrics are insufficient for use in some

applications, for example, time synchronization across a network as

defined in the Precision Time Protocol (PTP).  PTPv2 [IEEE.1588.2008]

uses "residence time", the time it takes for a PTPv2 event packet to

transit a node.  Residence times are accumulated in the

correctionField of the PTP event messages, as defined in

[IEEE.1588.2008], or of the associated follow-up messages (or

Delay_Resp message associated with the Delay_Req message) in case of

two-step clocks (detailed discussion in Section 7).  The residence

time values are specific to each output PTP port and message.

IEEE 1588 uses this residence time to correct the propagated time,

effectively making these nodes transparent.

This document proposes mechanism to accumulate packet residence time

from all LSRs that support the mechanism across a particular LSP.

The values accumulated in scratchpad fields of MPLS RTM messages can

be used by the last RTM-capable LSR on an LSP to update the

Mirsky, et al.           Expires August 15, 2016                [Page 4]

Internet-Draft         Residence Time Measurement          February 2016

correctionField of the corresponding PTP event packet prior to

performing the usual PTP processing.

3.  G-ACh for Residence Time Measurement

RFC 5586 [RFC5586] and RFC 6423 [RFC6423] extended applicability of

PW Associated Channel (ACH) [RFC5085] to LSPs.  G-ACh provides a

mechanism to transport OAM and other control messages.  Processing by

arbitrary transit LSRs can be triggered through controlled use of the

Time-to-Live (TTL) value.  In a way that is analogous to PTP

operations, the packet residence time can be handled by the RTM

capable node either as "one-step clock" or as a "two-step clock".

The packet format for Residence Time Measurement (RTM) is presented

in Figure 1

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0 0 0 1|Version|   Reserved    |          RTM Channel          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

|                     Scratch Pad                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|            Type               |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                             Value                             |

~                                                               ~

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 1: RTM G-ACh packet format for Residence Time Measurement

o  First four octets are defined as G-ACh Header in [RFC5586]

o  The Version field is set to 0, as defined in RFC 4385 [RFC4385].

o  The Reserved field MUST be set to 0 on transmit and ignored on

receipt.

o  The RTM G-ACh field, value (TBA1) to be allocated by IANA,

identifies the packet as such.

o  The Scratch Pad field is 8 octets in length.  The first RTM-

capable LSR MUST initialize the Scratch Pad field, it SHOULD set

it to zero value.  The Scratch Pad is used to accumulate the

residence time spent in each RTM capable LSR transited by the

packet on its path from ingress LSR to egress LSR.  Its format is

Mirsky, et al.           Expires August 15, 2016                [Page 5]

Internet-Draft         Residence Time Measurement          February 2016

IEEE double precision and its units are nanoseconds.  Note:

depending on one-step or two-step operation (Section 7), the

residence time might be related to the same packet carried in the

Value field or to a packet carried in a different RTM packet.

o  The Type field identifies the type of Value that the TLV carries.

IANA will be asked to create a sub-registry in Generic Associated

Channel (G-ACh) Parameters Registry called "MPLS RTM TLV

Registry".

o  The Length field contains the number of octets of the Value field.

o  The optional Value field may be used to carry a packet of a given

time synchronization protocol.  If packet data is carried in the

RTM message, then this is identified by Type accordingly.  The

data MAY be NTP [RFC5905] or PTP [IEEE.1588.2008].  It is

important to note that the packet may be authenticated or

encrypted and carried over MPLS LSP edge to edge unchanged while

residence time being accumulated in the Scratch Pad field.  Sub-

TLVs MAY be included in the Value field.

o  The TLV MUST be included in the RTM message, even if the length of

the Value field is zero.

3.1.  PTP Packet Sub-TLV

Figure 2 presents format of a PTP sub-TLV that MUST be precede every

PTP packet carried in RTM TLV.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|             Type              |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                         Flags                         |PTPType|

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                            Port ID                            |

|                                                               |

|                               +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                               |           Sequence ID         |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 2: PTP Sub-TLV format

where Flags field has format

Mirsky, et al.           Expires August 15, 2016                [Page 6]

Internet-Draft         Residence Time Measurement          February 2016

0                   1                   2

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|S|                      Reserved                       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 3: Flags field format of PTP Packet Sub-TLV

o  The Type field identifies PTP sub-TLV defined in the Table 19

Values of messageType field in [IEEE.1588.2008].

o  The Length field of the PTP sub-TLV contains the number of octets

of the Value field and MUST be 20.

o  The Flags field currently defines one bit, the S-bit, that defines

whether or not the current message has been processed by a 2-step

node, where the flag is cleared if the message has been handled

exclusively by 1-step nodes and there is no follow-up message, and

set if there has been at least one 2-step node and a follow-up

message is forthcoming.

o  The PTPType indicates the type of PTP packet carried in the TLV.

PTPType is the messageType field of the PTPv2 packet whose values

are defined in the Table 19 [IEEE.1588.2008].

o  The 10 octets long Port ID field contains the identity of the

source port.

o  The Sequence ID is the sequence ID of the PTP message carried in

the Value field of the message.

4.  Control Plane Theory of Operation

The operation of RTM depends upon TTL expiry to deliver an RTM packet

from one RTM capable interface to the next along the path from

ingress LSR to egress LSR.  This means that an LSR with RTM capable

interfaces MUST be able to compute a TTL which will cause the expiry

of an RTM packet at the next LSR with RTM capable interfaces.

4.1.  RTM Capability

Note that RTM capability of a node is with respect to the pair of

interfaces that will be used to forward an RTM packet.  In general,

the ingress interface of this pair must be able to capture the

arrival time of the packet and encode it in some way such that this

information will be available to the egress interface.

Mirsky, et al.           Expires August 15, 2016                [Page 7]

Internet-Draft         Residence Time Measurement          February 2016

The supported modes (1-step verses 2-step) of any pair of interfaces

is then determined by the capability of the egress interface.  In

both cases, the egress interface implementation MUST be able to

determine the precise departure time of the same packet and determine

from this, and the arrival time information from the corresponding

ingress interface, the difference representing the residence time for

the packet.

An interface with the ability to do this and update the associated

ScratchPad in real-time (i.e. while the packet is being forwarded) is

said to be 1-step capable.

Hence while both ingress and egress interfaces are required to

support RTM, for the pair to be RTM-capable, it is the egress

interface that determines whether or not the node is 1-step or 2-step

capable with respect to the interface-pair.

The RTM capability used in the sub-TLV shown in Figure 4 is thus

associated with the egress port of the node making the advertisement,

while the ability of any pair of interfaces that includes this egress

interface to support any mode of RTM depends on the ability of that

interface to record packet arrival time in some way that can be

conveyed to and used by that egress interface.

When an LSR uses an IGP to carry the RTM capability sub-TLV, the sub-

TLV MUST reflect the RTM capability (1-step or 2-step) associated

with egress interfaces and MUST NOT propagate this sub-TLV in IGP

LSAs sent from a router which describe a particular interface that

does not support the same capability for RTM messages it receives.

4.2.  RTM Capability Sub-TLV

The format for the RTM Capabilities sub-TLV is presented in Figure 4

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|              Type             |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

| RTM |                       Reserved                          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 4: RTM Capability sub-TLV

o  Type values TBA2 and TBA3 will be assigned by IANA from

appropriate registries for OSPFv2 and OSPFv3 respectively.

o  Length MUST be set to 4.

Mirsky, et al.           Expires August 15, 2016                [Page 8]

Internet-Draft         Residence Time Measurement          February 2016

o  RTM (capability) - is a three-bit long bit-map field with values

defined as follows:

*  0b001 - one-step RTM supported;

*  0b010 - two-step RTM supported;

*  0b100 - reserved.

o  Reserved field must be set to all zeroes on transmit and ignored

on receipt.

[RFC4202] explains that the Interface Switching Capability Descriptor

describes switching capability of an interface.  For bi-directional

links, the switching capabilities of an interface are defined to be

the same in either direction.  I.e., for data entering the node

through that interface and for data leaving the node through that

interface".  That principle SHOULD be applied when a node advertises

RTM Capability.

A node that supports RTM MUST be able to act in two-step mode and MAY

also support one-step RTM mode.  Detailed discussion of one-step and

two-step RTM modes in Section 7.

4.3.  RTM Capability Advertisement in OSPFv2

The capability to support RTM on a particular link advertised in the

OSPFv2 Extended Link Opaque LSA described in Section 3 [RFC7684] as

RTM Capability sub-TLV, presented in Figure 4, of the OSPFv2 Extended

Link TLV.

Type value will be assigned by IANA from the OSPF Extended Link TLV

Sub-TLVs registry that will be created per [RFC7684] request.

4.4.  RTM Capability Advertisement in OSPFv3

The capability to support RTM on a particular link in OSPFv3 can be

advertised by including an RTM Capability sub-TLV defined in

Section 4.3 in the following TLVs defined in

[I-D.ietf-ospf-ospfv3-lsa-extend] Intra-Area-Prefix TLV, IPv6 Link-

Local Address TLV, or IPv4 Link-Local Address TLV when these are

included in E-Link-LSA.

4.5.  RTM Capability Advertisement in IS-IS

The RTM capability logically belongs to a group of parameters

characterized as "generic information not directly related to the

operation of the IS-IS protocol" [RFC6823].  Hence the capability to

Mirsky, et al.           Expires August 15, 2016                [Page 9]

Internet-Draft         Residence Time Measurement          February 2016

process RTM messages can be advertised by including RTM Capability

sub-TLV in GENINFO TLV [RFC6823].

With respect to the Flags field of the GENINFO TLV:

o  The S bit MUST be cleared to prevent the RTM Capability sub-TLV

from leaking between levels.

o  The D bit of the Flags field MUST be cleared as required by

[RFC6823].

o  The I bit and the V bit MUST be set accordingly depending on

whether RTM capability being advertised for IPv4 or IPv6 interface

of the node.

Application ID (TBA4) will be assigned from the Application

Identifiers for TLV 251 IANA registry.  The RTM Capability sub-TLV,

presented in Figure 4, MUST be included in GENINFO TLV in Application

Specific Information.

4.6.  RSVP-TE Control Plane Operation to Support RTM

Throughout this document we refer to an LSR as RTM capable LSR when

at least one of its interfaces is RTM capable.  Figure 5 provides an

example of relationship between roles a network element may have in

PTP over MPLS scenario and RTM capability:

-----     -----     -----     -----     -----     -----     -----

| A |-----| B |-----| C |-----| D |-----| E |-----| F |-----| G |

-----     -----     -----     -----     -----     -----     -----

Figure 5: RTM capable roles

o  A is a Boundary Clock with its egress port in Master state.  Node

A transmits PTP messages;

o  B is the ingress LER for the MPLS LSP and is not RTM capable;

o  C is the first RTM capable LSR; it initializes the RTM Scratch Pad

field and encapsulates PTP messages in the RTM ACH; the

transmitted Scratch Pad information includes the residence time

measured by C;

o  D is a transit LSR that is not RTM capable; it passes along the

RTM ACH encapsulated PTP message unmodified;

Mirsky, et al.           Expires August 15, 2016               [Page 10]

Internet-Draft         Residence Time Measurement          February 2016

o  E is the last RTM capable LSR; it updates the Correction field of

the PTP message with the value in the Scratch Pad field of the RTM

ACH, and removes the RTM ACH encapsulation;

o  F is the egress LER for the MPLS LSP and is not RTM capable;

o  G is a Boundary Clock with its ingress port in Slave state.  Node

G receives PTP messages.

An ingress LSR that is configured to perform RTM along a path through

an MPLS network to an egress LSR verifies that the selected egress

LSR has an interface that supports RTM via the egress LSR's

advertisement of the RTM Capability sub-TLV.  In the Path message

that the ingress LSR uses to instantiate the LSP to that egress LSR

it places initialized Record Route Object (RRO) [RFC3209] and

LSP_ATTRIBUTES Object [RFC5420] with RTM Set Sub-object (RSSO)

[Section 4.7], which indicates to the egress LSR that RTM is

requested for this LSP.  RSSO SHOULD NOT be included into the

LSP_REQUIRED_ATTRIBUTES object [RFC5420] , unless it is known that

all LSRs support RSSO, because then LSR that does not recognize RSSO

would reject the Path message.

In the Resv message that the egress LSR sends in response to the

received Path message, it includes initialized RRO and RSSO.  The

RSSO contains an ordered list, from egress LSR to ingress LSR, of the

RTM capable LSRs along the LSP's path.  Each such LSR will use the ID

of the first LSR in the RSSO in conjunction with the RRO to compute

the hop count to its downstream LSR with reachable RTM capable

interface.  It will also insert its ID at the beginning of the RSSO

before forwarding the Resv message upstream.

After the ingress LSR receives the Resv, it MAY begin sending RTM

packets to the first RTM capable LSR on the LSP's path.  Each RTM

packet has its Scratch Pad field initialized and its TTL set to

expire on that first subsequent RTM capable LSR.

It should be noted that RTM can also be used for LSPs instantiated

using [RFC3209] in an environment in which all interfaces in an IGP

support RTM.  In this case the RSSO and LSP_ATTRIBUTES Object MAY be

omitted.

4.7.  RTM_SET Sub-object

RTM capable interfaces can be recorded via RTM_SET sub-object (RSSO).

The RTM_SET sub-object format is of generic Type, Length, Value

(TLV), presented in Figure 6

Mirsky, et al.           Expires August 15, 2016               [Page 11]

Internet-Draft         Residence Time Measurement          February 2016

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|      Type     |     Length    |          Reserved           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

~                             Value                           ~

|                                                             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 6: RTM Set Sub-object format

Type value (TBA5) will be assigned by IANA from its Attributes TLV

Space sub-registry.

The Length contains the total length of the sub-object in bytes,

including the Type and Length fields.

Reserved field must be zeroed on transmit and ignored on receipt.

The content of an RSSO is a series of variable-length sub-TLVs.  The

sub-TLVs are defined in Section 4.7.1 below.

The RSSO can be present in both RSVP Path and Resv messages.  If a

Path message contains multiple RSSOs, only the first RSSO is

meaningful.  Subsequent RSSOs SHOULD be ignored and SHOULD NOT be

propagated.  Similarly, if in a Resv message multiple RSSOs are

encountered following a FILTER_SPEC before another FILTER_SPEC is

encountered, only the first RSSO is meaningful.  Subsequent RSSOs

SHOULD be ignored and SHOULD NOT be propagated.

4.7.1.  RSSO Sub-TLVs

The RTM Set sub-object contains an ordered list, from egress LSR to

ingress LSR, of the RTM capable LSRs along the LSP's path.

The contents of a RTM_SET sub-object are a series of variable-length

sub-TLVs.  Each sub-TLV has its own Length field.  The Length

contains the total length of the sub-TLV in bytes, including the Type

and Length fields.  The Length MUST always be a multiple of 4, and at

least 8 (smallest IPv4 sub-object).

Sub-TLVs are organized as a last-in-first-out stack.  The first -out

sub-TLV relative to the beginning of RSSO is considered the top.  The

last-out sub-TLV is considered the bottom.  When a new sub-TLV is

added, it is always added to the top.

Three kinds of sub-TLVs for RSSO are currently defined.

Mirsky, et al.           Expires August 15, 2016               [Page 12]

Internet-Draft         Residence Time Measurement          February 2016

4.7.1.1.  IPv4 Sub-TLV

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|    Type     |     Length    |             Flags             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                       IPv4 address                          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 7: IPv4 sub-TLV format

Type

0x01 IPv4 address

Length

The Length contains the total length of the sub-TLV in bytes,

including the Type and Length fields.  The Length is always 8.

IPv4 address

A 32-bit unicast host address.

Flags

TBD

4.7.1.2.  IPv6 Sub-TLV

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|    Type     |     Length    |             Flags             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                             |

|                         IPv6 address                        |

|                                                             |

|                                                             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 8: IPv6 sub-TLV format

Type

0x02 IPv6 address

Mirsky, et al.           Expires August 15, 2016               [Page 13]

Internet-Draft         Residence Time Measurement          February 2016

Length

The Length contains the total length of the sub-TLV in bytes,

including the Type and Length fields.  The Length is always 20.

IPv6 address

A 128-bit unicast host address.

Flags

TBD

4.7.1.3.  Unnumbered Interface Sub-TLV

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|    Type     |     Length    |             Flags             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                         Router ID                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                       Interface ID                          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 9: IPv4 sub-TLV format

Type

0x03 Unnumbered interface

Length

The Length contains the total length of the sub-TLV in bytes,

including the Type and Length fields.  The Length is always 12.

Router ID

The Router ID interpreted as discussed in the Section 2 of RFC

3447 [RFC3477].

Interface ID

The identifier assigned to the link by the LSR specified by the

Router ID.

Flags

Mirsky, et al.           Expires August 15, 2016               [Page 14]

Internet-Draft         Residence Time Measurement          February 2016

TBD

5.  Data Plane Theory of Operation

After instantiating an LSP for a path using RSVP-TE [RFC3209] as

described in Section 4.6 or as described in the second paragraph of

Section 4 and in Section 4.6, ingress LSR MAY begin sending RTM

packets to the first downstream RTM capable LSR on that path.  Each

RTM packet has its Scratch Pad field initialized and its TTL set to

expire on the next downstream RTM-capable LSR.  Each RTM-capable LSR

on the explicit path receives an RTM packet and records the time at

which it receives that packet at its ingress interface as well as the

time at which it transmits that packet from its egress interface;

this should be done as close to the physical layer as possible to

ensure precise accuracy in time determination.  The RTM-capable LSR

determines the difference between those two times; for 1-step

operation, this difference is determined just prior to or while

sending the packet, and the RTM-capable egress interface adds it to

the value in the Scratch Pad field of the message in progress.  Note,

for the purpose of calculating a residence time, a common free

running clock synchronizing all the involved interfaces may be

sufficient, as, for example, 4.6 ppm accuracy leads to 4.6 nanosecond

error for residence time on the order of 1 millisecond.

For 2-step operation, the difference between packet arrival time (at

an ingress interface) and subsequent departure time (from an egress

interface) is determined at some later time prior to sending a

subsequent follow-up message, so that this value can be used to

update the correctionField in the follow-up message.

See Section 7 for further details on the difference between 1-step

and 2-step operation.

The last RTM-capable LSR on the LSP MAY then use the value in the

Scratch Pad field to perform time correction, if there is no follow-

up message.  For example, the egress LSR may be a PTP Boundary Clock

synchronized to a Master Clock and will use the value in the Scratch

Pad field to update PTP's correctionField.

6.  Applicable PTP Scenarios

The proposed approach can be directly integrated in a PTP network

based on the IEEE 1588 delay reqest-response mechanism.  The RTM

capable LSR nodes act as end-to-end transparent clocks, and typically

boundary clocks, at the edges of the MPLS network, use the value in

the Scratch Pad field to update the correctionField of the

corresponding PTP event packet prior to performing the usual PTP

processing.

Mirsky, et al.           Expires August 15, 2016               [Page 15]

Internet-Draft         Residence Time Measurement          February 2016

7.  One-step Clock and Two-step Clock Modes

One-step mode refers to the mode of operation where an egress

interface updates the correctionField value of an original event

message.  Two-step mode refers to the mode of operation where this

update is made in a subsequent follow-up message.

Processing of the follow-up message, if present, requires the

downstream end-point to wait for the arrival of the follow-up message

in order to combine correctionField values from both the original

(event) message and the subsequent (follow-up) message.  In a similar

fashion, each 2-step node needs to wait for the related follow-up

message, if there is one, in order to update that follow-up message

(as opposed to creating a new one.  Hence the first node that uses

2-step mode MUST do two things:

1.  Mark the original event message to indicate that a follow-up

message will be forthcoming (this is necessary in order to

Let any subsequent 2-step node know that there is already a

follow-up message, and

Let the end-point know to wait for a follow-up message;

2.  Create a follow-up message in which to put the RTM determined as

an initial correctionField value.

IEEE 1588v2 [IEEE.1588.2008] defines this behaviour for PTP messages.

Thus, for example, with reference to the PTP protocol, the PTPType

field identifies whether the message is a Sync message, Follow_up

message, Delay_Req message, or Delay_Resp message.  The 10 octet long

Port ID field contains the identity of the source port, that is, the

specific PTP port of the boundary clock connected to the MPLS

network.  The Sequence ID is the sequence ID of the PTP message

carried in the Value field of the message.

PTP messages also include a bit that indicates whether or not a

follow-up message will be coming.  This bit, once it is set by a

2-step mode device, MUST stay set accordingly until the original and

follow-up messages are combined by an end-point (such as a Boundary

Clock).

Thus, an RTM packet, containing residence time information relating

to an earlier packet, also contains information identifying that

earlier packet.

Mirsky, et al.           Expires August 15, 2016               [Page 16]

Internet-Draft         Residence Time Measurement          February 2016

For compatibility with PTP, RTM (when used for PTP packets) must

behave in a similar fashion.  To do this, a 2-step RTM capable egress

interface will need to examine the S-bit in the Flags field of the

PTP sub-TLV (for RTM messages that indicate they are for PTP) and -

if it is clear (set to zero), it MUST set it and create a follow-up

PTP Type RTM message.  If the S bit is already set, then the RTM

capable node MUST wait for the RTM message with the PTP type of

follow-up and matching originator and sequence number to make the

corresponding residence time update to the Scratch Pad field.

In practice an RTM operating according to two-step clock behaves like

a two-steps transparent clock.

A 1-step capable RTM node MAY elect to operate in either 1-step mode

(by making an update to the Scratch Pad field of the RTM message

containing the PTP even message), or in 2-step mode (by making an

update to the Scratch Pad of a follow-up message when its presence is

indicated), but MUST NOT do both.

Two main subcases can be identified for an RTM node operating as a

two-step clock:

A) If any of the previous RTM capable node or the previous PTP clock

(e.g. the BC connected to the first LSR), is a two-step clock, the

residence time is added to the RTM packet that has been created to

include the associated PTP packet (i.e. follow-up message in the

downstream direction), if the local RTM-capable LSR is also operating

as a two-step clock.  This RTM packet carries the related accumulated

residence time and the appropriate values of the Sequence Id and Port

Id (the same identifiers carried in the packet processed) and the

Two-step Flag set to 1.

Note that the fact that an upstream RTM-capable node operating in the

two-step mode has created a follow-up message does not require any

subsequent RTM capable LSR to also operate in the 2-step mode, as

long as that RTM-capable LSR forwards the follow-up message on the

same LSP on which it forwards the corresponding previous message.

A one-step capable RTM node MAY elect to update the RTM follow-up

message as if it were operating in two-step mode, however, it MUST

NOT update both messages.

A PTP event packet (sync) is carried in the RTM packet in order for

an RTM node to identify that residence time measurement must be

performed on that specific packet.

Mirsky, et al.           Expires August 15, 2016               [Page 17]

Internet-Draft         Residence Time Measurement          February 2016

To handle the residence time of the Delay request message on the

upstream direction, an RTM packet must be created to carry the

residence time on the associated downstream Delay Resp message.

The last RTM node of the MPLS network in addition to update the

correctionField of the associated PTP packet, must also properly

handle the two-step flag of the PTP packets.

B) When the PTP network connected to the MPLS and RTM node, operates

in one-step clock mode, the associated RTM packet must be created by

the RTM node itself.  The associated RTM packet including the PTP

event packet needs now to indicate that a follow up message will be

coming.

The last RTM node of the LSP, modeif it receives an RTM message with

a PTP payload indicating a follow-up message will be forthcoming,

must generate a follow-up message and properly set the two-step flag

of the PTP packets.

8.  IANA Considerations

8.1.  New RTM G-ACh

IANA is requested to reserve a new G-ACh as follows:

+-------+----------------------------+---------------+

| Value |        Description         | Reference     |

+-------+----------------------------+---------------+

| TBA1  | Residence Time Measurement | This document |

+-------+----------------------------+---------------+

Table 1: New Residence Time Measurement

8.2.  New RTM TLV Registry

IANA is requested to create sub-registry in Generic Associated

Channel (G-ACh) Parameters Registry called "MPLS RTM TLV Registry".

All code points in the range 0 through 127 in this registry shall be

allocated according to the "IETF Review" procedure as specified in

[RFC5226] .  Remaining code points are allocated according to the

table below.  This document defines the following new values RTM TLV

type s:

Mirsky, et al.           Expires August 15, 2016               [Page 18]

Internet-Draft         Residence Time Measurement          February 2016

+-----------+-------------+-------------------------+

| Value     | Description | Reference               |

+-----------+-------------+-------------------------+

| 0         |   Reserved  | This document           |

| 1         |  No payload | This document           |

| 2         |    PTPv2    | This document           |

| 3         |     NTP     | This document           |

| 4-127     |   Reserved  | IETF Consensus          |

| 128 - 191 |   Reserved  | First Come First Served |

| 192 - 255 |   Reserved  | Private Use             |

+-----------+-------------+-------------------------+

Table 2: RTM TLV Type

8.3.  New RTM Sub-TLV Registry

IANA is requested to create sub-registry in MPLS RTM TLV Registry,

requested in Section 8.2, called "MPLS RTM Sub-TLV Registry".  All

code points in the range 0 through 127 in this registry shall be

allocated according to the "IETF Review" procedure as specified in

[RFC5226] .  Remaining code points are allocated according to the

table below.  This document defines the following new values RTM sub-

TLV types:

+-----------+-------------+-------------------------+

| Value     | Description | Reference               |

+-----------+-------------+-------------------------+

| 0         |   Reserved  | This document           |

| 1         |  PTP 2-step | This document           |

| 2-127     |   Reserved  | IETF Consensus          |

| 128 - 191 |   Reserved  | First Come First Served |

| 192 - 255 |   Reserved  | Private Use             |

+-----------+-------------+-------------------------+

Table 3: RTM Sub-TLV Type

8.4.  RTM Capability sub-TLV in OSPFv2

IANA is requested to assign a new type for RTM Capability sub-TLV

from OSPFv2 Extended Link TLV Sub-TLVs registry as follows:

+-------+----------------+---------------+

| Value |  Description   | Reference     |

+-------+----------------+---------------+

| TBA2  | RTM Capability | This document |

+-------+----------------+---------------+

Table 4: RTM Capability sub-TLV

Mirsky, et al.           Expires August 15, 2016               [Page 19]

Internet-Draft         Residence Time Measurement          February 2016

8.5.  RTM Capability sub-TLV in OSPFv3

IANA is requested to assign a new type for RTM Capability sub-TLV

from future OSPFv3 Extended-LSA Sub-TLVs registry that would be part

of OSPFv3 IANA registry as follows:

+-------+----------------+---------------+

| Value |  Description   | Reference     |

+-------+----------------+---------------+

| TBA3  | RTM Capability | This document |

+-------+----------------+---------------+

Table 5: RTM Capability sub-TLV

8.6.  IS-IS RTM Application ID

IANA is requested to assign a new Application ID for RTM from the

Application Identifiers for TLV 251 registry as follows:

+-------+-------------+---------------+

| Value | Description | Reference     |

+-------+-------------+---------------+

| TBA4  |     RTM     | This document |

+-------+-------------+---------------+

Table 6: IS-IS RTM Application ID

8.7.  RTM_SET Sub-object RSVP Type and sub-TLVs

IANA is requested to assign a new Type for RTM_SET sub-object from

Attributes TLV Space sub-registry as follows:

+-----+------------+-----------+---------------+---------+----------+

| Typ |    Name    |  Allowed  | Allowed  on   | Allowed | Referenc |

| e   |            | on  LSP_A | LSP_REQUIRED_ |  on LSP | e        |

|     |            | TTRIBUTES |   ATTRIBUTES  | Hop Att |          |

|     |            |           |               | ributes |          |

+-----+------------+-----------+---------------+---------+----------+

| TBA |  RTM_SET   |    Yes    |       No      |    No   | This     |

| 5   | sub-object |           |               |         | document |

+-----+------------+-----------+---------------+---------+----------+

Table 7: RTM_SET Sub-object Type

IANA requested to create new sub-registry for sub-TLV types of

RTM_SET sub-object as follows:

Mirsky, et al.           Expires August 15, 2016               [Page 20]

Internet-Draft         Residence Time Measurement          February 2016

+-----------+----------------------+-------------------------+

| Value     |     Description      | Reference               |

+-----------+----------------------+-------------------------+

| 0         |       Reserved       |                         |

| 1         |     IPv4 address     | This document           |

| 2         |     IPv6 address     | This document           |

| 3         | Unnumbered interface | This document           |

| 4-127     |       Reserved       | IETF Consensus          |

| 128 - 191 |       Reserved       | First Come First Served |

| 192 - 255 |       Reserved       | Private Use             |

+-----------+----------------------+-------------------------+

Table 8: RTM_SET object sub-object types

9.  Security Considerations

Routers that support Residence Time Measurement are subject to the

same security considerations as defined in [RFC5586] .

In addition - particularly as applied to use related to PTP - there

is a presumed trust model that depends on the existence of a trusted

relationship of at least all PTP-aware nodes on the path traversed by

PTP messages.  This is necessary as these nodes are expected to

correctly modify specific content of the data in PTP messages and

proper operation of the protocol depends on this ability.

As a result, the content of the PTP-related data in RTM messages that

will be modified by intermediate nodes cannot be authenticated, and

the additional information that must be accessible for proper

operation of PTP 1-step and 2-step modes MUST be accessible to

intermediate nodes (i.e. - MUST NOT be encrypted in a manner that

makes this data inaccessible).

While it is possible for a supposed compromised LSR to intercept and

modify the G-ACh content, this is an issue that exists for LSRs in

general - for any and all data that may be carried over an LSP - and

is therefore the basis for an additional presumed trust model

associated with existing LSPs and LSRs.

The ability for potentially authenticating and/or encrypting RTM and

PTP data that is not needed by intermediate RTM/PTP-capable nodes is

for further study.

Security requirements of time protocols are provided in RFC 7384

[RFC7384].

Mirsky, et al.           Expires August 15, 2016               [Page 21]

Internet-Draft         Residence Time Measurement          February 2016

10.  Acknowledgements

Authors want to thank Loa Andersson for his thorough review and

thoghtful comments.

11.  References

11.1.  Normative References

[I-D.ietf-ospf-ospfv3-lsa-extend]

Lindem, A., Mirtorabi, S., Roy, A., and F. Baker, "OSPFv3

LSA Extendibility", draft-ietf-ospf-ospfv3-lsa-extend-09

(work in progress), November 2015.

[IEEE.1588.2008]

"Standard for a Precision Clock Synchronization Protocol

for Networked Measurement and Control Systems",

IEEE Standard 1588, March 2008.

[RFC2119]  Bradner, S., "Key words for use in RFCs to Indicate

Requirement Levels", BCP 14, RFC 2119,

DOI 10.17487/RFC2119, March 1997,

<http://www.rfc-editor.org/info/rfc2119>.

[RFC3209]  Awduche, D., Berger, L., Gan, D., Li, T., Srinivasan, V.,

and G. Swallow, "RSVP-TE: Extensions to RSVP for LSP

Tunnels", RFC 3209, DOI 10.17487/RFC3209, December 2001,

<http://www.rfc-editor.org/info/rfc3209>.

[RFC3477]  Kompella, K. and Y. Rekhter, "Signalling Unnumbered Links

in Resource ReSerVation Protocol - Traffic Engineering

(RSVP-TE)", RFC 3477, DOI 10.17487/RFC3477, January 2003,

<http://www.rfc-editor.org/info/rfc3477>.

[RFC4385]  Bryant, S., Swallow, G., Martini, L., and D. McPherson,

"Pseudowire Emulation Edge-to-Edge (PWE3) Control Word for

Use over an MPLS PSN", RFC 4385, DOI 10.17487/RFC4385,

February 2006, <http://www.rfc-editor.org/info/rfc4385>.

[RFC5085]  Nadeau, T., Ed. and C. Pignataro, Ed., "Pseudowire Virtual

Circuit Connectivity Verification (VCCV): A Control

Channel for Pseudowires", RFC 5085, DOI 10.17487/RFC5085,

December 2007, <http://www.rfc-editor.org/info/rfc5085>.

Mirsky, et al.           Expires August 15, 2016               [Page 22]

Internet-Draft         Residence Time Measurement          February 2016

[RFC5420]  Farrel, A., Ed., Papadimitriou, D., Vasseur, JP., and A.

Ayyangarps, "Encoding of Attributes for MPLS LSP

Establishment Using Resource Reservation Protocol Traffic

Engineering (RSVP-TE)", RFC 5420, DOI 10.17487/RFC5420,

February 2009, <http://www.rfc-editor.org/info/rfc5420>.

[RFC5586]  Bocci, M., Ed., Vigoureux, M., Ed., and S. Bryant, Ed.,

"MPLS Generic Associated Channel", RFC 5586,

DOI 10.17487/RFC5586, June 2009,

<http://www.rfc-editor.org/info/rfc5586>.

[RFC5905]  Mills, D., Martin, J., Ed., Burbank, J., and W. Kasch,

"Network Time Protocol Version 4: Protocol and Algorithms

Specification", RFC 5905, DOI 10.17487/RFC5905, June 2010,

<http://www.rfc-editor.org/info/rfc5905>.

[RFC6423]  Li, H., Martini, L., He, J., and F. Huang, "Using the

Generic Associated Channel Label for Pseudowire in the

MPLS Transport Profile (MPLS-TP)", RFC 6423,

DOI 10.17487/RFC6423, November 2011,

<http://www.rfc-editor.org/info/rfc6423>.

[RFC6823]  Ginsberg, L., Previdi, S., and M. Shand, "Advertising

Generic Information in IS-IS", RFC 6823,

DOI 10.17487/RFC6823, December 2012,

<http://www.rfc-editor.org/info/rfc6823>.

[RFC7684]  Psenak, P., Gredler, H., Shakir, R., Henderickx, W.,

Tantsura, J., and A. Lindem, "OSPFv2 Prefix/Link Attribute

Advertisement", RFC 7684, DOI 10.17487/RFC7684, November

2015, <http://www.rfc-editor.org/info/rfc7684>.

11.2.  Informative References

[I-D.ietf-tictoc-1588overmpls]

Davari, S., Oren, A., Bhatia, M., Roberts, P., and L.

Montini, "Transporting Timing messages over MPLS

Networks", draft-ietf-tictoc-1588overmpls-07 (work in

progress), October 2015.

[RFC4202]  Kompella, K., Ed. and Y. Rekhter, Ed., "Routing Extensions

in Support of Generalized Multi-Protocol Label Switching

(GMPLS)", RFC 4202, DOI 10.17487/RFC4202, October 2005,

<http://www.rfc-editor.org/info/rfc4202>.

Mirsky, et al.           Expires August 15, 2016               [Page 23]

Internet-Draft         Residence Time Measurement          February 2016

[RFC4655]  Farrel, A., Vasseur, J., and J. Ash, "A Path Computation

Element (PCE)-Based Architecture", RFC 4655,

DOI 10.17487/RFC4655, August 2006,

<http://www.rfc-editor.org/info/rfc4655>.

[RFC5226]  Narten, T. and H. Alvestrand, "Guidelines for Writing an

IANA Considerations Section in RFCs", BCP 26, RFC 5226,

DOI 10.17487/RFC5226, May 2008,

<http://www.rfc-editor.org/info/rfc5226>.

[RFC6374]  Frost, D. and S. Bryant, "Packet Loss and Delay

Measurement for MPLS Networks", RFC 6374,

DOI 10.17487/RFC6374, September 2011,

<http://www.rfc-editor.org/info/rfc6374>.

[RFC7384]  Mizrahi, T., "Security Requirements of Time Protocols in

Packet Switched Networks", RFC 7384, DOI 10.17487/RFC7384,

October 2014, <http://www.rfc-editor.org/info/rfc7384>.

Authors' Addresses

Greg Mirsky

Ericsson

Email: gregory.mirsky@ericsson.com

Stefano Ruffini

Ericsson

Email: stefano.ruffini@ericsson.com

Eric Gray

Ericsson

Email: eric.gray@ericsson.com

John Drake

Juniper Networks

Email: jdrake@juniper.net

Mirsky, et al.           Expires August 15, 2016               [Page 24]

Internet-Draft         Residence Time Measurement          February 2016

Stewart Bryant

Cisco Systems

Email: stbryant@cisco.com

Alexander Vainshtein

ECI Telecom

Email: Alexander.Vainshtein@ecitele.com

Mirsky, et al.           Expires August 15, 2016               [Page 25]