## Slide 1: STAMP over MPLS LSP draft-mirsky-mpls-stamp
Greg Mirsky (Ericsson)
Li Zhang (Huawei Technologies)
Loa Andersson (Bronze Dragon Consulting)
IETF-124, Nov, 2025

## Slide 2: Simple Two-way Active Measurement Protocol
RFC 8762 “Simple Two-Way Active Measurement Protocol” and RFC 8972 “Simple Two-Way Active Measurement Protocol Optional Extensions” defined the baseline protocol and several extensions (e.g., Extra Padding, Direct Loss Measurement, Timestamp Source Reporting, Follow-up Telemetry).
The protocol supports measurements of packet delay, packet loss, and detection of packet duplication and re-ordering.
Actors – Session-Sender and Session-Reflector.
Mechanism – echo request, echo reply.

## Slide 3: STAMP in MPLS
Use LSP Ping to bootstrap a STAMP test session
  Communicate STAMP Session ID and Destination UDP port number – 862 is recommended; a number from the Dynamic port numbers range - optional
Use IP/UDP encapsulation:
  Destination IP address:
    From 127/8 range for IPv4
    From Dummy IPv6 range (see draft-ietf-mpls-p2mp-bfd)
  Destination UDP port number – see above
  TTL/Hop count – 255

## Slide 4
Session-Sender
Session-Reflector
MPLS
IP
STAMP
MPLS
IP
STAMP
Session-Sender
Session-Reflector
MPLS
IP
STAMP
IP
STAMP
IP
STAMP
B
Drop vs Continue forwarding based on IP
Notes: Consider a simple use case: a STAMP test packet encapsulated in the MPLS using IP/UDP. When the LSP works correctly, the Session-Reflector receives the Packet, as shown in the left diagram. Assume that the LSP is terminated on the Node B (right diagram). The control plane looks at the STAMP packet with IP/UDP headers. The STAMP packet will be dropped if the IP DA is IPv4 loopback or IPv6 Dummy range. But if the IP DA is one of the addresses associated with the Session-Reflector, the STAMP packet may be forwarded by the Node B. In other words, MPLS OAM packets may be leaked into the IP network.