MPLS Working Group                                             G. Mirsky

Internet-Draft                                               J. Tantsura

Intended status: Standards Track                                Ericsson

Expires: February 6, 2016                                  I. Varlashkin

Google

M. Chen

Huawei

August 5, 2015

Bidirectional Forwarding Detection (BFD) Directed Return Path

draft-mirsky-mpls-bfd-directed-04

Abstract

Bidirectional Forwarding Detection (BFD) is expected to monitor bi-

directional paths.  When a BFD session monitors in its forward

direction an explicitly routed path there is a need to be able to

direct egress BFD peer to use specific path as reverse direction of

the BFD session.

Status of This Memo

This Internet-Draft is submitted in full conformance with the

provisions of BCP 78 and BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF).  Note that other groups may also distribute

working documents as Internet-Drafts.  The list of current Internet-

Drafts is at http://datatracker.ietf.org/drafts/current/.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

This Internet-Draft will expire on February 6, 2016.

Copyright Notice

Copyright (c) 2015 IETF Trust and the persons identified as the

document authors.  All rights reserved.

This document is subject to BCP 78 and the IETF Trust's Legal

Provisions Relating to IETF Documents

(http://trustee.ietf.org/license-info) in effect on the date of

publication of this document.  Please review these documents

carefully, as they describe your rights and restrictions with respect

Mirsky, et al.          Expires February 6, 2016                [Page 1]

Internet-Draft          BFD Directed Return Path             August 2015

to this document.  Code Components extracted from this document must

include Simplified BSD License text as described in Section 4.e of

the Trust Legal Provisions and are provided without warranty as

described in the Simplified BSD License.

Table of Contents

1.  Introduction  . . . . . . . . . . . . . . . . . . . . . . . .   2

1.1.  Conventions used in this document . . . . . . . . . . . .   3

1.1.1.  Terminology . . . . . . . . . . . . . . . . . . . . .   3

1.1.2.  Requirements Language . . . . . . . . . . . . . . . .   3

2.  Problem Statement . . . . . . . . . . . . . . . . . . . . . .   3

3.  Direct Reverse BFD Path . . . . . . . . . . . . . . . . . . .   4

3.1.  Case of MPLS Data Plane . . . . . . . . . . . . . . . . .   4

3.1.1.  BFD Reverse Path TLV  . . . . . . . . . . . . . . . .   4

3.1.2.  Static and RSVP-TE sub-TLVs . . . . . . . . . . . . .   5

3.1.3.  Segment Routing Tunnel sub-TLV  . . . . . . . . . . .   5

3.2.  Case of IPv6 Data Plane . . . . . . . . . . . . . . . . .   6

3.3.  Bootstrapping BFD session with BFD Reverse Path over

Segment Routed tunnel . . . . . . . . . . . . . . . . . .   6

3.4.  Return Codes  . . . . . . . . . . . . . . . . . . . . . .   7

4.  Use Case Scenario . . . . . . . . . . . . . . . . . . . . . .   7

5.  IANA Considerations . . . . . . . . . . . . . . . . . . . . .   8

5.1.  TLV . . . . . . . . . . . . . . . . . . . . . . . . . . .   8

5.2.  Sub-TLV . . . . . . . . . . . . . . . . . . . . . . . . .   8

5.3.  Return Codes  . . . . . . . . . . . . . . . . . . . . . .   8

6.  Security Considerations . . . . . . . . . . . . . . . . . . .   9

7.  Acknowledgements  . . . . . . . . . . . . . . . . . . . . . .   9

8.  Normative References  . . . . . . . . . . . . . . . . . . . .   9

Authors' Addresses  . . . . . . . . . . . . . . . . . . . . . . .  10

1.  Introduction

RFC 5880 [RFC5880], RFC 5881 [RFC5881], and RFC 5883 [RFC5883]

established the BFD protocol for IP networks and RFC 5884 [RFC5884]

set rules of using BFD asynchronous mode over IP/MPLS LSPs.  All

standards implicitly assume that the egress BFD peer will use the

shortest path route regardless of route being used to send BFD

control packets towards it.  As result, if the ingress BFD peer sends

its BFD control packets over explicit path that is diverging from the

best route, then reverse direction of the BFD session is likely not

to be on co-routed bi-directional path with the forward direction of

the BFD session.  And because BFD control packets are not guaranteed

to cross the same links and nodes in both directions detection of

Loss of Continuity (LoC) defect in forward direction may demonstrate

positive negatives.

Mirsky, et al.          Expires February 6, 2016                [Page 2]

Internet-Draft          BFD Directed Return Path             August 2015

This document defines the extension to LSP Ping [RFC4379], BFD

Reverse Path TLV, and proposes that it to be used to instruct the

egress BFD peer to use explicit path for its BFD control packets

associated with the particular BFD session.  The TLV will be

allocated from the TLV and sub-TLV registry defined by RFC 4379

[RFC4379].  As a special case, forward and reverse directions of the

BFD session can form bi-directional co-routed associated channel.

1.1.  Conventions used in this document

1.1.1.  Terminology

BFD: Bidirectional Forwarding Detection

MPLS: Multiprotocol Label Switching

LSP: Label Switching Path

LoC: Loss of Continuity

1.1.2.  Requirements Language

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT",

"SHOULD", "SHOULD NOT", "RECOMMENDED", "NOT RECOMMENDED", "MAY", and

"OPTIONAL" in this document are to be interpreted as described in

[RFC2119].

2.  Problem Statement

BFD is best suited to monitor bi-directional co-routed paths.  In

most cases, given stable environments, the forward and reverse

direction between two nodes is likely to be co-routed, this

fulfilling the implicit BFD requirements.  If BFD is used to monitor

unidirectional explicitly routed paths, e.g.  MPLS-TE LSPs, its

control packets in forward direction would be in-band using the

mechanism defined in [RFC5884] and [RFC5586].  But the reverse

direction of the BFD session would still follow the shortest path

route and that might lead to the following problems detecting

failures on the unidirectional explicit path:

o  failure detection on the reverse path cannot be interpreted as bi-

directional failure and thus trigger, for example, protection

switchover of the forward direction;

o  if reverse direction is in Down state, the head-end node would not

receive indication of forward direction failure from its egress

peer.

Mirsky, et al.          Expires February 6, 2016                [Page 3]

Internet-Draft          BFD Directed Return Path             August 2015

To address these challenges the egress BFD peer should be instructed

to use specific path for its control packets.

3.  Direct Reverse BFD Path

3.1.  Case of MPLS Data Plane

LSP ping, defined in [RFC4379], uses BFD Discriminator TLV [RFC5884]

to bootstrap a BFD session over an MPLS LSP.  This document defines a

new TLV, BFD Reverse Path TLV, that MUST contain a single sub-TLV

that can be used to carry information about reverse path for the

specified in BFD Discriminator TLV session.

3.1.1.  BFD Reverse Path TLV

The BFD Reverse Path TLV is an optional TLV within the LSP ping

protocol.  However, if used, the BFD Discriminator TLV MUST be

included in an Echo Request message as well.  If the BFD

Discriminator TLV is not present when the BFD Reverse Path TLV is

included, then it MUST be treated as malformed Echo Request, as

described in [RFC4379].

The BFD Reverse Path TLV carries the specified path that BFD control

packets of the BFD session referenced in the BFD Discriminator TLV

are required to follow.  The format of the BFD Reverse Path TLV is as

presented in Figure 1.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|   BFD Reverse Path TLV Type   |          Length             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                        Reverse Path                         |

~                                                             ~

|                                                             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 1: BFD Reverse Path TLV

BFD Reverse Path TLV Type is 2 octets in length and value to be

assigned by IANA.

Length is 2 octets in length and defines the length in octets of the

Reverse Path field.

Reverse Path field contains a sub-TLV.  Any Target FEC sub-TLV,

already or in the future defined, from IANA sub-registry Sub-TLVs for

TLV Types 1, 16, and 21 of MPLS LSP Ping Parameters registry MAY be

Mirsky, et al.          Expires February 6, 2016                [Page 4]

Internet-Draft          BFD Directed Return Path             August 2015

used in this field.  Only one sub-TLV MUST be included in the Reverse

Path TLV.  If more than one sub-TLVs are present in the Reverse Path

TLV, then only the first sub-TLV MUST be used and the rest MUST be

silently discarded.

If the egress LSR fails to establish the BFD session because path

specified in the Reverse Path TLV is not known, the egress MAY

establish the BFD session over IP network [RFC5884] and MAY send Echo

Reply with the Reverse Path TLV received and the return code set to

"Failed to establish the BFD session".  The specified reverse path

was not found" (TBD4) Section 3.4.  If the egress LSR cannot find

path specified in the Reverse Path TLV and does not establish BFD

session per RFC 5884, it MUST send Echo Reply with the Reverse Path

TLV received and the return code set to "Failed to establish the BFD

session.  The specified reverse path was not found".

3.1.2.  Static and RSVP-TE sub-TLVs

When explicit path on MPLS data plane set either as Static or RSVP-TE

LSP respective sub-TLVs defined in [RFC7110] identify explicit return

path.

3.1.3.  Segment Routing Tunnel sub-TLV

In addition to Static and RSVP-TE, Segment Routing with MPLS data

plane can be used to set explicit path.  In this case a new sub-TLV

is defined in this document as presented in Figure 2.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  SegRouting MPLS sub-TLV Type |          Length             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     Label Stack Element                     |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     Label Stack Element                     |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

~                                                             ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 2: Segment Routing MPLS Tunnel sub-TLV

The Segment Routing Tunnel sub-TLV Type is two octets in length, and

will be allocated by IANA.

The egress LSR MUST use the Value field as label stack for BFD

control packets for the BFD session identified by source IP address

and value in BFD Discriminator TLV.

Mirsky, et al.          Expires February 6, 2016                [Page 5]

Internet-Draft          BFD Directed Return Path             August 2015

The Segment Routing Tunnel sub-TLV MAY be used in Reply Path TLV

defined in [RFC7110]

3.2.  Case of IPv6 Data Plane

IPv6 can be data plane of choice for Segment Routed tunnels

[I-D.previdi-6man-segment-routing-header].  In such networks the BFD

Reverse Path TLV described in Section 3.1.1 can be used as well.  IP

networks, unlike IP/MPLS, do not require use of LSP ping with BFD

Discriminator TLV[RFC4379] to bootstrap BFD session.  But to specify

reverse path of a BFD session in IPv6 environment the BFD

Discriminator TLV MUST be used along with the BFD Reverse Path TLV.

The BFD Reverse Path TLV in IPv6 network MUST include sub-TLV.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  SegRouting IPv6 sub-TLV Type |          Length             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                             |

|                         IPv6 Prefix                         |

|                                                             |

|                                                             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                             |

|                         IPv6 Prefix                         |

|                                                             |

|                                                             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

~                                                             ~

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 3: Segment Routing IPv6 Tunnel sub-TLV

3.3.  Bootstrapping BFD session with BFD Reverse Path over Segment

Routed tunnel

As discussed in [I-D.kumarkini-mpls-spring-lsp-ping] introduction of

Segment Routing network domains with MPLS dataplane adds three new

sub-TLVs that may be used with Target FEC TLV.  Section 6.1 addresses

use of new sub-TLVs in Target FEC TLV in LSP ping and LSP traceroute.

For the case of LSP ping the [I-D.kumarkini-mpls-spring-lsp-ping]

states that:

"Initiator MUST include FEC(s) corresponding to the destination

segment.

Mirsky, et al.          Expires February 6, 2016                [Page 6]

Internet-Draft          BFD Directed Return Path             August 2015

Initiator, i.e. ingress LSR, MAY include FECs corresponding to some

or all of segments imposed in the label stack by the ingress LSR to

communicate the segments traversed.  "

When LSP ping is used to bootstrap BFD session this document updates

this and defines that LSP Ping MUST include the FEC corresponding to

the destination segment and SHOULD NOT include FECs corresponding to

some or all of segment imposed by the ingress LSR.  Operationally

such restriction would not cause any problem or uncertainty as LSP

ping with FECs corresponding to some or all segments or traceroute

may preceed the LSP ping that bootstraps the BFD session.

3.4.  Return Codes

This document defines the following Return Codes:

o  "Failed to establish the BFD session.  The specified reverse path

was not found", (TBD4).  When a specified reverse path is not

available at the egress LSR, an Echo Reply with the return code

set to "Failed to establish the BFD session.  The specified

reverse path was not found" MAY be sent back to the ingress LSR .

(Section 3.1.1)

4.  Use Case Scenario

In network presented in Figure 4 node A monitors two tunnels to node

H: A-B-C-D-G-H and A-B-E-F-G-H.  To bootstrap BFD session to monitor

the first tunnel, node A MUST include BFD Discriminator TLV with

Discriminator value foobar-1 and MAY include BFD Reverse Path TLV

that references H-G-D-C-B-A tunnel.  To bootstrap BFD session to

monitor the second tunnel, node A MUST include BFD Discriminator TLV

with Discriminator value foobar-2 and MAY include BFD Reverse Path

TLV that references H-G-F-E-B-A tunnel.

C---------D

|         |

A-------B         G-----H

|         |

E---------F

Figure 4: Use Case for BFD Reverse Path TLV

If an operator needs node H to monitor path to node A, e.g.

H-G-D-C-B-A tunnel, then by looking up list of known Reverse Paths it

MAY find and use existing BFD sessions.

Mirsky, et al.          Expires February 6, 2016                [Page 7]

Internet-Draft          BFD Directed Return Path             August 2015

5.  IANA Considerations

5.1.  TLV

The IANA is requested to assign a new value for BFD Reverse Path TLV

from the "Multiprotocol Label Switching Architecture (MPLS) Label

Switched Paths (LSPs) Ping Parameters - TLVs" registry, "TLVs and

sub-TLVs" sub-registry.

+----------+----------------------+---------------+

| Value    | Description          | Reference     |

+----------+----------------------+---------------+

| X (TBD1) | BFD Reverse Path TLV | This document |

+----------+----------------------+---------------+

Table 1: New BFD Reverse Type TLV

5.2.  Sub-TLV

The IANA is requested to assign two new sub-TLV types from

"Multiprotocol Label Switching Architecture (MPLS) Label Switched

Paths (LSPs) Ping Parameters - TLVs" registry, "Sub-TLVs for TLV

Types 1, 16, and 21" sub-registry.

+----------+-------------------------------------+---------------+

| Value    | Description                         | Reference     |

+----------+-------------------------------------+---------------+

| X (TBD2) | Segment Routing MPLS Tunnel sub-TLV | This document |

| X (TBD3) | Segment Routing IPv6 Tunnel sub-TLV | This document |

+----------+-------------------------------------+---------------+

Table 2: New Segment Routing Tunnel sub-TLV

5.3.  Return Codes

The IANA is requested to assign a new Return Code value from the

"Multi-Protocol Label Switching (MPLS) Label Switched Paths (LSPs)

Ping Parameters" registry, "Return Codes" sub-registry, as follows

using a Standards Action value.

Mirsky, et al.          Expires February 6, 2016                [Page 8]

Internet-Draft          BFD Directed Return Path             August 2015

+----------+----------------------------------------+---------------+

| Value    | Description                            | Reference     |

+----------+----------------------------------------+---------------+

| X (TBD4) | Failed to establish the BFD session.   | This document |

|          | The specified reverse path was not     |               |

|          | found.                                 |               |

+----------+----------------------------------------+---------------+

Table 3: New Return Code

6.  Security Considerations

Secuirity considerations discussed in [RFC5880], [RFC5884], and

[RFC4379], apply to this document.

7.  Acknowledgements

8.  Normative References

[I-D.kumarkini-mpls-spring-lsp-ping]

Kumar, N., Swallow, G., Pignataro, C., Akiya, N., Kini,

S., Gredler, H., and M. Chen, "Label Switched Path (LSP)

Ping/Trace for Segment Routing Networks Using MPLS

Dataplane", draft-kumarkini-mpls-spring-lsp-ping-03 (work

in progress), April 2015.

[I-D.previdi-6man-segment-routing-header]

Previdi, S., Filsfils, C., Field, B., Leung, I., Aries,

E., Vyncke, E., and D. Lebrun, "IPv6 Segment Routing

Header (SRH)", draft-previdi-6man-segment-routing-

header-07 (work in progress), July 2015.

[RFC2119]  Bradner, S., "Key words for use in RFCs to Indicate

Requirement Levels", BCP 14, RFC 2119,

DOI 10.17487/RFC2119, March 1997,

<http://www.rfc-editor.org/info/rfc2119>.

[RFC4379]  Kompella, K. and G. Swallow, "Detecting Multi-Protocol

Label Switched (MPLS) Data Plane Failures", RFC 4379,

DOI 10.17487/RFC4379, February 2006,

<http://www.rfc-editor.org/info/rfc4379>.

[RFC5586]  Bocci, M., Ed., Vigoureux, M., Ed., and S. Bryant, Ed.,

"MPLS Generic Associated Channel", RFC 5586,

DOI 10.17487/RFC5586, June 2009,

<http://www.rfc-editor.org/info/rfc5586>.

Mirsky, et al.          Expires February 6, 2016                [Page 9]

Internet-Draft          BFD Directed Return Path             August 2015

[RFC5880]  Katz, D. and D. Ward, "Bidirectional Forwarding Detection

(BFD)", RFC 5880, DOI 10.17487/RFC5880, June 2010,

<http://www.rfc-editor.org/info/rfc5880>.

[RFC5881]  Katz, D. and D. Ward, "Bidirectional Forwarding Detection

(BFD) for IPv4 and IPv6 (Single Hop)", RFC 5881,

DOI 10.17487/RFC5881, June 2010,

<http://www.rfc-editor.org/info/rfc5881>.

[RFC5883]  Katz, D. and D. Ward, "Bidirectional Forwarding Detection

(BFD) for Multihop Paths", RFC 5883, DOI 10.17487/RFC5883,

June 2010, <http://www.rfc-editor.org/info/rfc5883>.

[RFC5884]  Aggarwal, R., Kompella, K., Nadeau, T., and G. Swallow,

"Bidirectional Forwarding Detection (BFD) for MPLS Label

Switched Paths (LSPs)", RFC 5884, DOI 10.17487/RFC5884,

June 2010, <http://www.rfc-editor.org/info/rfc5884>.

[RFC7110]  Chen, M., Cao, W., Ning, S., Jounay, F., and S. Delord,

"Return Path Specified Label Switched Path (LSP) Ping",

RFC 7110, DOI 10.17487/RFC7110, January 2014,

<http://www.rfc-editor.org/info/rfc7110>.

Authors' Addresses

Greg Mirsky

Ericsson

Email: gregory.mirsky@ericsson.com

Jeff  Tantsura

Ericsson

Email: jeff.tantsura@ericsson.com

Ilya Varlashkin

Google

Email: Ilya@nobulus.com

Mach(Guoyi) Chen

Huawei

Email: mach.chen@huawei.com

Mirsky, et al.          Expires February 6, 2016               [Page 10]