MPLS Working Group                                         E. Bellagamba

Internet-Draft

Intended status: Standards Track                               G. Mirsky

Expires: February 22, 2016                                      Ericsson

L. Andersson

Huawei Technologies

P. Skoldstrom

Acreo AB

D. Ward

Cisco

J. Drake

Juniper

August 21, 2015

Configuration of Proactive Operations, Administration, and Maintenance

(OAM) Functions for MPLS-based Transport Networks using LSP Ping

draft-ietf-mpls-lsp-ping-mpls-tp-oam-conf-11

Abstract

This specification describes the configuration of proactive MPLS-TP

Operations, Administration, and Maintenance (OAM) Functions for a

given Label Switched Path (LSP) using a set of TLVs that are carried

by the LSP-Ping protocol.

Status of This Memo

This Internet-Draft is submitted in full conformance with the

provisions of BCP 78 and BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF).  Note that other groups may also distribute

working documents as Internet-Drafts.  The list of current Internet-

Drafts is at http://datatracker.ietf.org/drafts/current/.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

This Internet-Draft will expire on February 22, 2016.

Copyright Notice

Copyright (c) 2015 IETF Trust and the persons identified as the

document authors.  All rights reserved.

Bellagamba, et al.      Expires February 22, 2016               [Page 1]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

This document is subject to BCP 78 and the IETF Trust's Legal

Provisions Relating to IETF Documents

(http://trustee.ietf.org/license-info) in effect on the date of

publication of this document.  Please review these documents

carefully, as they describe your rights and restrictions with respect

to this document.  Code Components extracted from this document must

include Simplified BSD License text as described in Section 4.e of

the Trust Legal Provisions and are provided without warranty as

described in the Simplified BSD License.

Table of Contents

1.  Introduction  . . . . . . . . . . . . . . . . . . . . . . . .   3

1.1.  Conventions used in this document . . . . . . . . . . . .   4

1.1.1.  Terminology . . . . . . . . . . . . . . . . . . . . .   4

1.1.2.  Requirements Language . . . . . . . . . . . . . . . .   5

2.  Theory of Operations  . . . . . . . . . . . . . . . . . . . .   5

2.1.  MPLS OAM Configuration Operation Overview . . . . . . . .   5

2.1.1.  Configuration of BFD Sessions . . . . . . . . . . . .   5

2.1.2.  Configuration of Performance Monitoring . . . . . . .   6

2.1.3.  Configuration of Fault Management Signals . . . . . .   6

2.2.  MPLS OAM Functions TLV  . . . . . . . . . . . . . . . . .   7

2.2.1.  BFD Configuration Sub-TLV . . . . . . . . . . . . . .   9

2.2.2.  Local Discriminator Sub-TLV . . . . . . . . . . . . .  11

2.2.3.  Negotiation Timer Parameters Sub-TLV  . . . . . . . .  11

2.2.4.  BFD Authentication Sub-TLV  . . . . . . . . . . . . .  12

2.2.5.  Traffic Class Sub-TLV . . . . . . . . . . . . . . . .  13

2.2.6.  Performance Measurement Sub-TLV . . . . . . . . . . .  14

2.2.7.  PM Loss Measurement Sub-TLV . . . . . . . . . . . . .  16

2.2.8.  PM Delay Measurement Sub-TLV  . . . . . . . . . . . .  17

2.2.9.  Fault Management Signal Sub-TLV . . . . . . . . . . .  18

2.2.10. Source MEP-ID Sub-TLV . . . . . . . . . . . . . . . .  20

3.  Summary of MPLS OAM Configuration Errors  . . . . . . . . . .  20

4.  IANA Considerations . . . . . . . . . . . . . . . . . . . . .  22

4.1.  TLV and Sub-TLV Allocation  . . . . . . . . . . . . . . .  22

4.2.  MPLS OAM Function Flags Allocation  . . . . . . . . . . .  22

4.3.  OAM Configuration Errors  . . . . . . . . . . . . . . . .  23

5.  Acknowledgements  . . . . . . . . . . . . . . . . . . . . . .  24

6.  Security Considerations . . . . . . . . . . . . . . . . . . .  24

7.  References  . . . . . . . . . . . . . . . . . . . . . . . . .  25

7.1.  Normative References  . . . . . . . . . . . . . . . . . .  25

7.2.  Informative References  . . . . . . . . . . . . . . . . .  26

Authors' Addresses  . . . . . . . . . . . . . . . . . . . . . . .  27

Bellagamba, et al.      Expires February 22, 2016               [Page 2]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

1.  Introduction

MPLS Transport Profile (MPLS-TP) describes a profile of MPLS that

enables operational models typical in transport networks, while

providing additional Operations, Administration, and Maintenance

(OAM), survivability and other maintenance functions not currently

supported by MPLS.  860] defines the requirements for the OAM

functionality of MPLS-TP.

This document describes the configuration of proactive MPLS-TP OAM

Functions for a given Label Switched Path (LSP) using TLVs carried in

LSP Ping [RFC4379].  In particular it specifies the mechanisms

necessary to establish MPLS-TP OAM entities at the maintenance points

for monitoring and performing measurements on an LSP, as well as

defining information elements and procedures to configure proactive

MPLS-TP OAM functions running between LERs.  Initialization and

control of on-demand MPLS-TP OAM functions are expected to be carried

out by directly accessing network nodes via a management interface;

hence configuration and control of on-demand OAM functions are out-

of-scope for this document.

The Transport Profile of MPLS must, by definition [RFC5654], be

capable of operating without a control plane.  Therefore there are

several options for configuring MPLS-TP OAM, without a control plane

by either using an NMS or LSP Ping, or with a control plane using

signaling protocols RSVP Traffic engineering (RSVP-TE) [RFC3209] and/

or Targeted LDP [RFC5036].

Proactive MPLS-TP OAM is performed by set of protocols, Bi-

directional Forwarding Detection (BFD) [RFC6428] for Continuity

Check/Connectivity Verification, the delay measurement protocol (DM)

[RFC6374], [RFC6375] for delay and delay variation (jitter)

measurements, and the loss measurement (LM) protocol [RFC6374],

[RFC6375] for packet loss and throughput measurements.  Additionally,

there is a number of Fault Management Signals that can be configured

[RFC6427].

BFD is a protocol that provides low-overhead, fast detection of

failures in the path between two forwarding engines, including the

interfaces, data link(s), and, to the extent possible, the forwarding

engines themselves.  BFD can be used to detect the continuity and

mis-connection defects of MPLS-TP point-to-point and might also be

extended to support point-to-multipoint label switched paths (LSPs).

The delay and loss measurements protocols [RFC6374], [RFC6375] use a

simple query/response model for performing both uni- and bi-

directional measurements that allow the originating node to measure

packet loss and delay in forward or forward and reverse directions.

Bellagamba, et al.      Expires February 22, 2016               [Page 3]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

By timestamping and/or writing current packet counters to the

measurement packets at four times (Transmit and Receive in both

directions) current delays and packet losses can be calculated.  By

performing successive delay measurements the delay and/or inter-

packet delay variation (jitter) can be calculated.  Current

throughput can be calculated from the packet loss measurements by

dividing the number of packets sent/received with the time it took to

perform the measurement, given by the timestamp in LM header.

Combined with a packet generator the throughput measurement can be

used to measure the maximum capacity of a particular LSP.  It should

be noted that here we are not configuring on-demand throughput

estimates based on saturating the connection as defined in [RFC6371].

Rather, we only enable the estimation of the current throughput based

on loss measurements.

1.1.  Conventions used in this document

1.1.1.  Terminology

BFD - Bidirectional Forwarding Detection

DM - Delay Measurement

FMS - Fault Management Signal

G-ACh - Generic Associated Channel

LSP - Label Switched Path

LM - Loss Measurement

MEP - Maintenance Entity Group End Point

MPLS - Multi-Protocol Label Switching

MPLS-TP - MPLS Transport Profile

NMS - Network management System

PM - Performance Measurement

RSVP-TE - RSVP Traffic Engineering

TC - Traffic Class

Bellagamba, et al.      Expires February 22, 2016               [Page 4]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

1.1.2.  Requirements Language

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT",

"SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this

document are to be interpreted as described in RFC 2119 [RFC2119].

2.  Theory of Operations

2.1.  MPLS OAM Configuration Operation Overview

The MPLS-TP OAM tool set is described in the [RFC6669].

LSP Ping, or alternatively RSVP-TE [RFC7487], can be used to simply

enable the different OAM functions, by setting the corresponding

flags in the MPLS OAM Functions TLV, Section 2.2.  For a more

detailed configuration one may include sub-TLVs for the different OAM

functions in order to specify various parameters in detail.

Typically intermediate nodes simply forward OAM configuration TLVs to

the end-node without any processing or modification At least one

exception to this is if the FMS sub-TLV Section 2.2.9 is present.

This sub-TLV MUST be examined even by intermediate nodes that support

this extension.  The sub-TLV MAY be present if a flag is set in the

MPLS OAM Functions TLV.

2.1.1.  Configuration of BFD Sessions

For this specification, BFD MUST run in either one of the two modes:

- Asynchronous mode, where both sides should be in active mode

- Unidirectional mode

In the simplest scenario LSP Ping [RFC5884], or alternatively RSVP-TE

[RFC7487], is used only to bootstrap a BFD session for an LSP,

without any timer negotiation.

Timer negotiation can be performed either in subsequent BFD control

messages (in this case the operation is similar to LSP Ping based

bootstrapping described in [RFC5884]) or directly in the LSP-Ping

configuration messages.

When BFD Control packets are transported in the ACH encapsulation

they are not protected by any end-to-end checksum, only lower-layers

are providing error detection/correction.  A single bit error, e.g. a

flipped bit in the BFD State field could cause the receiving end to

wrongly conclude that the link is down and in turn trigger protection

switching.  To prevent this from happening the BFD Configuration sub-

Bellagamba, et al.      Expires February 22, 2016               [Page 5]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

TLV, Section 2.2.1, has an Integrity flag that when set enables BFD

Authentication using Keyed SHA1 with an empty key (all 0s) [RFC5880].

This would make every BFD Control packet carry an SHA1 hash of itself

that can be used to detect errors.

If BFD Authentication using a pre-shared key/password is desired

(i.e. authentication and not only error detection) the BFD

Authentication sub-TLV, Section 2.2.4, MUST be included in the BFD

Configuration sub-TLV.  The BFD Authentication sub-TLV is used to

specify which authentication method that should be used and which

pre-shared key/ password that should be used for this particular

session.  How the key exchange is performed is out of scope of this

document.

2.1.2.  Configuration of Performance Monitoring

It is possible to configure Performance Monitoring functionalities

such as Loss, Delay, Delay/Interpacket Delay variation (jitter), and

Throughput as described in [RFC6374].

When configuring Performance Monitoring functionalities it is

possible to choose either the default configuration, by only setting

the respective flags in the MPLS OAM functions TLV, or a customized

configuration.  To customize the configuration one would set the

respective flags in the MPLS OAM functions TLV and including the

respective Loss and/or Delay sub-TLVs.

By setting the PM Loss flag in the MPLS OAM Functions TLV and

including the PM Loss sub-TLV, Section 2.2.7, one can configure the

measurement interval and loss threshold values for triggering

protection.

Delay measurements are configured by setting PM Delay flag in the

MPLS OAM Functions TLV and including the PM Delay sub-TLV,

Section 2.2.8, one can configure the measurement interval and the

delay threshold values for triggering protection.

2.1.3.  Configuration of Fault Management Signals

To configure Fault Management Signals (FMS) and their refresh time

the FMS flag in the MPLS OAM Functions TLV MUST be set and the FMS

sub-TLV MUST be included.  When configuring FMS, an implementation

can enable the default configuration by setting the FMS flag in the

OAM Function Flags sub-TLV.  In order to modify the default

configuration the MPLS OAM FMS sub-TLV MUST be included.

If an intermediate point is meant to originate fault management

signal messages this means that such an intermediate point is

Bellagamba, et al.      Expires February 22, 2016               [Page 6]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

associated with a Server MEP through a co-located MPLS-TP client/

server adaptation function and the Fault Management subscription flag

in the MPLS OAM FMS sub-TLV been set as indication of the request to

create the association at each intermediate node of the client LSP.

The corresponding Server MEP needs to be configured by its own LSP-

ping session or, alternatively, via a Network Management system (NMS)

or RSVP-TE.

2.2.  MPLS OAM Functions TLV

The MPLS OAM Functions TLV presented in Figure 1 is carried as a TLV

of the MPLS Echo Request/Reply messages [RFC4379].

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  MPLS OAM Func. Type (TBA1)   |           Length              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                    MPLS OAM Function Flags                    |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

~                           sub-TLVs                            ~

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 1: MPLS OAM Functions TLV format

The MPLS OAM Functions TLV contains MPLS OAM Function Flags field.

The MPLS OAM Function Flags indicates which OAM functions should be

activated as well as OAM function specific sub-TLVs with

configuration parameters for the particular function.

Type: indicates the MPLS OAM Functions TLV Section 4.

Length: the length of the MPLS OAM Function Flags field including the

total length of the sub-TLVs in octets.

MPLS OAM Function Flags: a bitmap numbered from left to right as

shown in the Figure 2.These flags are managed by IANA Section 4.2.

Flags defined in this document are presented in Table 2.  Undefined

flags MUST be set to zero and unknown flags MUST be ignored.  The

flags indicate what OAM is being configured and direct the presence

of optional sub-TLVs as set out below.

Bellagamba, et al.      Expires February 22, 2016               [Page 7]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|C|V|F|L|D|T|             Reserved  (MBZ)                       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 2: MPLS OAM Function Flags format

Sub-TLVs corresponding to the different flags are as follows:

- If a flag in the MPLS OAM Function Flags is set and the

corresponding sub-TLVs listed below is absent, then this MPLS OAM

function MUST be initialized according to its default settings.

Default settings of MPLS OAM functions are outside the scope of

this document.

- If any sub-TLV is present without the corresponding flag being

set, the sub-TLV SHOULD be ignored.

- BFD Configuration sub-TLV, which MUST be included if either the

CC, the CV or both MPLS OAM Function flags being set in the MPLS

OAM Functions TLV .

- Performance Monitoring sub-TLV MUST be used to carry PM Loss

sub-TLV and/or PM Delay sub-TLV.  If neither one of these sub-TLVs

is present then Performance Monitoring sub-TLV SHOULD NOT be

included.  Empty, i.e. no enclosed sub-TLVs, Performance

Monitoring sub-TLV SHOULD be ignored.

- PM Loss sub-TLV MAY be included if the PM/Loss OAM Function flag

is set.  If the "PM Loss sub-TLV" is not included, default

configuration values are used.  Such sub-TLV MAY also be included

in case the Throughput function flag is set and there is the need

to specify measurement interval different from the default ones.

In fact the throughput measurement make use of the same tool as

the loss measurement, hence the same TLV is used.

- PM Delay sub-TLV MAY be included if the PM/Delay OAM Function

flag is set.  If the "PM Delay sub-TLV" is not included, default

configuration values are used.

- FMS sub-TLV, which MAY be included if the FMS OAM Function flag

is set.  If the "FMS sub-TLV" is not included, default

configuration values are used.

If all flags in the MPLS OAM Function Flags filed have the same value

of zero, that MUST be interpreted as the MPLS OAM Functions TLV not

present in the MPLS Echo Request.  If more than one MPLS OAM

Bellagamba, et al.      Expires February 22, 2016               [Page 8]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

Functions TLV is present in the MPLS Echo request packet, then the

first TLV SHOULD be processed and the rest be ignored.  Any parsing

error within nested sub-TLVs that is not specified in Section 3

SHOULD be treated as described in [RFC4379].

2.2.1.  BFD Configuration Sub-TLV

The BFD Configuration sub-TLV, depicted Figure 3, is defined for BFD

OAM specific configuration parameters.  The "BFD Configuration sub-

TLV" is carried as a sub-TLV of the "OAM Functions TLV".

This TLV accommodates generic BFD OAM information and carries sub-

TLVs.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

| BFD Conf. sub-Type    (100)   |           Length              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|Vers.|N|S|I|G|U|B|         Reserved (set to all 0s)            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

~                           sub-TLVs                            ~

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 3: BFD Configuration sub-TLV format

Sub-type: indicates a new sub-type, the BFD Configuration sub-TLV

(value 100).

Length: indicates the length of the Value field in octets.

Version: identifies the BFD protocol version.  If a node does not

support a specific BFD version an error must be generated: "OAM

Problem/Unsupported OAM Version".

BFD Negotiation (N): If set timer negotiation/re-negotiation via BFD

Control Messages is enabled, when cleared it is disabled and timer

configuration is achieved using Negotiation Timer Parameters sub-TLV

as described in Section 2.2.3.

Symmetric session (S): If set the BFD session MUST use symmetric

timing values.  If cleared the BFD session MAY use any timing values

either negotiated or explicitly configured.

Integrity (I): If set BFD Authentication MUST be enabled.  If the BFD

Configuration sub-TLV does not include a BFD Authentication sub-TLV

Bellagamba, et al.      Expires February 22, 2016               [Page 9]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

the authentication MUST use Keyed SHA1 with an empty pre-shared key

(all 0s).  If the egress LSR does not support BFD Authentication an

error MUST be generated: "OAM Problem/BFD Authentication

unsupported".  If the Integrity flag is clear, then Authentication

MUST NOT be used.

Encapsulation Capability (G): if set, it shows the capability of

encapsulating BFD messages into G-ACh channel.  If both the G bit and

U bit are set, configuration gives precedence to the G bit.

Encapsulation Capability (U): if set, it shows the capability of

encapsulating BFD messages into IP/UDP packets.  If both the G bit

and U bit are set, configuration gives precedence to the G bit.

If the egress LSR does not support any of the ingress LSR

Encapsulation Capabilities an error MUST be generated: "OAM Problem/

Unsupported BFD Encapsulation format".

Bidirectional (B): if set, it configures BFD in the Bidirectional

mode.  If it is not set it configures BFD in unidirectional mode.  In

the second case, the source node does not expect any Discriminator

values back from the destination node.

Reserved: Reserved for future specification and set to 0 on

transmission and ignored when received.

The BFD Configuration sub-TLV MUST include the following sub-TLVs in

the MPLS Echo Request message:

- Local Discriminator sub-TLV, if B flag is set in the MPLS Echo

Request;

- Negotiation Timer Parameters sub-TLV if the N flag is cleared.

The BFD Configuration sub-TLV MUST include the following sub-TLVs in

the MPLS Echo Reply message:

- Local Discriminator sub-TLV;

- Negotiation Timer Parameters sub-TLV if:

- the N and S flags are cleared, or if:

- the N flag is cleared and the S flag is set, and the

Negotiation Timer Parameters sub-TLV received by the egress

contains unsupported values.  In this case an updated

Negotiation Timer Parameters sub-TLV, containing values

Bellagamba, et al.      Expires February 22, 2016              [Page 10]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

supported by the egress node [RFC7419], is returned to the

ingress.

2.2.2.  Local Discriminator Sub-TLV

The Local Discriminator sub-TLV is carried as a sub-TLV of the "BFD

Configuration sub-TLV" and is depicted in Figure 4.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  Locl. Discr. sub-Type (101)  |            Length             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                       Local Discriminator                     |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 4: Local Discriminator sub-TLV format

Type: indicates a new type, the "Local Discriminator sub-TLV" (value

101).

Length: indicates the length of the Value field in octets . (4)

Local Discriminator: A nonzero discriminator value that is unique in

the context of the transmitting system that generates it.  It is used

to demultiplex multiple BFD sessions between the same pair of

systems.

2.2.3.  Negotiation Timer Parameters Sub-TLV

The Negotiation Timer Parameters sub-TLV is carried as a sub-TLV of

the BFD Configuration sub-TLV and is depicted in Figure 5.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

| Nego. Timer sub-type (102)    |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Acceptable Min. Asynchronous TX interval              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Acceptable Min. Asynchronous RX interval              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|               Required Echo TX Interval                       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 5: Negotiation Timer Parameters sub-TLV format

Bellagamba, et al.      Expires February 22, 2016              [Page 11]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

Sub-type: indicates a new sub-type, the Negotiation Timer Parameters

sub-TLV (value 102).

Length: indicates the length of the Value field in octets (12).

Acceptable Min. Asynchronous TX interval: in case of S (symmetric)

flag set in the BFD Configuration sub-TLV, defined in Section 2.2.1,

it expresses the desired time interval (in microseconds) at which the

ingress LER intends to both transmit and receive BFD periodic control

packets.  If the receiving edge LSR cannot support such value, it

SHOULD reply with an interval greater than the one proposed.

In case of S (symmetric) flag cleared in the BFD Configuration sub-

TLV, this field expresses the desired time interval (in microseconds)

at which a edge LSR intends to transmit BFD periodic control packets

in its transmitting direction.

Acceptable Min. Asynchronous RX interval: in case of S (symmetric)

flag set in the BFD Configuration sub-TLV, Figure 3, this field MUST

be equal to Acceptable Min. Asynchronous TX interval and has no

additional meaning respect to the one described for "Acceptable Min.

Asynchronous TX interval".

In case of S (symmetric) flag cleared in the BFD Configuration sub-

TLV, it expresses the minimum time interval (in microseconds) at

which edge LSRs can receive BFD periodic control packets.  In case

this value is greater than the value of Acceptable Min. Asynchronous

TX interval received from the other edge LSR, such edge LSR MUST

adopt the interval expressed in this Acceptable Min. Asynchronous RX

interval.

Required Echo TX Interval: the minimum interval (in microseconds)

between received BFD Echo packets that this system is capable of

supporting, less any jitter applied by the sender as described in

[RFC5880] sect. 6.8.9.  This value is also an indication for the

receiving system of the minimum interval between transmitted BFD Echo

packets.  If this value is zero, the transmitting system does not

support the receipt of BFD Echo packets.  If the receiving system

cannot support this value the "Unsupported BFD TX Echo rate interval"

error MUST be generated.  By default the value is set to 0.

2.2.4.  BFD Authentication Sub-TLV

The "BFD Authentication sub-TLV" is carried as a sub-TLV of the "BFD

Configuration sub-TLV" and is depicted in Figure 6.

Bellagamba, et al.      Expires February 22, 2016              [Page 12]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|    BFD Auth. sub-type (103)   |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|   Auth Type   |  Auth Key ID  |         Reserved (0s)         |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 6: BFD Authentication sub-TLV format

Sub-type: indicates a new type, the BFD Authentication sub-TLV (value

103).

Length: indicates the length of the Value field in octets (4).

Auth Type: indicates which type of authentication to use.  The same

values as are defined in section 4.1 of [RFC5880] are used.

Auth Key ID: indicates which authentication key or password

(depending on Auth Type) should be used.  How the key exchange is

performed is out of scope of this document.  If the egress LSR does

not support this Auth Key ID an "OAM Problem/Mismatch of BFD

Authentication Key ID" error MUST be generated.

Reserved: Reserved for future specification and set to 0 on

transmission and ignored when received.

If BFD Authentication sub-TLV used for a BFD session in Up state then

the Sender of the MPLS LSP Echo Request SHOULD ensure that old and

new modes of authentication, i.e. combination of Auth.Type and Auth.

Key ID, used to send and receive BFD control packets until the Sender

can confirm that its peer had switched to the new authentication.

2.2.5.  Traffic Class Sub-TLV

The Traffic Class sub-TLV is carried as a sub-TLV of the "BFD

Configuration sub-TLV" and "Fault Management Signal sub-TLV"

Section 2.2.9 and is depicted in Figure 7.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

| Traffic Class sub-Type (104)  |            Length             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  TC |                 Reserved (set to all 0s)                |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 7: Traffic Class sub-TLV format

Bellagamba, et al.      Expires February 22, 2016              [Page 13]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

Type: indicates a new type, the "Traffic Class sub-TLV" (value 104).

Length: indicates the length of the Value field in octets . (4)

TC: Identifies the Traffic Class (TC) [RFC5462] for periodic

continuity monitoring messages or packets with fault management

information.

If TC sub-TLV is present, then the value of the TC field MUST be used

as the value of the TC field of the MPLS label stack that corresponds

to the FEC for which fault detection is being performed.  If the TC

sub-TLV is absent from either "BFD Configuration sub-TLV" or "Fault

Management Signal sub-TLV", then selection of the TC value is local

decision.

2.2.6.  Performance Measurement Sub-TLV

If the MPLS OAM Functions TLV has any of the L (Loss), D (Delay) and

T (Throughput) flag set, the Performance Measurement sub-TLV MUST be

present.  Failure to include the correct sub-TLVs MUST result in an

"OAM Problem/ Configuration Error" error being generated.

The Performance Measurement sub-TLV provides the configuration

information mentioned in Section 7 of [RFC6374].  It includes support

for the configuration of quality thresholds and, as described in

[RFC6374], "the crossing of which will trigger warnings or alarms,

and result reporting and exception notification will be integrated

into the system-wide network management and reporting framework."

In case the values need to be different than the default ones the

Performance Measurement sub-TLV MAY include the following sub-TLVs:

- PM Loss sub-TLV if the L flag is set in the MPLS OAM Functions

TLV;

- PM Delay sub-TLV if the D flag is set in the MPLS OAM Functions

TLV.

The Performance Measurement sub-TLV depicted in Figure 8 is carried

as a sub-TLV of the MPLS OAM Functions TLV.

Bellagamba, et al.      Expires February 22, 2016              [Page 14]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

| Perf Monitoring Type (200)    |          Length               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     PM Configuration Flags                    |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

~                           sub-TLVs                            ~

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 8: Performance Measurement sub-TLV format

Sub-type: indicates a new sub-type, the Performance Management sub-

TLV" (value 200).

Length: indicates the length of the Value field in octets, including

PM Configuration Flags and optional sub-TLVs.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|D|L|J|Y|K|C|            Reserved (set to all 0s)               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 9: Performance Measurement sub-TLV format

PM Configuration Flags, format is presented in Figure 9, for the

specific function description please refer to [RFC6374]:

- D: Delay inferred/direct (0=INFERRED, 1=DIRECT).  If the egress

LSR does not support specified mode an "OAM Problem/Unsupported

Delay Mode" error MUST be generated.

- L: Loss inferred/direct (0=INFERRED, 1=DIRECT).  If the egress

LSR does not support specified mode an "OAM Problem/Unsupported

Loss Mode" error MUST be generated.

- J: Delay variation/jitter (1=ACTIVE, 0=NOT ACTIVE).  If the

egress LSR does not support Delay variation measurements and the J

flag is set, an "OAM Problem/Delay variation unsupported" error

MUST be generated.

- Y: Dyadic (1=ACTIVE, 0=NOT ACTIVE).  If the egress LSR does not

support Dyadic mode and the Y flag is set, an "OAM Problem/Dyadic

mode unsupported" error MUST be generated.

Bellagamba, et al.      Expires February 22, 2016              [Page 15]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

- K: Loopback (1=ACTIVE, 0=NOT ACTIVE).  If the egress LSR does

not support Loopback mode and the K flag is set, an "OAM Problem/

Loopback mode unsupported" error MUST be generated.

- C: Combined (1=ACTIVE, 0=NOT ACTIVE).  If the egress LSR does

not support Combined mode and the C flag is set, an "OAM Problem/

Combined mode unsupported" error MUST be generated.

Reserved: Reserved for future specification and set to 0 on

transmission and ignored when received.

2.2.7.  PM Loss Measurement Sub-TLV

The PM Loss Measurement sub-TLV depicted in Figure 10 is carried as a

sub-TLV of the Performance Measurement sub-TLV.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  PM Loss sub-type (201)       |          Length               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

| OTF |T|B|              Reserved (set to all 0s)               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                    Measurement Interval                       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                       Test Interval                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                      Loss Threshold                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 10: PM Loss Measurement sub-TLV format

Sub-type: indicates a new sub-type, the PM Loss Measurement sub-TLV

(value 201).

Length: indicates the length of the Value field in octets (16).

OTF: Origin Timestamp Format of the Origin Timestamp field described

in [RFC6374].  By default it is set to IEEE 1588 version 1.  If the

egress LSR cannot support this value an "OAM Problem/Unsupported

Timestamp Format" error MUST be generated.

Configuration Flags, please refer to [RFC6374] for further details:

- T: Traffic-class-specific measurement indicator.  Set to 1 when

the measurement operation is scoped to packets of a particular

traffic class (DSCP value), and 0 otherwise.  When set to 1, the

Bellagamba, et al.      Expires February 22, 2016              [Page 16]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

DS field of the message indicates the measured traffic class.  By

default it is set to 1.

- B: Octet (byte) count.  When set to 1, indicates that the

Counter 1-4 fields represent octet counts.  When set to 0,

indicates that the Counter 1-4 fields represent packet counts.  By

default it is set to 0.

Reserved: Reserved for future specification and set to 0 on

transmission and ignored when received.

Measurement Interval: the time interval (in milliseconds) at which

Loss Measurement query messages MUST be sent on both directions.  If

the edge LSR receiving the Path message cannot support such value, it

SHOULD reply with a higher interval.  By default it is set to (100)

as per [RFC6375].

Test Interval: test messages interval in milliseconds as described in

[RFC6374].  By default it is set to (10) as per [RFC6375].

Loss Threshold: the threshold value of measured lost packets per

measurement over which action(s) SHOULD be triggered.

2.2.8.  PM Delay Measurement Sub-TLV

The PM Delay Measurement sub-TLV" depicted in Figure 11 is carried as

a sub-TLV of the Performance Monitoring sub-TLV.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|  PM Delay Type (202)          |          Length               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

| OTF |T|B|             Reserved (set to all 0s)                |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                    Measurement Interval                       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                       Test Interval                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                      Delay Threshold                          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 11: PM Delay Measurement sub-TLV format

Sub-type: indicates a new sub-type, the PM Delay Measurement sub-TLV"

(value 202).

Length: indicates the length of the Value field in octets (16).

Bellagamba, et al.      Expires February 22, 2016              [Page 17]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

OTF: Origin Timestamp Format of the Origin Timestamp field described

in [RFC6374].  By default it is set to IEEE 1588 version 1.  If the

egress LSR cannot support this value an "OAM Problem/Unsupported

Timestamp Format" error MUST be generated.

Configuration Flags, please refer to [RFC6374] for further details:

- T: Traffic-class-specific measurement indicator.  Set to 1 when

the measurement operation is scoped to packets of a particular

traffic class (DSCP value), and 0 otherwise.  When set to 1, the

DS field of the message indicates the measured traffic class.  By

default it is set to 1.

- B: Octet (byte) count.  When set to 1, indicates that the

Counter 1-4 fields represent octet counts.  When set to 0,

indicates that the Counter 1-4 fields represent packet counts.  By

default it is set to 0.

Reserved: Reserved for future specification and set to 0 on

transmission and ignored when received.

Measurement Interval: the time interval (in milliseconds) at which

Delay Measurement query messages MUST be sent on both directions.  If

the edge LSR receiving the Path message cannot support such value, it

can reply with a higher interval.  By default it is set to (1000) as

per [RFC6375].

Test Interval: test messages interval (in milliseconds) as described

in [RFC6374].  By default it is set to (10) as per [RFC6375].

Delay Threshold: the threshold value of measured two-way delay (in

milliseconds) over which action(s) SHOULD be triggered.

2.2.9.  Fault Management Signal Sub-TLV

The FMS sub-TLV depicted in Figure 12 is carried as a sub-TLV of the

MPLS OAM Configuration sub-TLV.  When both working and protection

paths are configured, both LSPs SHOULD be configured with identical

settings of the E flag, T flag, and the refresh timer.

Bellagamba, et al.      Expires February 22, 2016              [Page 18]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|       FMS sub-type (300)      |            Length             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|E|S|T|            Reserved           |      Refresh Timer      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

~                           sub-TLVs                            ~

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 12: Fault Management Signal sub-TLV format

Sub-type: indicates a new sub-type, the FMS sub-TLV (value 300).

Length: indicates the length of the Value field in octets.

FMS Signal Flags are used to enable the FMS signals at end point MEPs

and the Server MEPs of the links over which the LSP is forwarded.  In

this document only the S flag pertains to Server MEPs.

The following flags are defined:

- E: Enable Alarm Indication Signal (AIS) and Lock Report (LKR)

signaling as described in [RFC6427].  Default value is 1

(enabled).  If the egress MEP does not support FMS signal

generation an "OAM Problem/Fault management signaling unsupported"

error MUST be generated.

- S: Indicate to a server MEP that it should transmit AIS and LKR

signals on the client LSP.  Default value is 0 (disabled).  If a

Server MEP which is capable of generating FMS messages is for some

reason unable to do so for the LSP being signaled an "OAM Problem/

Unable to create fault management association" error MUST be

generated.

- T: Set timer value, enabled the configuration of a specific

timer value.  Default value is 0 (disabled).

- Remaining bits: Reserved for future specification and set to 0.

Refresh Timer: indicates the refresh timer of fault indication

messages, in seconds.  The value MUST be between 1 to 20 seconds as

specified for the Refresh Timer field in [RFC6427].  If the edge LSR

receiving the Path message cannot support the value it SHOULD reply

with a higher timer value.

Bellagamba, et al.      Expires February 22, 2016              [Page 19]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

FMS sub-TLV MAY include Traffic Class sub-TLV Section 2.2.5.  If TC

sub-TLV is present, the value of the TC field MUST be used as the

value of the TC field of an MPLS label stack entry for FMS messages.

If the TC sub-TLV is absent, then selection of the TC value is local

decision.

2.2.10.  Source MEP-ID Sub-TLV

The Source MEP-ID sub-TLV depicted in Figure 13 is carried as a sub-

TLV of the MPLS OAM Functions TLV.

Note that support of ITU IDs is out-of-scope.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

| Source MEP-ID sub-type (400)  |           Length              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                       Source Node ID                          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|           Tunnel ID           |           LSP ID              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 13: Source MEP-ID sub-TLV format

Sub-type: indicates a new sub-type, the Source MEP-ID sub-TLV (value

400).

Length: indicates the length of the Value field in octets (8).

Source Node ID: 32-bit node identifier as defined in [RFC6370].

Tunnel ID: a 16-bit unsigned integer unique to the node as defined in

[RFC6370].

LSP ID: a 16-bit unsigned integer unique within the Tunnel_ID as

defined in [RFC6370].

3.  Summary of MPLS OAM Configuration Errors

This is the summary of Return Codes [RFC4379] defined in this

document:

- If an egress LSR does not support the specified BFD version, an

error MUST be generated: "OAM Problem/Unsupported BFD Version".

Bellagamba, et al.      Expires February 22, 2016              [Page 20]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

- If an egress LSR does not support the specified BFD

Encapsulation format, an error MUST be generated: "OAM Problem/

Unsupported BFD Encapsulation format".

- If an egress LSR does not support BFD Authentication, and it is

requested, an error MUST be generated: "OAM Problem/BFD

Authentication unsupported".

- If an egress LSR does not support the specified BFD

Authentication Type, an error MUST be generated: "OAM Problem/

Unsupported BFD Authentication Type".

- If an egress LSR is not able to use the specified Authentication

Key ID, an error MUST be generated: "OAM Problem/Mismatch of BFD

Authentication Key ID".

- If an egress LSR does not support the specified Timestamp

Format, an error MUST be generated: "OAM Problem/Unsupported

Timestamp Format".

- If an egress LSR does not support specified Delay mode, an "OAM

Problem/Unsupported Delay Mode" error MUST be generated.

- If an egress LSR does not support specified Loss mode, an "OAM

Problem/Unsupported Loss Mode" error MUST be generated.

- If an egress LSR does not support Delay variation measurements,

and it is requested, an "OAM Problem/Delay variation unsupported"

error MUST be generated.

- If an egress LSR does not support Dyadic mode, and it is

requested, an "OAM Problem/Dyadic mode unsupported" error MUST be

generated.

- If an egress LSR does not support Loopback mode, and it is

requested, an "OAM Problem/Loopback mode unsupported" error MUST

be generated.

- If an egress LSR does not support Combined mode, and it is

requested, an "OAM Problem/Combined mode unsupported" error MUST

be generated.

- If an egress LSR does not support Fault Monitoring Signals, and

it is requested, an "OAM Problem/Fault management signaling

unsupported" error MUST be generated.

- If an intermediate server MEP supports Fault Monitoring Signals

but is unable to create an association, when requested to do so,

Bellagamba, et al.      Expires February 22, 2016              [Page 21]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

an "OAM Problem/Unable to create fault management association"

error MUST be generated.

Ingress LSR MAY combine multiple MPLS OAM configuration TLVs and sub-

TLVs into single MPLS echo request.  In case an egress LSR doesn't

support any of the requested modes it MUST set the return code to

report the first unsupported mode in the list of TLVs and sub-TLVs.

And if any of the requested OAM configuration is not supported the

egress LSR SHOULD NOT process OAM Configuration TLVs and sub-TLVs

listed in the MPLS echo request.

4.  IANA Considerations

4.1.  TLV and Sub-TLV Allocation

IANA maintains the Multi-Protocol Label Switching (MPLS) Label

Switched Paths (LSPs) Ping Parameters registry, and within that

registry a sub-registry for TLVs and sub-TLVs.

IANA is requested a new TLV from the standards action range (0-16383)

and sub-TLVs as follows from this sub-registry.

+------+----------+---------------------------------+---------------+

| Type | Sub-type | Value Field                     | Reference     |

+------+----------+---------------------------------+---------------+

| TBA1 |          | MPLS OAM Functions              | This document |

|      | 100      | BFD Configuration               | This document |

|      | 101      | BFD Local Discriminator         | This document |

|      | 102      | BFD Negotiation Timer           | This document |

|      |          | Parameters                      |               |

|      | 103      | BFD Authentication              | This document |

|      | 104      | Traffic Class                   | This document |

|      | 200      | Performance Measurement         | This document |

|      | 201      | PM Loss Measurement             | This document |

|      | 202      | PM Delay Measurement            | This document |

|      | 300      | Fault Management Signal         | This document |

|      | 400      | Source MEP-ID                   | This document |

+------+----------+---------------------------------+---------------+

Table 1: IANA TLV Type Allocation

4.2.  MPLS OAM Function Flags Allocation

IANA is requested to create a new registry called the "MPLS OAM

Function Flags" registry and to populate it as follows.

Bellagamba, et al.      Expires February 22, 2016              [Page 22]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

+------------+--------------------+---------------------------------+

|    Bit     | MPLS OAM Function  | Description                     |

|  Position  |        Flag        |                                 |

+------------+--------------------+---------------------------------+

|     0      |         C          | Continuity Check (CC)           |

|     1      |         V          | Connectivity Verification (CV)  |

|     2      |         F          | Fault Management Signal (FMS)   |

|     3      |         L          | Performance Measurement/Loss    |

|            |                    | (PM/Loss)                       |

|     4      |         D          | Performance Measurement/Delay   |

|            |                    | (PM/Delay)                      |

|     5      |         T          | Throughput Measurement)         |

|    6-31    |                    | Unassigned (Must be zero)       |

+------------+--------------------+---------------------------------+

Table 2: MPLS OAM Function Flags

4.3.  OAM Configuration Errors

IANA maintains a registry "Multi-Protocol Label Switching (MPLS)

Label Switched Paths (LSPs) Ping Parameters" registry, and within

that registry a sub-registry "Return Codes".

IANA is requested to assign new Return Codes from the Standards

Action range (0-191) as follows:

Bellagamba, et al.      Expires February 22, 2016              [Page 23]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

+---------------+-----------------------------------+---------------+

| Error Value   | Description                       | Reference     |

| Sub-codes     |                                   |               |

+---------------+-----------------------------------+---------------+

| TBA3          | OAM Problem/Unsupported BFD       | This document |

|               | Version                           |               |

| TBA4          | OAM Problem/Unsupported BFD       | This document |

|               | Encapsulation format              |               |

| TBA5          | OAM Problem/Unsupported BFD       | This document |

|               | Authentication Type               |               |

| TBA6          | OAM Problem/Mismatch of BFD       | This document |

|               | Authentication Key ID             |               |

| TBA7          | OAM Problem/Unsupported Timestamp | This document |

|               | Format                            |               |

| TBA8          | OAM Problem/Unsupported Delay     | This document |

|               | Mode                              |               |

| TBA9          | OAM Problem/Unsupported Loss Mode | This document |

| TBA10         | OAM Problem/Delay variation       | This document |

|               | unsupported                       |               |

| TBA11         | OAM Problem/Dyadic mode           | This document |

|               | unsupported                       |               |

| TBA12         | OAM Problem/Loopback mode         | This document |

|               | unsupported                       |               |

| TBA13         | OAM Problem/Combined mode         | This document |

|               | unsupported                       |               |

| TBA14         | OAM Problem/Fault management      | This document |

|               | signaling unsupported             |               |

| TBA15         | OAM Problem/Unable to create      | This document |

|               | fault management association      |               |

+---------------+-----------------------------------+---------------+

Table 3: IANA Return Codes Allocation

5.  Acknowledgements

The authors would like to thank Nobo Akiya, David Allan and Adrian

Farrel for their thorough reviews and insightful comments.

6.  Security Considerations

The signaling of OAM related parameters and the automatic

establishment of OAM entities introduces additional security

considerations to those discussed in [RFC4379].  In particular, a

network element could be overloaded if an attacker were to request

high frequency liveliness monitoring of a large number of LSPs,

targeting a single network element.  Implementations must be made

cognizant of available OAM resources and MAY refuse new OAM

configurations that would overload a node.  Additional policies to

Bellagamba, et al.      Expires February 22, 2016              [Page 24]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

manage OAM resources may be used to provide some fairness in OAM

resource distribution among monitored LSPs.

Security of OAM protocols configured with extenssions to LSP Ping

described in this document are discussed in [RFC5880], [RFC5884],

[RFC6374], [RFC6427], and [RFC6428].

Additional discussion of security for MPLS protocols can be found in

[RFC5920].

7.  References

7.1.  Normative References

[RFC2119]  Bradner, S., "Key words for use in RFCs to Indicate

Requirement Levels", BCP 14, RFC 2119,

DOI 10.17487/RFC2119, March 1997,

<http://www.rfc-editor.org/info/rfc2119>.

[RFC4379]  Kompella, K. and G. Swallow, "Detecting Multi-Protocol

Label Switched (MPLS) Data Plane Failures", RFC 4379,

DOI 10.17487/RFC4379, February 2006,

<http://www.rfc-editor.org/info/rfc4379>.

[RFC5654]  Niven-Jenkins, B., Ed., Brungard, D., Ed., Betts, M., Ed.,

Sprecher, N., and S. Ueno, "Requirements of an MPLS

Transport Profile", RFC 5654, DOI 10.17487/RFC5654,

September 2009, <http://www.rfc-editor.org/info/rfc5654>.

[RFC5880]  Katz, D. and D. Ward, "Bidirectional Forwarding Detection

(BFD)", RFC 5880, DOI 10.17487/RFC5880, June 2010,

<http://www.rfc-editor.org/info/rfc5880>.

[RFC5884]  Aggarwal, R., Kompella, K., Nadeau, T., and G. Swallow,

"Bidirectional Forwarding Detection (BFD) for MPLS Label

Switched Paths (LSPs)", RFC 5884, DOI 10.17487/RFC5884,

June 2010, <http://www.rfc-editor.org/info/rfc5884>.

[RFC6370]  Bocci, M., Swallow, G., and E. Gray, "MPLS Transport

Profile (MPLS-TP) Identifiers", RFC 6370,

DOI 10.17487/RFC6370, September 2011,

<http://www.rfc-editor.org/info/rfc6370>.

[RFC6374]  Frost, D. and S. Bryant, "Packet Loss and Delay

Measurement for MPLS Networks", RFC 6374,

DOI 10.17487/RFC6374, September 2011,

<http://www.rfc-editor.org/info/rfc6374>.

Bellagamba, et al.      Expires February 22, 2016              [Page 25]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

[RFC6427]  Swallow, G., Ed., Fulignoli, A., Ed., Vigoureux, M., Ed.,

Boutros, S., and D. Ward, "MPLS Fault Management

Operations, Administration, and Maintenance (OAM)",

RFC 6427, DOI 10.17487/RFC6427, November 2011,

<http://www.rfc-editor.org/info/rfc6427>.

[RFC6428]  Allan, D., Ed., Swallow Ed., G., and J. Drake Ed.,

"Proactive Connectivity Verification, Continuity Check,

and Remote Defect Indication for the MPLS Transport

Profile", RFC 6428, DOI 10.17487/RFC6428, November 2011,

<http://www.rfc-editor.org/info/rfc6428>.

7.2.  Informative References

[RFC3209]  Awduche, D., Berger, L., Gan, D., Li, T., Srinivasan, V.,

and G. Swallow, "RSVP-TE: Extensions to RSVP for LSP

Tunnels", RFC 3209, DOI 10.17487/RFC3209, December 2001,

<http://www.rfc-editor.org/info/rfc3209>.

[RFC5036]  Andersson, L., Ed., Minei, I., Ed., and B. Thomas, Ed.,

"LDP Specification", RFC 5036, DOI 10.17487/RFC5036,

October 2007, <http://www.rfc-editor.org/info/rfc5036>.

[RFC5462]  Andersson, L. and R. Asati, "Multiprotocol Label Switching

(MPLS) Label Stack Entry: "EXP" Field Renamed to "Traffic

Class" Field", RFC 5462, DOI 10.17487/RFC5462, February

2009, <http://www.rfc-editor.org/info/rfc5462>.

[RFC5920]  Fang, L., Ed., "Security Framework for MPLS and GMPLS

Networks", RFC 5920, DOI 10.17487/RFC5920, July 2010,

<http://www.rfc-editor.org/info/rfc5920>.

[RFC6371]  Busi, I., Ed. and D. Allan, Ed., "Operations,

Administration, and Maintenance Framework for MPLS-Based

Transport Networks", RFC 6371, DOI 10.17487/RFC6371,

September 2011, <http://www.rfc-editor.org/info/rfc6371>.

[RFC6375]  Frost, D., Ed. and S. Bryant, Ed., "A Packet Loss and

Delay Measurement Profile for MPLS-Based Transport

Networks", RFC 6375, DOI 10.17487/RFC6375, September 2011,

<http://www.rfc-editor.org/info/rfc6375>.

[RFC6669]  Sprecher, N. and L. Fang, "An Overview of the Operations,

Administration, and Maintenance (OAM) Toolset for MPLS-

Based Transport Networks", RFC 6669, DOI 10.17487/RFC6669,

July 2012, <http://www.rfc-editor.org/info/rfc6669>.

Bellagamba, et al.      Expires February 22, 2016              [Page 26]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

[RFC7419]  Akiya, N., Binderberger, M., and G. Mirsky, "Common

Interval Support in Bidirectional Forwarding Detection",

RFC 7419, DOI 10.17487/RFC7419, December 2014,

<http://www.rfc-editor.org/info/rfc7419>.

[RFC7487]  Bellagamba, E., Takacs, A., Mirsky, G., Andersson, L.,

Skoldstrom, P., and D. Ward, "Configuration of Proactive

Operations, Administration, and Maintenance (OAM)

Functions for MPLS-Based Transport Networks Using RSVP-

TE", RFC 7487, DOI 10.17487/RFC7487, March 2015,

<http://www.rfc-editor.org/info/rfc7487>.

Authors' Addresses

Elisa Bellagamba

Email: elisa.bellagamba@gmail.com

Gregory Mirsky

Ericsson

Email: Gregory.Mirsky@ericsson.com

Loa Andersson

Huawei Technologies

Email: loa@mail01.huawei.com

Pontus Skoldstrom

Acreo AB

Electrum 236

Kista  164 40

Sweden

Phone: +46 8 6327731

Email: pontus.skoldstrom@acreo.se

Dave Ward

Cisco

Email: dward@cisco.com

Bellagamba, et al.      Expires February 22, 2016              [Page 27]

Internet-Draft       Extensions for MPLS-TP OAM Conf         August 2015

John Drake

Juniper

Email: jdrake@juniper.net

Bellagamba, et al.      Expires February 22, 2016              [Page 28]