## Slide 1: Generalized Network Control Automation YANG Model draft-bryskin-netconf-automation-yang-02
Igor Bryskin (Huawei Technologies)
Xufeng Liu (Volta Networks)
Alex Clemm (Huawei Technologies)
Henk Birkholz (Fraunhofer SIT)
Tianran Zhou (Huawei Technologies)

## Slide 2: Objectives
Purpose: to manipulate network close loop automation via configuration of standardized Event-Condition-Action (ECA) containers
ECA – a set of NETCONF style requests/primitives (e.g. get data, edit-config, call-rpc, etc), whose execution on the server is triggered by a specified event, and whose order of execution is conditioned by current and/or historical network states and/or their derivatives
Explicit non-goal: introducing a new interpreter/language/scripting environment

## Slide 3: ECAs, when and why
Reaction to events could be articulated to the network server in advance
To enhance network responsiveness to events
To improve scalability of network control
To configure on the server programmable by a client logic

## Slide 4: Policy Variables
Policy Variable (PV) is an ECA state, i.e. a structure to keep results of the ECA execution for immediate or future use
PV types: global (shared between ECAs), local (ECA scope, static or dynamic)
PV content structure:
of a common type (e.g. integer, uint64, etc.)
Or
of an existing YANG node pointed by XPath (e.g. TE_Topologies/links/te_link)

## Slide 5: What could be done with PVs?
read from/write to YANG data store
Used as input/output when calling YANG RPCs
Used to generate notification messages;
Used as input/output for function calls, for example Fmult(a, 0.75) to calculate 0.75*a
Used in XPath expressions with PVs referred to by their respective positions in the YANG tree

## Slide 6: ECA Events
Subscribable events:
- explicitly defined by YANG modules
- YANG Push or/and smart filter subscriptions
Timers

## Slide 7: ECA Conditions
Logical expressions with YANG data store nodes and/or PVs
A condition could be configured as:
- a single XPath expression
a hierarchy of comparisons and logical combinations of thereof
(e.g. (X == Y || A<B) && (C<=D || E>F))

## Slide 8: ECA Actions
NETCONF style primitives:
- get data, edit-config, etc.
- calling YANG defined RPCs (e.g. TE_TunnelPathComputation RPC defined by YANG TE Tunnel model)
- sending notification messages to the client
- adding/removing event notification subscriptions
Starting/stopping timers
Calling other ECAs
Performing operations on PVs (e.g. function calls)

## Slide 9: ECA Structure
Event name
List of local PVs
Normal Condition-Action list
Cleanup Condition-Action list (to undo actions from the normal Condition-Action list in case one of the normal actions was rejected by the server)

## Slide 10: Changes since IETF101
A mechanism is introduced to define ECA events via YANG PUSH subscriptions
A structure is defined to correlate by the client ECA notifications with corresponding events

## Slide 11: Defining ECA Events via YANG PUSH Subscriptions
Client:
- configures a PUSH subscription
- configures an ECA event specifying the PUSH subscription name

## Slide 12: Defining ECA Events via YANG PUSH Subscriptions
Server (at the moment of event configuration):
- registers the event interpreting the referred PUSH subscription trigger as event firing trigger
uses the PUSH subscription filters to auto-configure the event’s ECA input in the form of ECA’s local PVs
Server (at the moment of even firing):
- copies data store states pointed by the PUSH subscription filters into ECA’s auto-configured local PVs and triggers the ECA’s Condition-Action chain execution

## Slide 13: ECA Events and Notifications Correlation
ECA notification is the only ECA action that interacts directly with the client
Multiple ECAs could be triggered simultaneously, each of which potentially generating multiple semantically different one-time and/or repetitive notifications
Every ECA notification message includes mandatorily the event name and event-scope unique notification name to facilitate for the client event-notification correlation

## Slide 14: Next Steps
Solicit more discussions and feedback from WG