## Slide 1: NTPv5 Modular Architecture
Proposal: Define NTPv5 as two interacting subsystems
  Timing engine
  protocol engine
Purpose: allow different timing engines to be defined for different applications
  For example, General purpose IT (time for logfiles, security ticket times outs, …)
  For example, precision timing for financial networks
Purpose: allow different protocol engines to be defined for different applications
  For example, with and without security

## Slide 2: Client Functional Block diagram
Management Interface
Timing engine
Protocol engine
OS clock
Network stack
config
config
Packet
data
Timing
data
Clock
corrections
Packets
sw
timestamps
hw
timestamps
NTPv5
PHY clock
Timing
Protocol
interface
Alternatively
Mgmt could
Have separate
Network stack

## Slide 3: Server Functional Block diagram
Management Interface
Timing engine
Protocol engine
OS clock
Network stack
config
config
Packet
data
Timing
data
Timestamps,
corrections
Packets
sw
timestamps
hw
timestamps
NTPv5
PHY clock
Timing
Protocol
interface
Alternatively
Mgmt could
Have separate
Network stack
Timing
Reference
Time,
status
Config,
status

## Slide 4: Functional Block Diagram Notes
Local clocks
  OS system clock (SW timestamps)
  Steerable counter on a PHY chip (HW timestamps)
  Custom HW clock. Often implemented in time servers or cyber physical systems
Timing engine
  Clients do not need to read local clock, only to determine its offset via NTP
  Server needs to read local clocks to steer them to the timing reference
  Timing reference: GNSS receiver, PTP input, 1PPS input, etc

## Slide 5: Protocol Engine
Interfaces with network stack
  Builds packets for transmission
  Software layer timestamps
  Parses packets upon receipt
Executes network security
Determines when to send packets
  Based on average packet rate from timing engine
Passes received information to timing engine
  Timestamps and timing metadata
  Message status, such as expected message not received, security working, etc

## Slide 6: Timing engine
Selects servers to receive time from
  Allows for optimization based on analysis of timing data
Analyze received timing information
  Outlier detection and removal
  False ticker identification and removal
  Lucky packet pre-filters
  Generate timing statistics
Clock control
  PLL filter
  Clock corrections
Report statistics to management interface

## Slide 7: Timing engine - protocol engine interface
From timing engine
List of target server IP addresses
Average packet time interval for each server
From protocol engine
Server not responding flags
Received packet data
  Four timestamps
  Root delay & root dispersion
  Reference ID
  Leap second flag
  Server stratum
  Security on/off flag

## Slide 8: Feedback welcome
Thanks to Ulrich Windl, and Hal Murry for astute questions and suggestions
Looking for coauthors for a draft architecture document
doug.Arnold@meinberg-usa.com