## Slide 1: Forwarding Plane OAM for MPLS-based Tunneling Applications: A Position Paper
Alexander Vainshtein Robert Rennison Prashant Desai
Alexander Kugel Andrew Sergeev Rotem Cohen

## Slide 2: Background
MPLS has become the dominant tunneling technology:
  Started from IP VPN
  Expanded to cover also PWs and VPLS
MPLS forwarding plane (FP):
  Defined in RFC 3031, RFC 3032, RFC 3443
  Augmented by RFC 5331 and RFC 5332
  Inherited by MPLS transport profile (MPLS-TP)
  Includes a set of mechanisms for separating OAM and traffic:
    IP-based exceptions at the LSP tail-end in IP/MPLS
      Martian IP addresses
      IP Router Alert option etc.
    TTL expiration (RFC 3031, RFC 3443)
      For interception of packets in the middle of an LSP or in an S-PE for multi-segment PWs
    PW Associated Channel (RFC 4385)
    GAL and G-ACH at LSP tail-end (RFC 5586)
      For MPLS-TP LSPs and Sections

## Slide 3: Expected Forwarding Plane OAM Functionality
Basic non-intrusive OAM Functions:
  Connectivity check (proactive)
  Connectivity verification (on-demand)
  Trace route (on-demand)
  Forward and Backward Defect Notification
Extended non-intrusive OAM Functions:
  Packet loss measurement (proactive and/or on-demand)
  Packet delay measurement (proactive and/or on-demand)
Non-intrusive OAM:
  OAM packets and regular (customer) traffic are fate-sharing
Intrusive OAM:
  FP-related (e.g., intrusive loopback)
  Is it really required?
  Limited to bi-directional LSPs in MPLS-TP?
Alarms Suppression:
  Seems to be out of scope (not FP)

## Slide 4: Existing FP OAM Mechanisms: MPLS and PW
LSP-Ping
  Defined in RFC 4379
  Provides on-demand connectivity verification and trace route for LSPs
  Extended to PWs using VCCV (RFC 5085)
  Extended to MPLS-TP LSPs using GAL/G-ACh
BFD
  Defined in RFC 5580
  Supports proactive connectivity check and BDI
  Adapted for usage in LSPs in RFC 5884
  Extended to PWs in RFC 5885
  Extended to MPLS-TP LSPs using GAL/G-ACh
Loss and Delay Measurements:
  Definitions are in progress (as part of the MPLS-TP effort)
  Two options for loss measurement:
    Based on user traffic – ideal, but perceived as very complicated
    Based on synthetic traffic – estimate only, but pretty simple

## Slide 5: Forward Defect Notification
RFC 5860 strongly hints that FDI functionality is required in MPLS-TP
Definition is in progress
Highly problematic if combined with MPLS Fast re-Route
  See the next slide

## Slide 6: FDI vs. FRR
A
B
C
D
E
C’
The LSP runs A  B  C  D  E with MEPs at A and D and MIPs in the rest of the nodes
If the link BC is broken, the link-level MEP at C detects that and initiates FDI/AIS insertion
  Assume hard binding between the failed link and LSP (e.g., because per-interface label space has been used)
  FDI is received and acted upon by a MEP in E
At the same time, B operates a node protection bypass (B  C’  D)
  C is not aware of the bypass
  D is not aware of FDI/AIS insertion
As a consequence, E receives both regular traffic and FDI/AIS

## Slide 7: Summary
Non-Intrusive FP OAM:
  Mainly covered by the existing or emerging techniques
    CC and RDI are provided by BFD
    On-demand CV and trace route are provided by LSP-Ping
    Loss and delay measurements – the definitions are in progress
    Multiple encapsulations are already defined with well-understood scope
      LSP can use IP-based techniques (default) or GAL/G-ACh (where a split between MPLS and IP is required)
      PW can use VCCV Type 3, VCCV Type 1 and their combinations
  No need to develop brand new OAM mechanisms
    E.g., to “import” Ethernet Service OAM (IEEE 802.1ag, ITU-T Y.1731) which has been designed with a very different FP in mind
  FDI mechanisms (if required) should be introduced with caution:
    The linkage between server and client layers in the MPLS FP is weak (as in the case of per-platform label space)
    Merging capabilities of the MPLS FP make these mechanisms potentially harmful
Intrusive FP OAM:
  The need and applicability area are not clear

## Slide 8: Questions?
Alexander.Vainshtein@ecitele.com
Robert.Rennison@ecitele.com
Prashant.desai@ecitele.com
Alexander.Kugel@ecitele.com
Andrew.Sergeev@ecitele.com
Rotem.Cohdn@ecitele.com