Draft

bbf2013.1062

WT-321

Public Wi-Fi Access in Multi-service Broadband Networks

Revision: 02

Revision Date: January 2014

Notice

The Broadband Forum is a non-profit corporation organized to create guidelines for broadband network system development and deployment.  This Broadband Forum Working Text is a draft, and has not been approved by members of the Forum.  Even if approved, this Broadband Forum Working Text is not binding on the Broadband Forum, any of its members, or any developer or service provider.  This Broadband Forum Working Text is subject to change.  This Broadband Forum Working Text is copyrighted by the Broadband Forum, and portions of this Broadband Forum Working Text may be copyrighted by Broadband Forum members. This Working Text is for use by Broadband Forum members only.  Advance written permission by the Broadband Forum is required for distribution of this Broadband Forum Working Text in its entirety or in portions outside the Broadband Forum.

This Broadband Forum Working Text is provided AS IS, WITH ALL FAULTS.  Any person holding a copyright in this Broadband Forum Working Text, or any portion thereof, disclaims to the fullest extent permitted by law any representation or warranty, express or implied, including, but not limited to, any warranty:

(A)	OF ACCURACY, COMPLETENESS, MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, NON-INFRINGEMENT, OR TITLE;

(B)	THAT THE CONTENTS OF THIS BROADBAND FORUM Working Text ARE SUITABLE FOR ANY PURPOSE, EVEN IF THAT PURPOSE IS KNOWN TO THE COPYRIGHT HOLDER;

(C)	THAT THE IMPLEMENTATION OF THE CONTENTS OF THE Working Text WILL NOT INFRINGE ANY THIRD PARTY PATENTS, COPYRIGHTS, TRADEMARKS OR OTHER RIGHTS.

By using this Broadband Forum Working Text, users acknowledge that there is no obligation upon Broadband Forum members to license patents that are necessary to implement a Working Text, and such licensing obligations as may exist with respect to Broadband Forum Technical Reports do not attach until a proposed Technical Report is finalized by the Broadband Forum.

ANY PERSON HOLDING A COPYRIGHT IN THIS BROADBAND FORUM Working Text, OR ANY PORTION THEREOF, DISCLAIMS TO THE FULLEST EXTENT PERMITTED BY LAW (A) ANY LIABILITY (INCLUDING DIRECT, INDIRECT, SPECIAL, OR CONSEQUENTIAL DAMAGES UNDER ANY LEGAL THEORY) ARISING FROM OR RELATED TO THE USE OF OR RELIANCE UPON THIS Working Text; AND (B) ANY OBLIGATION TO UPDATE OR CORRECT THIS Working Text.

The text of this notice must be included in all copies of this Broadband Forum Working Text.

Revision History

| Revision Number | Revision Date | Revision Editor | Changes |
| --- | --- | --- | --- |
| 00 | March 2013 |  | Purpose, Scope text based on Q4 2012 Osaka Meeting |
| 01 | September, 2013 | Jianjie You Bo Wang | Updated based on Q3 2013 Atlanta meeting including: bbf2013.878.02, bbf2013.884.02, bbf2013.888.02. |
| 02 | January 2014 | Bo Wang | Updated based on Q4 2013 Rome meeting including: bbf2013.1202.01 bbf2013.1203.01 |

Comments or questions about this Broadband Forum Working Text should be directed to:

| Editor | Jianjie You Bo Wang | ZTE Corporation China Telecom |  |
| --- | --- | --- | --- |
| E2EArchitecture WG Chairs | David Allan David Thorne | Ericsson BT |  |
| Vice Chair | Sven Ooghe | Alcatel-Lucent |  |

Table of Contents

Executive Summary	7

1	Purpose and Scope	8

1.1	Purpose	8

1.2	Scope	8

2	References and Terminology	10

2.1	Conventions	10

2.2	References	10

2.3	Definitions	11

2.4	Abbreviations	11

3	Working Text Impact	12

3.1	Energy Efficiency	12

3.2	IPv6	12

3.3	Security	12

3.4	Privacy	12

4	Introduction	13

5	Use Cases for Public Wi-Fi Access	14

6	Public Wi-Fi Access Network Architecture	15

6.1	Public WiFi Access Network Architecture	15

6.1.1	Architecture 1: AC and BNG are separated	15

6.1.2	Architecture 2: AC and BNG are integrated	16

6.2	Infrastructure Network Specification	16

6.3	Access Point Function Virtualization	17

7	Authentication Technologies	18

7.1	802.1x Authentication	18

7.1.1	Scenario 1: AC and BNG are separated, AC is the Authenticator, BNG acts as RADIUS Proxy	18

7.1.2	Scenario 2: AC and BNG are separated, AC is the Authenticator, BNG is not as RADIUS Proxy	19

7.1.3	Scenario 3: AC and BNG are separated, BNG acts as Authenticator	21

7.1.4	Scenario 4: AC and BNG are integrated, AC/BNG is the authenticator	23

7.2	Portal Authentication	25

7.3	MAC Authentication	25

8	Nodal Requirements	26

8.1	General Requirements	26

8.2	Access Point Requirements	26

8.3	Access Node Requirements	26

8.4	BNG Requirements	26

8.5	Access Controller Requirements	26

8.6	Portal Server Requirements	26

8.7	AAA Server Requirements	26

List of Figures

Figure 1 - Architecture 1a: AC deployed close to the APs	15

Figure 2 - Architecture 1b: AC co-located with BNG	16

Figure 3 - Architecture 2: AC and BNG integrated	16

Figure 4 - Scenario 1: AC BNG separated (AC: Authenticator, BNG: RADIUS Proxy)	18

Figure 5 - Scenario 2: AC BNG separated (AC: Authenticator, BNG: not RADIUS Proxy)	20

Figure 6 - Scenario 3: AC BNG separated (BNG: Authenticator)	22

Figure 7 - Scenario 4: AC BNG integrated	24

List of Tables

No table of figures entries found.

Executive Summary

Wi-Fi has recently become a ubiquitous access technology available at homes, enterprises and hot spots. Offloading data traffic from the mobile network using Wi-Fi to the broadband network is the current trend with the Fixed Mobile Convergence. The Broadband Forum is developing architecture and solutions for this new access technology.

WT-321 builds on the work done in IETF’s CAPWAP architecture and comes up with a new public Wi-Fi access network architecture.

# Purpose and Scope

## Purpose

Since the introduction of mobile devices that include Wi-Fi, there has been an increasing interest in improving Broadband Forum’s multi-service broadband architecture to incorporate the public Wi-Fi access. The rise in the use of smartphones at public hotspots has accelerated this interest.  As the popularity of Wi-Fi enabled devices along with access to Internet and other data services continues to increase, an emerging ecosystem is taking shape where applications are developed largely independently of access types. There is increased desire to provide network capabilities that offer better user experiences and more efficient network utilization for these devices and this is becoming a requirement for operators that wish to provide superior user experiences.

## Scope

The WT-321 scope includes, use cases, physical and logical architecture and functional and/or nodal requirements for public Wi-Fi access capabilities that are used nomadically as part of a broadband network. Architecture includes data, signaling, and management, as well as functional decomposition and placement into network nodes. Functional and nodal requirements will be considered for the following: Wi-Fi Access Point (AP), Residential Gateway (RG), CAPWAP Access Controller (AC), Broadband Network Gateway (BNG). The scope also includes potential interactions with PDP and/or Authentication Authorization Accounting Server (AAA).

WT-321 covers requirements on:

  - The potential to simplify Wi-Fi APs by placing some of their current functions (e.g. authenticator) in a more centralized controller.

  - Retain the current capability for a single physical AP to host multiple Wi-Fi providers and services.

  - Vetting the use of CAPWAP as the protocol supporting centralization of AP control, and then building upon this or the chosen protocol as necessary.

  - AP control (including authentication and management) deployed as an overlay over the broadband access - regardless of type.

  - Traffic management of AP broadband access supporting both aggregate traffic management between Wi-Fi service providers and also per-subscriber traffic management.

  - Support for both co-located and also separated AC and BNG.

  - Mutual authentication between APs and ACs.

  - Authentication of attaching devices using the AP or AC as the authenticator.

  - Security mechanisms including key management.

  - Reliability mechanisms.

  - The support of location based services.

  - Client connection management, including choice of AP.

  - Interoperability between the AP and AC.

  - The interface between an AC and broadband network.

WT-321refers to WT-145, WT-146, WT-178, WT-124i3 and IETF specifications RFC 5415 and RFC 5416 as appropriate.

# References and Terminology

## Conventions

In this Working Text, several words are used to signify the requirements of the specification. These words are always capitalized. More information can be found be in RFC 2119 [5].

| MUST | This word, or the term “REQUIRED”, means that the definition is an absolute requirement of the specification. |
| --- | --- |
| MUST NOT | This phrase means that the definition is an absolute prohibition of the specification. |
| SHOULD | This word, or the term “RECOMMENDED”, means that there could exist valid reasons in particular circumstances to ignore this item, but the full implications need to be understood and carefully weighed before choosing a different course. |
| SHOULD NOT | This phrase, or the phrase "NOT RECOMMENDED" means that there could exist valid reasons in particular circumstances when the particular behavior is acceptable or even useful, but the full implications need to be understood and the case carefully weighed before implementing any behavior described with this label. |
| MAY | This word, or the term “OPTIONAL”, means that this item is one of an allowed set of alternatives. An implementation that does not include this option MUST be prepared to inter-operate with another implementation that does include the option. |

## References

The following references are of relevance to this Working Text. At the time of publication, the editions indicated were valid. All references are subject to revision; users of this Working Text are therefore encouraged to investigate the possibility of applying the most recent edition of the references listed below.

A list of currently valid Broadband Forum Technical Reports is published at 
www.broadband-forum.org.

| Document | Title | Source | Year |
| --- | --- | --- | --- |
| WT-124i3 | Functional Requirements for Broadband Residential Gateway Devices | BBF |  |
| WT-134 | Policy Control Framework for DSL | BBF |  |
| WT-146 | IP Sessions | BBF |  |
| WT-178 | Multi-service Broadband Network Architecture and Nodal Requirements | BBF |  |
|  |  |  | 2011 |
|  |  |  | 2011 |
|  |  |  | 2011 |
|  |  |  | 2010 |
| RFC 2119 | Key words for use in RFCs to Indicate Requirement Levels | IETF | 1997 |

## Definitions

The following terminology is used throughout this Working Text.

## Abbreviations

This Working Text uses the following abbreviations:

| AAA | Authentication, Authorization & Accounting |
| --- | --- |
| AN | Access Node |
| BNG | Broadband Network Gateway |
| EUD | End User Device |
| TR | Technical Report |
| RG | Residential Gateway |
| WG | Working Group |
| WLAN | Wireless Local Area Network. |
| WT | Working Text |

# Working Text Impact

## Energy Efficiency

WT-321 has no impact on energy efficiency.

## IPv6

New considerations need to be given for pair-wise operator interworking where one or the other operator has migrated or is in the process of migrating to IPv6.  For example, if a wireline operator is using 6rd as a migration path and the wireless operator is using IPv6, then the network elements involved in interworking may need to be changed or the interworking model may differ.

## Security

TBD.

## Privacy

TBD.

# Introduction

This section provides an overview.

# Use Cases for Public Wi-Fi Access

# Public Wi-Fi Access Network Architecture

This section provides requirements about how the public Wi-Fi architecture is aligned with WT-145 and WT-178 architectural principles.

## Public WiFi Access Network Architecture

### Architecture 1: AC and BNG are separated

In this architecture, the AC and BNG are deployed separately as shown in Figure 1 and Figure 2.

A single physical AP can provide multiple SSIDs for different WiFi providers or different services. For example, enterprise traffic can be offloaded locally via a specific SSID.

There are several deployment assumptions in this architecture:

- AC is responsible for AP management.

- AC is not responsible for IP assignment.

- BNG manages traffic on a per subscriber basis.

- AC can be deployed close to the APs if there are dense APs environment.

- AC can be co-located with BNG.

- AC can communicate with AAA directly, or via RADIUS proxy (e.g. BNG).

- AP needs to support multiple SSIDs.

- Different authentication methods (e.g. 802.1X, Web portal) need to be supported for different SSIDs.

- Different SSIDs can be used to connect to different service provider or enterprise networks.

Figure 1 - Architecture 1a: AC deployed close to the APs

Figure 2 - Architecture 1b: AC co-located with BNG

### Architecture 2: AC and BNG are integrated

In this architecture, the AC is integrated with BNG as shown in Figure 3. A single physical AP  can provide multiple SSIDs for different WiFi providers or different services. For example, enterprise traffic can be offloaded locally via a specific SSID.

There are several deployment assumptions in this architecture:

- AC is responsible for AP management.

- AC&BNG node manages traffic on a per subscriber basis.

- AP needs to support multiple SSIDs.

- Different authentication methods (e.g. 802.1X, Web portal) need to be supported for different SSIDs.

- Different SSIDs can be used to connect to different service provider or enterprise networks.

Figure 3 - Architecture 2: AC and BNG are integrated

## Infrastructure Network Specification

This section provides the infrastructure network specification based on the architectures mentioned in section 6.1. This specification includes the public WiFi access network architecture,  nodal requirements and deployment options.

## Access Point Function Virtualization

# Authentication Technologies

## 802.1X Authentication

### Scenario 1: AC and BNG are separated, AC is the Authenticator, BNG acts as RADIUS Proxy

In this scenario, AC is deployed as the 802.1X authenticator, and BNG is the RADIUS proxy. In the network, BNG is the service gateway. BNG can be aware of the EUD’s information, and is responsible for IP address assignment and traffic management on a per subscriber basis. Key exchange  and IP address assignment procedures are initiated after the successful EAP session. An example of authentication flow for scenario 1 is shown in Figure 5.

Figure 4 - Scenario 1: AC and BNG are separated (AC: authenticator, BNG: RADIUS proxy)

Figure 5 - Example of authentication flows for scenario 1

### Scenario 2: AC and BNG are separated, AC is the Authenticator, BNG is not as RADIUS Proxy

In this scenario, AC is deployed as the 802.1X authenticator,  and BNG isn’t the RADIUS proxy. In the network, BNG is the service gateway.BNG is responsible for IP address assignment, and traffic management on a per subscriber basis. In this architecture, it is assumed that  BNG can obtain EUD’s authentication information from the AAA. Key exchange and IP address assignment procedures are initiated after the successful EAP session. An example of authentication flow for scenario 2 is shown in Figure 7.

Figure 6 - Scenario 2: AC and BNG are separated (AC: authenticator, BNG: not RADIUS proxy)

Figure 7 - Example of authentication flows for scenario 2

### Scenario 3: AC and BNG are separated, BNG acts as Authenticator

In this scenario, BNG is deployed as the 802.1X authenticator. BNG is responsible for IP address assignment, and traffic management on a per subscriber basis. AC/AP needs to acquire the PMK based on 802.11i requirement in the procedure of Key Exchange via RADIUS packets. An example of authentication flow for scenario 3 is shown in Figure 9.

Figure 8 - Scenario 3: AC and BNG are separated (BNG: authenticator)

Figure 9 - Example of authentication flows for scenario 3

### Scenario 4: AC and BNG are integrated, AC/BNG is the authenticator

In this scenario, AC is integrated with BNG, as the 802.1X authenticator. Key exchange and IP address assignment procedures are initiated after the successful EAP session. An example of authentication flow for scenario 4 is shown in Figure 11.

Figure 10 - Scenario 4: AC and BNG are integrated

Figure 10 - Example of authentication flows for scenario 4

## Portal Authentication

### Scenario 1: AC and BNG are separated

When AC and BNG are separated, BNG is responsible for IP address assignment and traffic management on a per subscriber basis. In portal authentication, a pair of username and password allocated by the operator is considered as a subscriber.

BNG is responsible for redirecting the HTTP traffic of the EUD to the portal server before the EUD is successfully authenticated. The subscriber needs to input the username and password in the portal page provided by portal server. After successful authentication, traffic is forwarded in normal manner.

AAA is responsible for authentication and accounting. Additionally, AAA provides the policy and QoS configuration of the EUD to the BNG as part of the RADIUS Access Accept message.

Reauthentication may be required after specified period of time or volume quota.

Figure X1 - Scenario 1: AC and BNG are separated (portal authentication)

### Scenario 2: AC and BNG are integrated

When AC is integrated with BNG, AC/BNG is responsible for IP address assignment and traffic management on a per subscriber basis, and redirecting the HTTP traffic of the EUD to the portal server before the user is successfully authenticated. The subscriber needs to input the username and password in the portal page provided by portal server. After successful authentication, traffic is forwarded in normal manner.

AAA is responsible for authentication and accounting. Additionally, AAA provides the policy and QoS configuration of the EUD to the BNG as part of the RADIUS Access Accept message.

Reauthentication may be required after specified period of time or volume quota.

Figure X3 - Scenario 2: AC and BNG are integrated (portal authentication)

## MAC Authentication

# Nodal Requirements

## General Requirements

## Access Point Requirements

This section provides a set of requirements the AP/RG must fulfill in support of the architecture.

[R-a1] AP MUST be able to support multiple SSIDs.

## Access Node Requirements

This section provides a set of the requirements the Access Node must fulfill in support of the architecture.

## BNG Requirements

This section provides a set of requirements the BNG must fulfill in support of the architecture.

Table Y1 - BNG requirements for different scenarios of 802.1X authentication

|  | Scenario 1 | Scenario 2 | Scenario 3 | Scenario 4 |
| --- | --- | --- | --- | --- |
| R-b1 |  |  | MUST | MUST |
| R-b2 | MUST |  |  |  |
| R-b3 |  | MUST | MUST | MUST |
| R-b4 | MUST |  |  |  |
| R-b5 | MUST | MUST | MUST | MUST |
| R-b6 |  | MUST |  |  |
| R-b7 |  | MUST |  |  |
| R-b8 |  |  | MUST |  |
| R-b9 | MUST | MUST | MUST | MUST |
| R-b10 |  |  |  | MUST |

[R-b1] BNG MUST support 802.1X Authenticator.

[R-b2] BNG MUST support RADIUS proxy.

[R-b3] BNG MUST support RADIUS client.

[R-b4] BNG MUST proxy the EAPoR packets in order to acquire EUD information (e.g., MAC address, IMSI) for accounting and management.

[R-b5] Before assigning an IP address to the EUD, BNG MUST confirm that the EUD has been successfully authenticated.

[R-b6] Upon receiving the DHCP Discover message, BNG MUST initiate the RADIUS Access Request message based on MAC address to AAA in order to check whether the EUD has been successfully authenticated.

[R-b7] BNG MUST be able to receive the EUD information (e.g. IMSI) for accounting and user management from the AAA if the EUD has been successfully authenticated.

[R-b8] BNG MUST transfer PMK (Pairwise Master Key) obtained from AAA to the AC

(Editor’s note: It parked. This requirement depends on finding or creating a standardized way to do it.)

[R-b9] Upon successful IP address allocation, BNG MUST send the Accounting Start Message to the AAA.

[R-b10] BNG MUST support 4-way 802.11i handshake with EUD.

## Access Controller Requirements

This section provides a set of requirements the Access Controller (AC) must fulfill in order to support the architecture.

Table Y2 - AC requirements for different scenarios of 802.1X authentication

|  | Scenario 1 | Scenario 2 | Scenario 3 | Scenario 4 |
| --- | --- | --- | --- | --- |
| R-c1 | MUST | MUST |  | MUST |
| R-c2 | MUST | MUST |  | MUST |
| R-c3 | MUST | MUST | MUST | MUST |
| R-c4 |  |  |  | MUST |
| R-c5 |  |  |  | MUST |

[R-c1] AC MUST support 802.1X Authenticator.

[R-c2] AC MUST support RADIUS client .

[R-c3] AC MUST support 4-way 802.11i handshake with EUD.

[R-c4] Before assigning an IP address to the EUD, AC MUST confirm that the EUD has been successfully authenticated.

[R-c5] Upon successful IP address allocation, AC MUST send the Accounting Start Message to the AAA.

## Portal Server Requirements

This section provides a set of requirements the Portal Server must fulfill in order to support the architecture.

## AAA Server Requirements

This section provides a set of requirements of the AAA (Authentication, Authorization and Accounting) Server must fulfill in order to support the architecture.

Table Y3 - AAA requirements for different scenarios of 802.1X authentication

|  | Scenario 1 | Scenario 2 | Scenario 3 | Scenario 4 |
| --- | --- | --- | --- | --- |
| R-d1 | MUST | MUST | MUST | MUST |
| R-d2 | MUST | MUST | MUST | MUST |
| R-d3 |  | MUST |  |  |
| R-d4 | MUST | MUST | MUST | MUST |

[R-d1] AAA MUST support 802.1X Authentication Server.

[R-d2] AAA MUST send the policy and QoS configuration (e.g., bandwidth, time/traffic quota) to the RADIUS client (AC or BNG) for the EUDs successfully authenticated.

[R-d3] Upon receiving the RADIUS Access Request message with the MAC address of the EUD from BNG, AAA MUST send the corresponding EUD information to BNG in the RADIUS Access Accept message.

[R-d4] AAA MUST support storage of the EUD information.

End of Broadband Forum Working Text WT-321