## Slide 1: Advertisement for BIER in ROLL Design Team
Consider joining/collaborating in BIER design team in ROLL-WG:
Email: roll-bier-dt@ietf.org (normal subscribe)
Issues: tte@cs.fau.de
What could be cool about this (if design team decides to do it) ?
End-to-end BIER (with TE) in low-power networks (e.g.: building control)
  Example: Application Controller sends BIER packet to subset of clients (lightbulbs)
  Each client is BFER (has a bit)
  Every packet can address a separate subset of actors through bitstring
  Only controller app needs to be BIER aware. Receivers can think its just IP multicast.
BIER TE bits to save power/memory
  Routers are low-power (memory/CPU). Do not want to keep large routing table (1000 lightbulbs). Links are low power too.
  Every interface has a bit. Routers only need to route on bits to directly connected downstream neighbors.
No ASIC constraints. Everything is software
  Headers/Bitstring can be compressed (loss free, lossy (bloom) to support long bitstrings.
  Should result in header more compact than existing ROLL/RPL headers even for unicast: Only hop-by-hop bits sets to one receiver: Would also be used for unicast forwarding.
ROLL/BFER
stack
IP multicast App
10..1000 clients/actors
ROLL/BFR
Low-power
router
ROLL/BFIR
Root node
1
2
3
4
6
5
10
Bits for interfaces
(BIER-TE) to allow
explicit steering of
traffic
Root also acts as
Controller assigning/
Managing Bits
BIER aware
Application
Controller
Tunnel Encap
BIER / IP
App-Payload
Data Packet
Root node adds
Interface bits and
compresses header ?!
Application controller can efficiently send packets to
Every subset of receivers by being BIER aware.
AnyTransit
Slide v1.0
Control: learn which bit maps to which client
11.. 999