## Slide 1: Overlay OAM Requirements draft-ooamdt-rtgwg-ooam-requirement
Greg Mirsky gregory.mirsky@ericsson.com
Carlos Pignataro cpignata@cisco.com
Nagendra Kumar naikumar@cisco.com
Deepak Kumar dekumar@cisco.com
IETF-95 April, 2016
Erik Nordmark nordmark@acm.org
David Mozes davidm@mellanox.com
Mach Chen mach.chen@huawei.com
Santosh Pallagatti santosh.pallagatti@gmail.com

## Slide 2: Motivation
Work in NVO3, SFC and BIER WGs on OAM Framework and Requirements drafts
Proposed adaptation, extension of existing OAM protocols (BFD in VXLAN)
Proposed new mechanism (Transcending Traceroute)
Common OAM presentation and discussion at IETF-94

## Slide 3: Structure
Fault Management
  Proactive FM
  On-demand FM
Performance Management
Alarm Indication Signal (Supression)
Resiliency

## Slide 4: Requirements
OOAM independent from a transport layer
Any node implicitly serves as MEP
SDN-azation of Overlay OAM
Proactive and on-demand OAM created equal
Unidirectional Overlay OAM (CC and PM) optimization as services (multicast, SFC) are unidirectional
OAM is about what is going in the transport layer and thus it must be in-band , i.e. fate sharing with data traffic
Bi-directional OAM is important too, e.g. CC-CV and out-of-band Fault Management Signal

## Slide 5: Fault Management
Proactive
  Continuity Check
  Remote Defect Indication
  Connectivity Verification
On-demand
  LoC defect localization
  path tracing through overlay network
  verification of mapping between overlay network and client layer services
  ECMP discovery and verification
  proxy ping/traceroute
Fault Management Signals like Alarm Indication Signal to suppress client layer alarms when server layer fault detected
Overlay network survivability may use protection switching and restoration

## Slide 6: Performance Measurements
Passive and Active Performance Measurement OAM are complimentary instruments in OOAM toolbox
  One-way active and passive
  Two-way active
Support calculation of performance metrics:
  packet delay
  packet delay variation
  packet loss
  goodput (delivered throughput)

## Slide 7: Next steps
Welcome comments from the WGs
Notes: <number>