## Slide 1: Use Case
Where the BFD session will be established?
  Where to start? Where to terminate?
  End-2-end ? e.g., Ingress<->SF2
  Segment? e.g., Classifier<->SFF1, SFF1<->SFF2, SF1<->SF2, etc. ?
SFF1
SF1
Source
Classifier
SFF2
SF2
Destination

## Slide 2: NSH BFD with IP/UDP Encapsulation
Same as RFC5881 and 5884
The source/destination addresses and UDP port are derived from the IP/UDP header
Notes: O (OAM bit) must be set
MD-type = 0x2
Next Protocol = ?
TLV Class = IETF
C (critical bit ) must be set
Type = BFD

## Slide 3: NSH BFD without IP/UDP Encapsulation
Add source and destination addresses field
UDP port is not necessary, the “Next Protocol” and/or “type” fields can be used to indicate a BFD packet

## Slide 4: NSH BFD with embedded Src/Dst Info
Source and destination address are embedded in the BFD control packet
Similar to RFC6428, e.g., Source MEP ID TLV