## Slide 1: Performance measurement with the marking method in BIER draft-mirsky-bier-pmmm-01
Greg Mirsky gregory.mirsky@ericsson.com
Vero Zheng vero.zheng@huawei.com
Mach Chen mach.chen@huawei.com
Giuseppe Fioccola giuseppe.fioccola@telecomitalia.it
IETF-95 April 2016, Buenos Aires
IETF-95

## Slide 2: What and why
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 0 1 0 1 | Ver | Len | Entropy |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| BitString (first 32 bits) ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ BIER Header
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ BitString (last 32 bits) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|OAM| Reserved | Proto | BFIR-id |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+-+-+ OAM field
|S|D| S – single mark method
+-+-+ D – double mark method
IETF-95

## Slide 3: Single Mark Method
Batching packets based on time interval to measure packet loss by switching value of the S flag. D flag MUST be set to 0 on transmit and ignored on receipt.
First/Last Packet Delay calculation:
  capture timestamp of when S flag value flips. Method is sensitive to packet loss and packet re-ordering
Average Packet Delay calculation:
  collect timestamps for each packet received within a single block. Average of the timestamp is the sum of all the timestamps divided by the total number of packets received. Hence minimally impacted by a packet loss and no impact if packets get re-ordered.
IETF-95
S=0
S=1
S=1
S=1
S=0
S=0
S=1

## Slide 4: Double Mark Method
Use S flag to create batch of packets as in Single Mark method
Use D flag to create new set of marked packets that are fully identified over the BIER network
Collect and compare timestamps on D-marked packets to calculate packet delay as well as the minimum and maximum delay values.
IETF-95
S=0, D=0
S=1, D=0
S=1, D=1
S=1, D=0
S=0, D=0
S=0, D=1
S=1, D=0
Notes: <number>

## Slide 5: Sample BIER sub-domain
BFR A applies Double Mark method
BFRs B, E, and H record timestamps of D-tagged BIER packets
IETF-95
A
B
C
D
E
F
G
H

## Slide 6: Next Steps
Welcome questions, comments
Address comments
Adopt by WG
Thank you
IETF-95