## Slide 1: Overlay OAM Design Team Report
Greg Mirsky gregory.mirsky@ericsson.com
Carlos Pignataro cpignata@cisco.com
Nagendra Kumar naikumar@cisco.com
Deepak Kumar dekumar@cisco.com
IETF-95 April, 2016
Erik Nordmark nordmark@acm.org
David Mozes davidm@mellanox.com
Mach Chen mach.chen@huawei.com
Santosh Pallagatti santosh.pallagatti@gmail.com

## Slide 2: Motivation
Existing work in NVO3, SFC and BIER WGs on OAM Framework, Requirements, and Solutions
Look at the OAM “puzzle” holistically, prevent divergence
E.g.:
  Proposed adaptation, extension of existing OAM protocols (BFD in VXLAN)
  Proposed new mechanism (Transcending Traceroute)
Common OAM presentation and discussion at IETF-94

## Slide 3: OOAM DT Charter
This Design Team is chartered to first produce a brief gap analysis and requirements document to focus its work on protocol extensions. This should be published by March 2016. With that basis, this Design Team is chartered to rapidly propose extensions to existing IETF OAM protocols such as those discussed in [RFC 7276] and new ones to support the requirements for OAM from NVO3, BIER, and SFC. The Design Team will produce an initial proposal by IETF 95. It is expected that the initial proposal will provide guidance to additional people who will be interested in working on the details and gaps.
The Design Team will consider the preliminary OAM requirements from NVO3, BIER, and SFC. The Design Team should align with the LIME WG's work on common YANG models of OAM.
https://trac.tools.ietf.org/area/rtg/trac/wiki/RtgOoamDT

## Slide 4: Overlay OAM Requirements draft-ooamdt-rtgwg-ooam-requirement-00

## Slide 5: Structure
Fault Management
  Proactive FM
  On-demand FM
Performance Management
Alarm Indication Signal (Supression)
Resiliency

## Slide 6: Requirements
OOAM independent from a transport layer
Any node implicitly serves as MEP
SDN-azation of Overlay OAM
Proactive and on-demand OAM created equal
Unidirectional Overlay OAM (CC and PM) optimization as services (multicast, SFC) are unidirectional
OAM is about what is going in the transport layer and thus it must be in-band , i.e. fate sharing with data traffic
Bi-directional OAM is important too, e.g. CC-CV and out-of-band Fault Management Signal

## Slide 7: Fault Management
Proactive
  Continuity Check
  Remote Defect Indication
  Connectivity Verification
On-demand
  LoC defect localization
  path tracing through overlay network
  verification of mapping between overlay network and client layer services
  ECMP discovery and verification
  proxy ping/traceroute
Fault Management Signals like Alarm Indication Signal to suppress client layer alarms when server layer fault detected
Overlay network survivability may use protection switching and restoration

## Slide 8: Performance Measurements
Passive and Active Performance Measurement OAM are complimentary instruments in OOAM toolbox
  One-way active and passive
  Two-way active
Support calculation of performance metrics:
  packet delay
  packet delay variation
  packet loss
  goodput (delivered throughput)
Definition of Terms at: https://tools.ietf.org/html/rfc7276

## Slide 9: Overlay OAM: Gap Analysis draft-ooamdt-rtgwg-oam-gap-analysis-01

## Slide 10: Gap Analysis Goals
Today, we can ping/traceroute/BFD the underlay; that does not tell us much about the VNI/SFP/overlay.
Two dimensions:
  Operators: Functionally adjacent to long-existing operational practice (format on the wire is less important)
  Implementers: Similar across different Encaps (reuse encodings?)

## Slide 11: Gap Analysis Detail
Done:
  Identification of existing OAM Protocols
To be Done:
  Possible feature Gaps within each OAM protocol
  Applicability of OAM Protocol to different Overlays
  Encapsulation-specific requirements of OAM Protocol (extensions to the underlay encap)

## Slide 12: Document Structure
2. Working Group Overview . . . . . . . . . . . . . . . . . . . 5
2.1. BIER . . . . . . . . . . . . . . . . . . . . . . . . . . 5
2.2. NVO3 . . . . . . . . . . . . . . . . . . . . . . . . . . 5
2.3. SFC . . . . . . . . . . . . . . . . . . . . . . . . . . . 5
3. Overlay OAM Toolset . . . . . . . . . . . . . . . . . . . . . 5
3.1. Overlay OAM Fault Management . . . . . . . . . . . . . . 5
3.1.1. Proactive Continuity Check and Connectivity
Verification . . . . . . . . . . . . . . . . . . . . 5
3.1.2. On-demand Continuity Check and Connectivity
Verification . . . . . . . . . . . . . . . . . . . . 7
3.1.3. Alarm Indication Signal . . . . . . . . . . . . . . . 8
3.2. Overlay OAM Performance Measurement . . . . . . . . . . . 8
3.2.1. Overlay OAM PM Active . . . . . . . . . . . . . . . . 8
3.2.2. Overlay OAM PM Passive . . . . . . . . . . . . . . . 8
3.3. Telemetry in Overlay OAM . . . . . . . . . . . . . . . . 9
3.4. Conclusions . . . . . . . . . . . . . . . . . . . . . . . 9

## Slide 13: Available OAM tools
Fault Management:
proactive continuity check:
  Bidirectional Forwarding Detection (BFD) for point-to-point as defined in [RFC5880], [RFC5882], [RFC5883], [RFC5884], [RFC5885], [RFC6428] and [RFC7726];
  BFD for multipoint network as defined in [I-D.ietf-bfd-multipoint] and [I-D.ietf-bfd-multipoint-active-tail];
  S-BFD as defined in [I-D.ietf-bfd-seamless-base] and [I-D.ietf-bfd-seamless-ip];
on-demand continuity check and connectivity verification:
  MPLS Echo Request/Reply, a.k.a. LSP Ping, as defined in [RFC4379] and its numerous extensions;
  LSP Self-ping, as defined in [RFC7746];
  [I-D.kumarzheng-bier-ping] is a good example of generic troubleshooting and defect localization tool that can be extended and suited for more specific requirements of the particular type of an overlay network.

## Slide 14: Available OAM tools
Performance Measurement:
packet loss and delay measurement in MPLS networks, as defined in [RFC6374] with ability to export measurement results for post-processing [I-D.ietf-mpls-rfc6374-udp-return-path];
Two-Way Active Measurement Protocol (TWAMP), as defined in [RFC5357], [RFC6038], and [RFC7750];
use of the Marking Method [I-D.tempia-ippm-p3m] that, if accordingly supported by the overlay layer, can behave as close as technically possible to a passive method to measure performance, e.g. [I-D.mirsky-bier-pmmm-oam].

## Slide 15: Example 1: BFD for SFC based on draft-ooamdt-rtgwg-gap-analysis-00

## Slide 16: OAM for SFC Scope
Continuity Check on the SFP
Verify that the SFF has the attachment point to talk to the SF
Testing connectivity, NOT SF Functionality

## Slide 17: Use Case
SFF3
Where to deploy the BFD sessions?
  Between SFFs (the major case)
    Hop-by-hop BFD session (e.g., SFF1<->SFF2, SFF2<->SFF3)
    End-2-end BFD session (e.g., SFF1<->SFF3)
  Other possibilities ?
SFF1
SF1
Source
Classifier
SFF2
SF2
Destination
SF3
Hop-by-Hop
BFD Session
End-2-end
BFD Session

## Slide 18: Hop-by-hop Case
An SFF should have capability to determine whether a packet should be delivered to an SF or terminated.
Encapsulation dependent
SFF3
SFF1
SFF2

## Slide 19: End-2-End Case
An SFF (e.g., SFF2) should have capability to determine whether a packet should be delivered to an SF or the next hop SFF.
Encapsulation dependent
SFF3
SFF1
SFF2

## Slide 20: Control Plane
BFD session bootstrapping
  In-band signaling
  Out-of-band channel
  Centralized controller

## Slide 21: Encapsulations
BFD with IP/UDP encapsulation
  Same as RFC5881 and 5884
  The source/destination addresses and UDP port are derived from the IP/UDP header
BFD without IP/UDP encapsulation
  Add source and destination addresses field
  UDP port is not necessary, the “Next Protocol” and/or “type” fields can be used to indicate a BFD packet
BFD with embedded Src/Dst Info
  Source and destination address are embedded in the BFD control packet
  Similar to RFC6428, e.g., Source MEP ID TLV

## Slide 22: Example 2: SFC Trace based on draft-ooamdt-rtgwg-gap-analysis-00

## Slide 23: SFC Traceroute
sff_client.py --remote-sff-ip 10.0.1.41 --remote-sff-port 4789 --sfp-id 22 --sfp-index 255 --trace-req --num-trace-hops 3
Sending Trace packet to Service Path and Service Index: (22, 255)
Trace response...
Service-hop: 0. Service Type: dpi, Service Name: SF1, Address of Reporting SFF: ('10.0.1.41', 4789)
Service-hop: 1. Service Type: firewall, Service Name: SF4, Address of Reporting SFF: ('10.0.1.42', 4789)
Service-hop: 2. Service Type: napt44, Service Name: SF5, Address of Reporting SFF: ('10.0.1.43', 4789)
Trace end

## Slide 24: In-band Telemetry Probe (Yes, we need this too for)

## Slide 25: What is this ?
At some moment in time we would like to know the exact network state of the data path traffic
    Example: ECMP next hop
    Real time control feedback loop
      Like ECN, XCP, RCP or utilization aware routing (CONGA)
    Real time of network event detections
    OAM
We would like to get this info without control plan intervention.

## Slide 26: How it works
Traffic source (Application, NIC,TOR, etc.) will embed a request inside the data packet generate special probe packet
Destination nodes, Sink, receive the instructions and possibly report the collected results of those instructions to an application or a controller
Allowing the traffic Sink to monitor the exact state of the network
The request and response have to be send over an Overlay network. Documented use-cases for some overlays already exist:
  NSH
  Geneve
  Vxlan GPE

## Slide 27: Telemetry Next steps
Update the draft to cover following aspects of the gaps
  Use Case
  Control plane
  Data plane/Encapsulations

## Slide 28: Conclusion
We need your review and comments!
We are ready to start the protocol work –> What’s missing from the Requirements or Gap Analysis?