## Slide 1: Inbound Telemetry Probe
David Mozes .
Benny Koren .
Mellanox

## Slide 2: What is this ?
  Some time we would like to know the exact network state of the data path traffic .
      Example :ECMP next hop.
      Real time control feedback loop
      Real time of network event detections
      OAM
We would like to get this info with out control plan intervention.

## Slide 3: How it is work
Traffic source (Application,Nic,Tor ,etc ) will embedded the requests inside data packets or special probe packets .
“Destination “ nodes (“Sinks”) receive the instructions and possible report the collected result of those instructions to the application or controller .
Allowing the traffic sink to monitor the exact state of the network .

## Slide 4: Protocol principle without packet format
The proposal will supply a list of recommended parameters that need to be collected by the device
Since it HW depended , each device will report what it can supported by him .
The Source will tell what from the evitable supported list he like to get

## Slide 5: Why it related to the ODT
The request and response have to be send over overlay networks ad well
  Curently there are proposal for:
  NSH
  Geneve
  Vxlan GPE

## Slide 6: Example of optional parametrs

## Slide 7: Buffers parameters
Buffers pools parameters :
Pool number ; (The pool idenifier )
Size ; (The pool size )
Direction ; (Ingress or egress)
buffer occupancy ; (current buffer occupancy)
Max buffer occupancy; ( the maximum we monitored)
Clear ; (Clear the max buffers occupancy )
time ?

## Slide 8: Buffers parameters continue
Puffer class parameters (Port ,prio)
  Local port
  Priority
  Direction ; (Ingress or egress)
  buffer occupancy ; (current buffer occupancy)
  Max buffer occupancy; ( the maximum we monitored
  Clear ; (Clear the max buffers occupancy )
  Threshold ?

## Slide 9: Time
Seconds (32 bits )
Microseconds (32 bits)
Nanoseconds (32 bits)

## Slide 10: Multicast buffer usages
Traffic class
  buffer occupancy ; (current buffer occupancy)
  Max buffer occupancy; ( the maximum we monitored
  Clear ; (Clear the max buffers occupancy )

## Slide 11: Drop Counters
Buffer drop :
  Receive port
  Priority
WRED drop per egress port per priority
Tail drop per egress port per priority

## Slide 12: More optional parameters
Rate per egress port .
Latency of a packets .