KARP Working Group                                           G. Lebovitz

Internet-Draft                                    Juniper Networks, Inc.

Intended status: Informational                                 M. Bhatia

Expires: December 20, 2011                                Alcatel-Lucent

R. White

Cisco Systems

June 18, 2011

The Threat Analysis and Requirements for Cryptographic Authentication of

Routing Protocols' Transports

draft-ietf-karp-threats-reqs-03

Abstract

Different routing protocols exist and each employs its own mechanism

for securing the protocol packets on the wire.  While most already

have some method for accomplishing cryptographic message

authentication, in many cases the existing methods are outdated,

vulnerable to attack, and employ cryptographic algorithms that have

been deprecated.  The "Keying and Authentication for Routing

Protocols" (KARP) effort aims to overhaul and improve these

mechanisms.

This document has two main parts - the first describes the threat

analysis for attacks against routing protocols' transports and the

second enumerates the requirements for addressing the described

threats.  This document, along with the KARP design guide will be

used by KARP design teams for specific protocol review and overhaul.

This document reflects the input of both the IETF's Security Area and

Routing Area in order to form a jointly agreed upon guidance.

Status of this Memo

This Internet-Draft is submitted in full conformance with the

provisions of BCP 78 and BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF).  Note that other groups may also distribute

working documents as Internet-Drafts.  The list of current Internet-

Drafts is at http://datatracker.ietf.org/drafts/current/.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

This Internet-Draft will expire on December 20, 2011.

Lebovitz, et al.        Expires December 20, 2011               [Page 1]

Internet-Draft        KARP Threats and Requirements            June 2011

Copyright Notice

Copyright (c) 2011 IETF Trust and the persons identified as the

document authors.  All rights reserved.

This document is subject to BCP 78 and the IETF Trust's Legal

Provisions Relating to IETF Documents

(http://trustee.ietf.org/license-info) in effect on the date of

publication of this document.  Please review these documents

carefully, as they describe your rights and restrictions with respect

to this document.  Code Components extracted from this document must

include Simplified BSD License text as described in Section 4.e of

the Trust Legal Provisions and are provided without warranty as

described in the Simplified BSD License.

Table of Contents

1.  Introduction . . . . . . . . . . . . . . . . . . . . . . . . .  3

1.1.  Terminology  . . . . . . . . . . . . . . . . . . . . . . .  3

1.2.  Requirements Language  . . . . . . . . . . . . . . . . . .  6

1.3.  Scope  . . . . . . . . . . . . . . . . . . . . . . . . . .  6

1.4.  Incremental Approach . . . . . . . . . . . . . . . . . . .  7

1.5.  Goals  . . . . . . . . . . . . . . . . . . . . . . . . . .  8

1.6.  Non-Goals  . . . . . . . . . . . . . . . . . . . . . . . . 11

1.7.  Audience . . . . . . . . . . . . . . . . . . . . . . . . . 11

2.  Threats  . . . . . . . . . . . . . . . . . . . . . . . . . . . 13

2.1.  Threats In Scope . . . . . . . . . . . . . . . . . . . . . 13

2.2.  Threats Out of Scope . . . . . . . . . . . . . . . . . . . 15

3.  Requirements for Phase 1 of a Routing Protocol Transport's

Security Update  . . . . . . . . . . . . . . . . . . . . . . . 17

4.  Security Considerations  . . . . . . . . . . . . . . . . . . . 22

5.  IANA Considerations  . . . . . . . . . . . . . . . . . . . . . 23

6.  Acknowledgements . . . . . . . . . . . . . . . . . . . . . . . 24

7.  References . . . . . . . . . . . . . . . . . . . . . . . . . . 25

7.1.  Normative References . . . . . . . . . . . . . . . . . . . 25

7.2.  Informative References . . . . . . . . . . . . . . . . . . 25

Authors' Addresses . . . . . . . . . . . . . . . . . . . . . . . . 27

Lebovitz, et al.        Expires December 20, 2011               [Page 2]

Internet-Draft        KARP Threats and Requirements            June 2011

1.  Introduction

In March 2006 the Internet Architecture Board (IAB) held a workshop

on the topic of "Unwanted Internet Traffic".  The report from that

workshop is documented in [RFC4948].  Section 8.1 of that document

states "A simple risk analysis would suggest that an ideal attack

target of minimal cost but maximal disruption is the core routing

infrastructure."  Section 8.2 calls for "[t]ightening the security of

the core routing infrastructure."  Four main steps were identified

for that tightening:

o  More secure mechanisms and practices for operating routers.  This

work is being addressed in the OPSEC Working Group.

o  Cleaning up the Internet Routing Registry repository (IRR), and

securing both the database and the access, so that it can be used

for routing verification.  This work should be addressed through

liaisons with those running the IRR's globally.

o  Specifications for cryptographic validation of routing message

content.  This work is being addressed in the SIDR Working

Group.

o  Securing the routing protocols' packets on the wire

This document addresses the last item in the list above, securing the

transmission of routing protocol packets on the wire, or rather

securing routing protocol transport.  This effort is referred to as

Keying and Authentication for Routing Protocols, or "KARP".  This

document specifically addresses the threat analysis for per packet

routing protocol transport authentication (and integrity), and the requirements for

protocols to mitigate those threats.

This document is one of two that together form the guidance and

instructions for KARP design teams working to overhaul routing

protocol transport security.  The other document is the KARP Design

Guide [I-D.ietf-karp-design-guide].

1.1.  Terminology

Within the scope of this document, the following words, when

beginning with a capital letter, or spelled in all capitals, hold the

meanings described to the right of each term.  If the same word is

used un-capitalized, then it is intended to have its common English

definition.

Lebovitz, et al.        Expires December 20, 2011               [Page 3]

Internet-Draft        KARP Threats and Requirements            June 2011

PSK (Pre-Shared Key)

A key used by both peers in a secure configuration.  Usually

exchanged out-of-band prior to a first connection.

Routing Protocol

When used with capital "R" and "P" in this document the term

refers the Routing Protocol for which work is being done to

provide or enhance its peer authentication mechanisms.

PRF

In cryptography, a pseudorandom function, abbreviated PRF,

is a collection of efficiently-computable functions which emulate

a random oracle in the following way: No efficient algorithm can

distinguish (with significant advantage) between a function chosen

randomly from the PRF family and a random oracle (a function whose

outputs are determined at random).  Informally, a PRF takes

a secret key and a set of input values and produces random-seeming

output values for each input value.

KDF (Key derivation function)

A KDF is a function in which an input key and other input data is

used to generate (or derive) keying material that can be employed

by cryptographic algorithms.  The key that is input to a KDF is

called a key derivation key.  KDFs can be used to generate one or

more keys from either (i) a truly random or pseudorandom seed

value or (ii) a Diffie-Hellman shared secret or (iii) a non-

uniform random source or (iv) a passphrase.

Identifier

The type and value used by one peer of an authenticated message

exchange to signify to the other peer who they are.  The

Identifier is used by the receiver as an index into a table

containing further information about the peer that is required to

continue processing the message, for example a Security

Association (SA) or keys.

Identity Proof

Once the form of identity is decided, then there must be a

cryptographic proof of that identity, that the peer really is who

they assert themselves to be.  Proof of identity can be arranged

between the peers in a few ways, for example pre-shared keys, raw

asymmetric keys, or a more user-friendly representation of

Lebovitz, et al.        Expires December 20, 2011               [Page 4]

Internet-Draft        KARP Threats and Requirements            June 2011

asymmetric keys, such as a certificate.  Certificates can be used

in a way requiring no additional supporting systems -- e.g. public

keys for each peer can be maintained locally for verification upon

contact.  Certificate management can be made simpler and

scalable with the use of minor additional supporting systems, as

is the case with self-signed certificates and a flat file list of

"approved thumbprints".  Self-signed certificates will have

somewhat lower security properties than Certification Authority

signed certificates.  The use of these different identity proofs

vary in ease of deployment, ease of ongoing management, startup

effort, ongoing effort and management, security strength, and

consequences from loss of secrets from one part of the system to

the rest of the system.  For example, they differ in resistance to

a security breach, and the effort required to remediate the whole

system in the event of such a breach.  The point here is that

there are options, many of which are quite simple to employ and

deploy.

SA (Security Association)

The parameters and keys that together form the required

information for processing secure sessions between (or among) peers.

Examples of items that may be associated with an SA include: Identifier,

PSK, Traffic Key, cryptographic algorithms, key lifetimes.

KMP (Key Management Protocol)

A protocol used between peers for creation, distribution and

maintenance of secret keys.  It determines how secret keys are

generated and made available to both the parties.  If session or

traffic keys are being used, KMP is responsible for generating

them and determining when they should be renewed.

A KMP is helpful because it negotiates unique, pair wise, random

keys without administrator involvement.  It also negotiates, as

mentioned earlier, several of the SA parameters required for the

secure connection, including key life times.  It keeps track of

those lifetimes using counters, and negotiates new keys and

parameters before they expire, again, without administrator

interaction.  Additionally, in the event of a security breach, changing the

KMP key will immediately cause a rekey to occur for the Traffic

Key, and those new Traffic Keys will be installed and used in the

current connection.

KMP Function

Lebovitz, et al.        Expires December 20, 2011               [Page 5]

Internet-Draft        KARP Threats and Requirements            June 2011

Any actual KMP used in the general KARP solution framework

Peer Key

Keys that are used between (or among) peers as a basis for identifying one another.  These

keys may or may not be connection-specific, depending on how they

were established, and what forms of identity and identity proof are

used in the system.  A peer key generally would be provided by a

KMP that would later be used to derive fresh traffic keys.

Traffic Key

The key (or set of keys) used for protecting the routing

protocol traffic.  Since the traffic keys used in a particular

connection are not a fixed part of a device configuration no data

exists anywhere else in the operator's systems which can be

stolen, e.g. in the case of a terminated or turned employee.  If a

server or other data store is stolen or compromised, the thieves

gain no access to current traffic keys.  They may gain access to

key derivation material, like a PSK, but not current traffic keys

in use.

1.2.  Requirements Language

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT",

"SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this

document are to be interpreted as described in RFC2119 [RFC2119].

When used in lower case, these words convey their typical use in

common language, and are not to be interpreted as described in

RFC2119 [RFC2119].

1.3.  Scope

Three basic services may be employed in order to

secure any piece of data as it is transmitted over the wire: confidentiality,

authenticity, or integrity.  The focus for this effort,

and the scope for this roadmap document, will be message

authentication and packet integrity only.  This work explicitly

excludes, at this point in time, privacy services.  Non-repudiation

is also excluded as a goal at this time.  Since the objective of most

routing protocols is to broadly advertise the routing topology,

routing protocol packets are commonly sent in the clear;

confidentiality is not normally required for routing protocols.

However, ensuring that routing peers are authentically identified

, and that no rogue peers or unauthenticated packets can compromise the

stability of the routing environment is critical, and thus our focus.

Confidentiality and non-repudiation may be addressed in future work.

Lebovitz, et al.        Expires December 20, 2011               [Page 6]

Internet-Draft        KARP Threats and Requirements            June 2011

OSPF [RFC5709], IS-IS [RFC5310], LDP [RFC5036], and RIP have

existing mechanisms for cryptographically authenticating and

integrity checking the packets.  Products with these

mechanisms have been produced, code has been written,

and both have been optimized for these existing security mechanisms.  Rather

than turn away from these mechanisms, this document aims to enhance

them, updating them to modern and secure levels.

Therefore, the scope of this roadmap of work includes:

o  Making use of existing routing protocol transport security

mechanisms, where they exist, and enhancing or updating them as

necessary for modern cryptographic best practices

o  Developing a framework for using automatic key management in order

to ease deployment, lower cost of operation, and allow for rapid

responses to security breaches

o  Specifying the automated key management protocol that may be

combined with the bits-on-the-wire mechanisms.

This document does not contain protocol specifications.  Instead, it

defines the areas where protocol specification work is needed and

sets a direction, a set of requirements, and priorities for

addressing that specification work.

There are a set of threats to routing protocols that are considered

in-scope for this document, and a set considered out-of- scope.

These are described in detail in the Threats (Section 2) section

below.

1.4.  Incremental Approach

The work also serves as an agreement between the Routing Area and the

Security Area about the priorities and work plan for incrementally

delivering the above work.  The principle of “crawl, walk, run” will be

employed. Thus routing protocol authentication mechanisms may not go

immediately from their current state to a state reflecting the best

possible, most modern security practices.  This point is important as

there will be times when the best-security-possible will give way to

vastly-improved-over-current-security-but-admittedly-not-yet-best-

security-possible, in order that incremental progress toward a more

secure Internet may be achieved.  As such, this document will call

out places where agreement has been reached on such trade offs.

Incremental steps will need to be taken for a few very practical

reasons.  First, there are a considerable number of deployed routing

devices in operating networks that will not be able to run the most

Lebovitz, et al.        Expires December 20, 2011               [Page 7]

Internet-Draft        KARP Threats and Requirements            June 2011

modern cryptographic mechanisms without significant and unacceptable

performance penalties.  The roadmap for any one routing protocol MUST

allow for incremental improvements on existing operational devices.

Second, current routing protocol performance on deployed devices has

been achieved over the last 20 years through extensive tuning of

software and hardware elements, and is a constant focus for

improvement by vendors and operators alike.  The introduction of new

security mechanisms affects this performance balance.  The

performance impact of any incremental step of security improvement

will need to be weighed by the community, and introduced in such a

way that allows the vendor and operator community a path to adoption

that upholds reasonable performance metrics.  Therefore, certain

specification elements may be introduced carrying the "SHOULD"

guidance, with the intention that the same mechanism will carry a

"MUST" in a future release of the specification.

This approach gives the vendors and implementors the guidance they need to

tune their software and hardware appropriately over time.  Last, some

security mechanisms require the build out of other operational

support systems, and this will take time.  An example where these

three reasons are at play in an incremental improvement roadmap is

seen in the improvement of BGP's [RFC4271] security via

the TCP Authentication Option (TCP-AO) [RFC5925] effort.  It would be

ideal, and reflect best common security practice, to have a fully

specified key management protocol for negotiating TCP-AO's

keying material, e.g., using certificates for peer authentication.

However, in the spirit of incremental deployment, we will first

address issues like cryptographic algorithm agility, replay attacks,

TCP session resetting in the base TCP-AO protocol before we layer key

management on top of it.

1.5.  Goals

The goals and general guidance for the KARP work follow.

1.  Provide authentication and integrity protection for packets on

the wire of existing routing protocols

2.  Define a path to incrementally improve security of the routing

infrastructure as explained in the earlier sections.

3.  The deployability of the improved security solutions on currently

running routing infrastructure equipment.  This begs the

consideration of the current state of processing power available

on routers in the network today.

Lebovitz, et al.        Expires December 20, 2011               [Page 8]

Internet-Draft        KARP Threats and Requirements            June 2011

4.  Operational deployability - A solution’s acceptability will also

be measured by how deployable the solution is by common operator

teams using common deployment processes and infrastructures.

Specifically, we will try to make these solutions fit as well as possible

into current operational practices or router deployment.  This

will be heavily influenced by operator input, to ensure that what

we specify can -- and, more importantly, will -- be deployed once

specified and implemented by vendors.  Deployment of

incrementally more secure routing infrastructure in the Internet

is the final measure of success.  Measurably, we would like to

see an increase in the number of surveyed respondents who report

deploying the updated authentication and integrity mechanisms in

their networks, as well as a sharp rise in usage for the total

percentage of their network's routers.

Interviews with operators show several points about routing

security.  First, over 70% of operators have deployed transport

connection protection via TCP-MD5 [RFC3562] on their eBGP

[ISR2008] sessions.  Over 55% also deploy this TCP option on their iBGP connections,

and 50% make use of keyed MD5 integrity features offered on some other IGP.  The survey states that "a

considerable increase was observed over previous editions of the

survey for use of TCP MD5 with external peers (eBGP), internal

peers (iBGP) and MD5 extensions for IGPs."  Though the data is

not captured in the report, the authors believe anecdotally that

of those who have deployed MD5 somewhere in their network, only

about 25-30% of the routers in their network are deployed with

the authentication enabled.  None report using IPsec [RFC4301] to

protect the routing protocol, and this was a decline from the few

that reported doing so in the previous year's report.

From my

personal conversations with operators, of those using MD5, almost

all report using one, manually-distributed key throughout the

entire network.  These same operators report that the single

key has not been changed since it was originally installed,

sometimes five or more years ago.  When asked why, particularly

for the case of protecting BGP sessions using TCP MD5, the following reasons are

often given:

A. Changing the keys triggers a TCP reset, and thus bounces the

links/adjacencies, undermining Service Level Agreements

(SLAs).

B. For external peers, the difficulty of coordination with the other

organization is an issue.  Once they find the correct contact

at the other organization (not always so easy), the

coordination function is serialized and on a per peer/AS

basis.  The coordination is very cumbersome and tedious to

execute in practice.

Lebovitz, et al.        Expires December 20, 2011               [Page 9]

Internet-Draft        KARP Threats and Requirements            June 2011

C. Keys must be changed at precisely the same time, or at least

within 60 seconds (as supported by two major vendors) in order

to limit connectivity outage duration.  This is incredibly

difficult to do, operationally, especially between different

organizations.

D. Key change is perceived as a relatively low priority compared to other operational issues.

E. Lack of staff to implement the changes on a device-by-device basis.

F. There are three use cases for operational peering at play

here: peers and interconnection with other operators,

iBGP, and other routing sessions within a single operator, and

operator-to-customer devices.  All three have very

different properties, and all are reported as cumbersome.  One

operator reported that the same key is used for all customer

premise equipment (CPE).  The same operator reported that if the

customer mandated it, a unique key could be created, although the

last time this occurred it created such an operational

headache that the administrators now usually tell customers

that the option doesn't even exist, to avoid the difficulties.

These customer-unique keys are never changed, unless the

customer demands so.  The main threat at play here is that a

terminated employee from such an operator who had access to

the one (or few) keys used for authentication in these

environments could easily wage an attack -- or offer the keys

to others who would wage the attack -- and bring down many of

the adjacencies, causing destabilization to the routing

system.

5.  Whatever mechanisms KARP specifies need to be easier to deploy than the current

methods, and should provide obvious operational

efficiency gains along with significantly better security and

threat protection.  This combination of value may be enough to

drive much broader adoption.

6.  Address the threats enumerated above in the "Threats" section

(Section 2) for each routing protocol, along a roadmap.  Not all

threats may be able to be addressed in the first specification

update for any one protocol.  Roadmaps will be defined so that

both the security area and the routing area agree on how the

threats will be addressed completely over time.

7.  Create a re-usable architecture, framework, and guidelines for

various IETF working groups who will address these security

improvements for various Routing Protocols.  The crux of the KARP

work is to re-use that framework as much as possible across

relevant Routing Protocols.  For example, designers should aim to

Lebovitz, et al.        Expires December 20, 2011              [Page 10]

Internet-Draft        KARP Threats and Requirements            June 2011

re-use the key management protocol that will be defined for BGP's

TCP-AO key establishment for as many other routing protocols as

possible.

8.  Bridge any gaps between IETF's Routing and Security Areas by

recording agreements on work items, roadmaps, and guidance from

the cognizant Area Directors and the Internet Architecture Board (IAB).

1.6.  Non-Goals

The following two goals are considered out-of-scope for this effort:

o  Confidentiality of the packets on the wire.  Once this roadmap is

realized, we may revisit work on privacy.

o  Message content validity (routing database validity).  This work

is being addressed in other IETF efforts, like SIDR.

1.7.  Audience

The audience for this document includes:

o  Routing Area working group chairs and participants - These people

are charged with updates to the Routing Protocol specifications.

Any and all cryptographic authentication work on these

specifications will occur in Routing Area working groups, with

close partnership with the Security Area.  Co-advisors from the

Security Area may often be named for these partnership efforts.

o  Security Area reviewers of Routing Area documents - These people

are delegated by the Security Area Directors to perform reviews on

routing protocol specifications as they pass through working group

last call or IESG review.  They will pay particular attention to

the use of cryptographic authentication and corresponding security

mechanisms for the routing protocols.  They will ensure that

incremental security improvements are being made, in line with

this roadmap.

o  Security Area engineers - These people partner with routing area

authors/designers on the security mechanisms in routing protocol

specifications.  Some of these security area engineers will be

assigned by the Security Area Directors, while others will be

interested parties in the relevant working groups.

o  Operators - The operators are a key audience for this work, as the

work is considered to have succeeded only if operators deploy the

technology, presumably due to a perception of significantly

Lebovitz, et al.        Expires December 20, 2011              [Page 11]

Internet-Draft        KARP Threats and Requirements            June 2011

improved security value coupled with relative similarity to

deployment complexity and cost.  Conversely, the work will be

considered a failure if the operators do not care to deploy it,

either due to lack of value or perceived (or real) over-

complexity of operations.  As a result, the GROW and OPSEC WGs

should be kept squarely in the loop as well.

Lebovitz, et al.        Expires December 20, 2011              [Page 12]

Internet-Draft        KARP Threats and Requirements            June 2011

2.  Threats

In RFC 4949 [RFC4949], a threat is defined as a potential for

violation of security, which exists when there is a circumstance,

capability, action, or event that could breach security and cause

harm.  This section defines the threats that are in scope for this

roadmap, and those that are explicitly out of scope.  This document

leverages the "Generic Threats to Routing Protocols" model, RFC 4593

[RFC4593], capitalizes terms from that document, and offers a terse

definition of those terms.  (More thorough description of routing

protocol threats sources, motivations, consequences and actions can

be found in RFC 4593 [RFC4593]).  The threat listings below

expand upon these threat definitions.

2.1.  Threats In Scope

The threats that will be addressed in this roadmap are those from

OUTSIDERS, attackers that may reside anywhere in the Internet, have

the ability to send IP traffic to the router, may be able to observe

the router's replies, and may even control the path for a legitimate

peer's traffic.  OUTSIDERS are not legitimate participants in the routing

protocol.  Message authentication and integrity protection

specifically aims to identify packets originating from OUTSIDERS.

The concept of OUTSIDERS can be further refined to include attackers

who are terminated employees, and those sitting on-path.

o  On-Path - attackers with control of a network resource or a tap (a form of passive wiretapping)

along the path of packets between two routers.  An on-path

outsider can attempt a man-in-the-middle (MiTM) attack (an active wiretapping attack).  A man-in-the-middle attack

occurs when an attacker who has access to packets flowing between

two peers tampers with those packets in such a way that both peers

think they are talking to each other directly, when in fact they

are actually talking to the attacker.  Protocols conforming

to this roadmap will use cryptographic mechanisms to detect

MiTM attacks and reject packets from such attacks (i.e., treat them as not authentic).

o  Terminated Employees - in this context, those who had access

router configuration that included keys or keying material (e.g.,

pre-shared keys) used in securing the routing protocol.  Using this

material, the attacker could send packets that pass the integrity and authenticity checks based on message authentication codes (MACs). The resulting

traffic might appear to come from router A to router B, and thus the attacker could impersonate

an authorized peer.  The attacker could then send false traffic

that adversely affects network behavior.  The

goal of addressing this threat specifically is to call out the

case where new keys or keying material becomes necessary very

quickly, with little operational expense, upon the termination of

Lebovitz, et al.        Expires December 20, 2011              [Page 13]

Internet-Draft        KARP Threats and Requirements            June 2011

an employee (with access to such material).  This threat class also refers to any attacker

who manages to gain access to keying material, and said

access had been detected by the operators such that the operators

have an opportunity to move to new keys in order to counter an

attack if this type..

These attack actions are in scope for this roadmap:

o  Spoofing - when an unauthorized device assumes the identity of an

authorized one.  Spoofing can be used, for example, to inject

malicious routing information that causes the disruption of

network services.  Spoofing can also be used to cause a neighbor

relationship to form that subsequently denies the formation of the

relationship with the legitimate router.

o  Falsification - an action whereby an attacker sends false routing

information.  To falsify the routing information, an attacker has

to be either the originator or a forwarder of the routing

information.  Falsification may occur by an originator, or a

forwarder, and may involve overclaiming, misclaiming, or

mistatement of network resource reachability.  We must be careful

to remember that in this work we are only targeting falsification

from outsiders as may occur from tampering with packets in flight.

Falsification from BYZANTINES (see the Threats Out of Scope

section (Section 2.2) below) are not addressed by the KARP effort.

o  Interference - when an attacker inhibits the exchanges by

legitimate routers.  The types of interference addressed by this

work include:

A.  Adding noise

B.  Replaying out-dated packets

C.  Inserting protocol packets

D.  Corrupting protocol packets

E.  Breaking synchronization

F.  Changing message content

o  DoS attacks at the transport layer - This includes any other DoS

attacks specifically based on the above attack types.  This is

when an attacker sends spoofed packets aimed at halting or

preventing the underlying protocol over which the routing protocol

runs.  For example, BGP running over TLS will still not solve the

problem of being able to send a TCP FIN or TCP RST and causing the

Lebovitz, et al.        Expires December 20, 2011              [Page 14]

Internet-Draft        KARP Threats and Requirements            June 2011

BGP session to go down.  Since this attack depends on spoofing,

operators are encouraged to deploy proper authentication

mechanisms to prevent such attacks.  Routing Protocols should thus

be made resilient to potential attacks on the layers above which

they run.

o  DoS attacks using the authentication mechanism - This includes an

attacker sending packets that confuse or overwhelm a security

mechanism itself.  An example is initiating an overwhelming load

of spoofed routing protocol packets that contain a MAC, so that the

receiver needs to check the MAC, only to discard the spoofed

packet, consuming substantial CPU resources.  Another example is when an

attacker sends an overwhelming load of keying protocol initiations

from bogus sources.  All other possible DoS attacks are out of

scope (see next section).

o  Brute Force Attacks Against Password/Keys - This includes either

online or offline attacks where attempts are made repeatedly using

different keys/passwords until a match is found.  While it is

impossible to make brute force attacks on keys completely

unsuccessful, proper design can make such attacks much harder to

succeed.  For example, the key length should be sufficiently long

so that covering the entire space of possible keys is improbable

using computational power expected to be available 10 years out or

more.  Using per session keys is another widely used method for

reducing the number of brute force attacks as this would make it

difficult to guess the keys.

2.2.  Threats Out of Scope

Threats from BYZANTINE sources -- faulty, misconfigured, or subverted

routers, i.e., legitimate participants in the routing protocol -- are

out of scope for this roadmap.  Any of the attacks described in the

above section (Section 2.1) that may be levied by a BYZANTINE source

are therefore also out of scope.

In addition, these other attack actions are out of scope for this

work:

o  Sniffing - passive observation of route message contents in flight

o  Falsification by Byzantine sources - unauthorized message content

by a legitimate authorized source.

o  Interference due to:

A.  Not forwarding packets - cannot be prevented with

cryptographic authentication

Lebovitz, et al.        Expires December 20, 2011              [Page 15]

Internet-Draft        KARP Threats and Requirements            June 2011

B.  Delaying protocol packets - cannot be prevented with

cryptographic authentication

C.  Denial of receipt - cannot be prevented with cryptographic

authentication

D.  Unauthorized message content - the work of the IETF's SIDR

working group

(http://www.ietf.org/html.charters/sidr-charter.html).

E.  Any other type of DoS attack.  For example, a flood of traffic

that fills the link ahead of the router, so that the router is

rendered unusable and unreachable by valid packets is NOT an

attack that this work will address.  Many other such examples

could be contrived.

Lebovitz, et al.        Expires December 20, 2011              [Page 16]

Internet-Draft        KARP Threats and Requirements            June 2011

3.  Requirements for Phase 1 of a Routing Protocol Transport's Security

Update

The following list of requirements SHOULD be addressed by a KARP Work

Phase 1 security update to any Routing Protocol (according to section

4.1 of the KARP Design Guide [I-D.ietf-karp-design-guide] document).

IT IS RECOMMENDED that any Phase 1 security update to a Routing

Protocol contain a section of the specification document that

describes how each of these requirements is met.  It is further

RECOMMENDED that textual justification be presented for any

requirements that are NOT addressed.

1.   Clear definitions of which elements of the transmitted data (frame,

packet, segment, etc.) are protected by the authentication

mechanism

2.   Strong cryptographic algorithms, as defined and accepted by the security

community, MUST be specified.  Security mechanisms should use algorithms

considered accepted by the IETF's Security community, which are

considered appropriately safe.  The use of non-standard or

unpublished algorithms SHOULD BE avoided.

3.   Algorithm agility for the cryptographic algorithms used in the

authentication MUST be specified, i.e. more than one algorithm

MUST be specified and it MUST be clear how new algorithms MAY be

specified and used within the protocol.  This requirement exists

in case one algorithm gets broken suddenly.  Research to

identify weakness in algorithms is constant.  Breaking a cipher

isn't a matter of if, but when it will occur.  It's highly

unlikely that two different algorithms will be broken

simultaneously.  So, if two are supported, and one gets broken,

we can use the other until we get a new one in place.  Having

the ability within the protocol specification to support such an

event, having algorithm agility, is essential.  Mandating two

algorithms provides both a redundancy, and a mechanism for

enacting that redundancy when needed.  Further, the mechanism

MUST describe the generic interface for new cryptographic

algorithms to be used, so that implementers can use algorithms

other than those specified, and so that new algorithms may be

specified and supported in the future.

4.   Secure use of simple PSKs, offering both operational convenience

as well as building something of a fence around stupidity, MUST

be specified.

5.   Replay of routing protocol packets shouldn’t affect the routing

system.  For non TCP based protocols like OSPF [RFC2328], IS-IS

[RFC1195] , etc., two routers are said to have a session up if

Lebovitz, et al.        Expires December 20, 2011              [Page 17]

Internet-Draft        KARP Threats and Requirements            June 2011

they are able to exchange protocol packets.  Packets captured

from one session must not be able to be re-sent and accepted

during a later session.  Additionally, replay mechanisms must

work correctly even in the presence of routing protocol packet

prioritization by the router.

6.   A change of security parameters REQUIRES, and even forces, a

change of session traffic keys.

7.   Intra-connection re-keying which occurs without a break or

interruption to the current peering session, and, if possible,

without data loss, MUST be specified.  Keys need to be changed

periodically, for operational confidentiality (e.g. when an

administrator who had access to the keys leaves an organization)

and for entropy purposes, and a re-keying mechanism enables the

operators to execute the change without productivity loss.

8.   Efficient re-keying SHOULD be provided.  The specification SHOULD

support rekeying during a connection without the need to expend

undue computational resources.  In particular, the specification

SHOULD avoid the need to try/compute multiple keys on a given

packet.

9.   Prevent DoS attacks as those described as in-scope in the

threats section Section 2.1 above.

10.  Default mechanisms and algorithms specified and defined are

REQUIRED for all implementations.

11.  For backward compatibility reasons, manual keying MUST be

supported.

12.  Architecture of the specification SHOULD consider and allow for

future use of a KMP.

13.  The authentication mechanism in the Routing Protocol MUST be

decoupled from the key management system used.  It MUST be

obvious how the keying material was obtained, and the process

for obtaining the keying material MUST exist outside of the

Routing Protocol.  This will allow for the various key

generation methods, like manual keys and KMPs, to be used with

the same Routing Protocol mechanism.

14.  Convergence times of the Routing Protocols SHOULD NOT be

materially affected.  Materially here is defined as anything

greater than a 5% convergence time increase.  Note that

convergence is different than boot time.  Also note that

convergence time has a lot to do with the speed of processors

Lebovitz, et al.        Expires December 20, 2011              [Page 18]

Internet-Draft        KARP Threats and Requirements            June 2011

used on individual routing peers, and this processing power

increases by Moore's law over time, meaning that the same route

calculations and table population routines will decrease in

duration over time.  Therefore, this requirement should be

considered only in terms of total number of protocol packets

that must be exchanged, and less for the computational intensity

of processing any one message.  Alternatively this can be

simplified by saying that the new mechanisms should only result

in a minimal increase in the number of routing protocol packets

passed between the peers.

15.  The changes to or addition of security mechanisms SHOULD NOT cause

a refresh of route updates or cause additional route updates to

be generated.

16.  Router implementations provide prioritized treatment for certain

protocol packets.  For example, OSPF HELLO packets and ACKs are

prioritized for processing above other OSPF packets.  The

authentication mechanism SHOULD NOT interfere with the ability

to observe and enforce such prioritization.  Any effect on such

priority mechanisms MUST be explicitly documented and

justified. Replay mechanisms provided by the routing protocols

MUST work even if certain protocol packets are offered

prioritized treatment.

17.  The authentication mechanism does not provide message

confidentiality, but SHOULD NOT preclude the possibility of

confidentiality support being added in the future.

18.  Routing protocols MUST only send minimal information regarding

the authentication mechanisms and the parameters in its protocol

packets to avoid exposing the information to parties on the

path.

19.  In most routing protocols (e.g., OSPF [RFC2328], IS-IS [RFC1195], BFD

[RFC5880], RIP [RFC2453], etc.), all speakers share the same key

on a broadcast segment.  Possession of the key itself is used

for identity validation, and no other identity check is used.

This opens a window for an attack where the sender can

masquerade as some other neighbor.  Routing protocols SHOULD

thus use some other information besides the key to authenticate a

neighbor.  One could look at [RFC6039] for details on such

attacks.

20.  Routing protocols that rely on the IP header (or information

separate from the routing protocol payload) to identify the neighbor

that originated the packet, MUST either protect the IP header or

provide some other means to identify the neighbor.  [RFC6039]

Lebovitz, et al.        Expires December 20, 2011              [Page 19]

Internet-Draft        KARP Threats and Requirements            June 2011

describes some attacks that are based on this.

21.  Every new (KARP-developed) security mechanisms MUST support

incremental deployment.  It will not be feasible to deploy a new

Routing Protocol authentication mechanism throughout a network

instantaneously.  It also may not be possible to deploy such a

mechanism to all routers in a large autonomous system (AS) at

one time.  Proposed solutions SHOULD support an incremental

deployment method that provides some benefit for those who

participate.  Because of this, there are several requirements

that any proposed KARP mechanism should consider.

A.  The Routing Protocol security mechanism MUST enable each

router to configure use of the security mechanism on a per-

peer basis where the communication is peer-to-peer (unicast).

B.  Every new (KARP-developed) security mechanism MUST provide backward compatibility

in the message formatting, transmission, and processing of

routing information carried through a mixed security

environment.  Message formatting in a fully secured

environment MAY be handled in a non-backward compatible

fashion though care must be taken to ensure that routing

protocol packets can traverse intermediate routers that

don't support the new format.

C.  In an environment where both secured and non-secured systems

are interoperating, a mechanism MUST exist for secured

systems to identify whether an peer intended the

information to be secured.

D.  In an environment where secured service is in the process of

being deployed, a mechanism MUST exist to support a

transition free of service interruption (caused by the

deployment per se).

22.  The introduction of mechanisms to improve routing security may increase the processing performed by a router.

Since most of the currently deployed routers do not have

hardware to accelerate cryptographic operations, these

operations could impose a significant processing burden under

some circumstances.  Thus proposed solutions should be evaluated

carefully with regard to the processing burden they may impose,

since deployment may be impeded if network operators perceive

that a solution will impose a processing burden which either

incurs substantial capital expense, or threatens to

destabilize routers.

Lebovitz, et al.        Expires December 20, 2011              [Page 20]

Internet-Draft        KARP Threats and Requirements            June 2011

23.  Given the high number of routers that would require the new

authentication mechanisms in a typical ISP deployment, solutions

can increase their appeal by minimizing the burden imposed on

all routers in favor of confining significant work loads to a

relatively small number of devices.  Optional features or

increased assurance that engenders more pervasive processing loads

MAY be made available for deployments where the additional

resources are economically justifiable.

24. New authentication and security mechanisms should not rely

on systems external to the routing system (the equipment that is

performing forwarding).  In order to ensure the rapid

initialization and/or return to service of failed nodes it is

important to reduce reliance on these external systems to the

greatest extent possible.  Therefore, proposed solutions SHOULD

NOT require connections to external systems, beyond those

directly involved in peering relationships, in order to return

to full service.  It is, however, acceptable for the proposed

solutions to require post initialization synchronization with

external systems in order to fully synchronize the security

information.

Lebovitz, et al.        Expires December 20, 2011              [Page 21]

Internet-Draft        KARP Threats and Requirements            June 2011

4.  Security Considerations

This document is mostly about security considerations for the KARP

efforts, both threats and requirements for addressing those threats.

More detailed security considerations were placed in the Security

Considerations section of the KARP Design Guide

[I-D.ietf-karp-design-guide] document.

Lebovitz, et al.        Expires December 20, 2011              [Page 22]

Internet-Draft        KARP Threats and Requirements            June 2011

5.  IANA Considerations

This document has no actions for IANA.

Lebovitz, et al.        Expires December 20, 2011              [Page 23]

Internet-Draft        KARP Threats and Requirements            June 2011

6.  Acknowledgements

The majority of the text for version -00 of this document was taken

from draft-lebovitz-karp-roadmap, authored by Gregory Lebovitz.

Lebovitz, et al.        Expires December 20, 2011              [Page 24]

Internet-Draft        KARP Threats and Requirements            June 2011

7.  References

7.1.  Normative References

[RFC2119]  Bradner, S., "Key words for use in RFCs to Indicate

Requirement Levels", BCP 14, RFC 2119, March 1997.

[RFC4593]  Barbir, A., Murphy, S., and Y. Yang, "Generic Threats to

Routing Protocols", RFC 4593, October 2006.

[RFC4948]  Andersson, L., Davies, E., and L. Zhang, "Report from the

IAB workshop on Unwanted Traffic March 9-10, 2006",

RFC 4948, August 2007.

7.2.  Informative References

[I-D.ietf-karp-design-guide]

Lebovitz, G. and M. Bhatia, "Keying and Authentication for

Routing Protocols (KARP) Design Guidelines",

draft-ietf-karp-design-guide-02 (work in progress),

March 2011.

[ISR2008]  McPherson, D. and C. Labovitz, "Worldwide Infrastructure

Security Report", October 2008,

<http://www.arbornetworks.com/dmdocuments/ISR2008_US.pdf>.

[RFC1195]  Callon, R., "Use of OSI IS-IS for routing in TCP/IP and

dual environments", RFC 1195, December 1990.

[RFC2328]  Moy, J., "OSPF Version 2", STD 54, RFC 2328, April 1998.

[RFC2453]  Malkin, G., "RIP Version 2", STD 56, RFC 2453,

November 1998.

[RFC3562]  Leech, M., "Key Management Considerations for the TCP MD5

Signature Option", RFC 3562, July 2003.

[RFC4271]  Rekhter, Y., Li, T., and S. Hares, "A Border Gateway

Protocol 4 (BGP-4)", RFC 4271, January 2006.

[RFC4301]  Kent, S. and K. Seo, "Security Architecture for the

Internet Protocol", RFC 4301, December 2005.

[RFC4949]  Shirey, R., "Internet Security Glossary, Version 2",

RFC 4949, August 2007.

[RFC5036]  Andersson, L., Minei, I., and B. Thomas, "LDP

Specification", RFC 5036, October 2007.

Lebovitz, et al.        Expires December 20, 2011              [Page 25]

Internet-Draft        KARP Threats and Requirements            June 2011

[RFC5310]  Bhatia, M., Manral, V., Li, T., Atkinson, R., White, R.,

and M. Fanto, "IS-IS Generic Cryptographic

Authentication", RFC 5310, February 2009.

[RFC5709]  Bhatia, M., Manral, V., Fanto, M., White, R., Barnes, M.,

Li, T., and R. Atkinson, "OSPFv2 HMAC-SHA Cryptographic

Authentication", RFC 5709, October 2009.

[RFC5880]  Katz, D. and D. Ward, "Bidirectional Forwarding Detection

(BFD)", RFC 5880, June 2010.

[RFC5925]  Touch, J., Mankin, A., and R. Bonica, "The TCP

Authentication Option", RFC 5925, June 2010.

[RFC6039]  Manral, V., Bhatia, M., Jaeggli, J., and R. White, "Issues

with Existing Cryptographic Protection Methods for Routing

Protocols", RFC 6039, October 2010.

Lebovitz, et al.        Expires December 20, 2011              [Page 26]

Internet-Draft        KARP Threats and Requirements            June 2011

Authors' Addresses

Gregory Lebovitz

Juniper Networks, Inc.

1194 North Mathilda Ave.

Sunnyvale, California  94089-1206

USA

Email: gregory.ietf@gmail.com

Manav Bhatia

Alcatel-Lucent

Bangalore,

India

Phone:

Email: manav.bhatia@alcatel-lucent.com

Russ White

Cisco Systems

USA

Phone:

Email: russ@cisco.com

Lebovitz, et al.        Expires December 20, 2011              [Page 27]

# Comments

I think this characterization is misleading. If the concern is attacks against the “transports” used by routing protocols, then no attacks against security mechanisms built into the protocols themselves would be in scope.   Most of the routing protocols being discussed have security mechanisms built into the protocols themselves.

Although the phrase “on the wire” is used in the KARP charter. It seems redundant. What routing protocols exchange packets via other than “on the wire” means?

Poor choice of terms, since most of this document seems to focus on the routing protocol PDUs, not on transport layer security.

This definition excludes multicast keys (“both peers” and the phrase “secure configuration” is at best redundant. The “usually exchanged out of band” is an odd characterization. When is a PSK not configured in an OOB fashion? And, if the key comes from a third party, it would more accurately described as having been “distributed” to the peers, vs. “exchanged.” The second string of words in the definition is not a sentence.

Do you mean the output of a DH exchange?

Why distinguish between i and iii?

Is the intent to capture a human memorable secret value here? If so, then just say that.

Not always authenticated.

They is plural, but the  (apparent) antecedent “peer” is singular.

Why is this not just “authentication?”

Not the just form, the specific identity per se.

Again, themselves is plural, but the antecedent is peer, a singular noun!

“Between” implies pairwise. Do you means to exclude multicast or group keying?

A raw asymmetric key that is not a PSK does not provide a basis for proof of identity.

A certificate is not merely a “more user  friendly representation …”

This sentence is ambiguous.

“somewhat lower?” an SS certificate provides no proof of identity. It is a convenient format for conveyance of a public key, algorithm info,  and a purported identity

use the RFC 4949 defintion: “A relationship established between two or more entities to enable them to protect data they exchange.”

what is a session, and does one SA protection multiple sessions, as suggested here?

See RFC 4949 for a better definition.

Again, see 4949 for a better base for this definition.

No group keys here? Pairwise implies  that exactly 2 entities share a key

Not always?

You have not defined a KMP key, and I think the term is generally ambiguous. Did you mean KEK or key agreement key, or key distribution  key?

not accurate. An RSA public key often is used to prove identity, yet is not pairwise (as the originally wording of the sentence implied)

A traffic key is one key. More than one traffic key may be used to protect traffic on a  connection, e.g., IPsec uses one key per (unicast) SA, and a unicast SA is unidirectional.

Services are not mechanisms

Why “message” authentication but “packet” integrity?  Do you means routing protocol PDUs?

Why no  cite here?

Packets or routing protocol PDUs?

For OSPF, IS-IS and RIP, the authentication mechanisms are NOT based on a form of transport (protocol) security; they are built into the routing protocols per se. LDP calls for use of TLS.

Just one?

Again, do you mean packets or  routing protocol PDUs?

Not a sentence, and ambiguous as well (.

And?

First use, expand the acronym

First use, expand the acronym

First use, expand the acronym

Do you mean TCP-MD5 or any keyed MD5 integrity feature of an IGP?

There are 3 co-authors, so “my” is inappropriate here.

How does this differ from A above?

Sentence is way too long.

Not a sentence.

Plural here, but just on roadmap in the previous sentence and throughout the document previously. Which is it?

Just the framework? You cited an architecture and guidelines in the previoius sentence

Odd term, as cryptographic authentication is a security mechanism. Do you mean “related” here?

You cite 4949 for the definition of threats, but fail to use it for most other definitions (in section 1.1 and in 2.1). why?

This section is a hodgepodge of terms, many of which are badly defined and often redundant. It’s need to be thoroughly re-written.

A terminated employee who has access to keys that were not changed when he left generally would be considered an insider.

MiTM is a class of attacks, but “terminated employees” represent a class of adversaries. thus the classes here are not parallel.

Since confidentiality is not a security service being considered, you need to explain the relevance of passive attacks to the integrity and authentication services that are in scope.

A MiTM may allow some packets to pass w/o tampering, so the “only” is misleading.

These  are insiders!

You fail to indicate whether this class of adversary is acting in an off path or on=path fashion, an important part of the attack profile.

Why didn’t you start with the 4949 definition for spoofing?

section 1.6: says that “Message content validity (routing database validity)” is a non-goal. This attack (by an outsider) is just an authentication failure of, and does not need to be described separately.

Not a standard attack term. Replay is a type of active attack. Re-ordering is a type of attack. Masquerading yields “inserting protocol packets.” Corrupting packets is an integrity violation, and is the encompassing case for “falsification.” “changing message content” is also an integrity attack example.  This list is redundant. You should just describe active attack types  (that have been well documented for 25+ years), and then discuss how these map to routing protocols.

This is ambiguous. Are you talking  about a physical layer attack on a wireless link?

This sentence suggests that this bullet is redundant.

Not necessarily spoofed packets. A DoS attack could result if the packets fill an input buffer and cause legitimate packets to be dropped, before the claimed packet origin can be examined.

An adverse effect that results from spoofing is countered by detecting an rejecting spoofed traffic. So, again this discuss is largely redundant.

This seems odd. Are you suggesting that BGP should be changed to become resilient to spoofed TCP RSTs, instead or securing the TCP layer?

Probably not what you want to say, as it suggests that you have carefully identified all the DoS attacks of interest.  (Reading this section I would not be convinced of that.)

The IETF regularly mandates key sizes for security protocols, when mandatory-to-implement algorithms are specified.   Why bring this up here? (In contrast, I don’t think we have ever mandated password sizes or entropy levels, so …)

Such attacks were already declared out of scope in Section 1.6, where the following text appears: “Message content validity (routing database validity).”

You probably do not want to rule this out, as it is a way for an attacker to gather data needed to perform an off-path packet injection attack. And, this seems to conflict with the broad definition of an on-path attack ( “…attackers with control of a network resource or a tap…”) presented in section 2.1!

redundant

again, “interference” is a terrible, non-standard term to characterize attacks

if one uses sequence numbers, a receiver can detect this form of a MiTM attacks, so why rule it out?

Timestamps can be used to detect delays. When  did cryptographic auth become the ONLY security mechanism?

Since non-repudiation was declared out of scope, this is just one of many NR-related attacks that are irrelevant. Also, it likely is excluded by the section 1.6 text.

Again, already addresses by the section 1.6 exclusion rule.

“any other” is a questionable characterization, for the reasons I cited earlier.

As opposed to pictographic (

Not a meaningful term. Also, the Security ADs will ensure this, so …

Algorithm agility does NOT require that more than one algorithm be “specified.”  It means that there must be a way to identify which algorithms are used in a protocol, and a way to transition from one to another.

It  also exists because algorithms age over time, often gracefully (.

Nonsense.

As noted above, this is NOT what algorithm agility means, nor it is what ANY Security ADs have mandated for ANY security protocols.

What is a “simple” PSK, and what is an example of a not simple PSK?

We put a fence around stupidity because we wan to protect it from ???

Do you mean that the routing protocol SHOULD be able to detect and reject replayed packets (PDUs)?

That is technically a matter of “peer entity authentication” see RFC 4949.  Replay within a session is addressed by “stream integrity” mechanisms (4949).

Since this document has not specified what “security parameters” are, this isn’t a good requirement.

Sounds BGP-centric

Not very precise.

Usually one does not prevent DoS attacks. One detects and rejects, as soon as possible, traffic that constitutes the DoS attack.

Do you mean mandatory to implement?

Integrity too.

Are there generally accepted math models for each of the target routing protocols that will enable designers of security mechanisms to verify that this requirement is being met?

Is this a generic routing protocol term or is it BGP-centric?

It is unlikely that authentication mechanisms would interfere with this, but integrity mechanisms (e.g., for stream integrity) might. So, is this a case where the use of “authentication” as a generic security term is causing confusion?

This is a silly statement. Authentication mechanisms DO NOT provide confidentiality. Also, I don’t recall ever seeing a design in which an authentication mechanism precluded use of confidentiality, when both were intended to be processed at the same point.

Nonsense. Who believes this is a legitimate concern?

This is a very odd statement. It basically says that if you have a routing protocol that uses multicast on a link, and if a group key is used to provide group-granularity authentication, you should use some additional method to provide per-peer authentication. If finer granularity authentication is required, then maybe group keying is inappropriate.

Authenticate?

SHOULD here, but MUST two sentence above! Pick one.

Since the scope of this work is peer-to-peer authentication and integrity, can’t one just  negotiate use of the new, secured version of the protocol one a peer-by-peer basis, and avoid the need for backward compatibility in many respects? Also, the reference to traversing routers that do not support the new mechanisms seems to inconsistent with the peer-to-peer  model, except for a routing protocol like RSVP (which is not mentioned anywhere in this document).

“Originator” seems like an odd term here, since the scope of this work is mostly transport security. Also, if one needs to establish an SA with a peer to effect authentication, isn’t that enough to let you k now if the peer is security-enabled?

Since ISPs come in all seizes, the term “high numbers” seems questionable here.

Too broad a requirement. The third sentence is a better characterization of the real concern here.