## Slide 1: Address + Port addressing (A+P) Purpose and Origin
Rémi Després - remi.despres@free.fr
76 th IETF – aplusp BOF - 2009-11-11
Notes: Work in progress.
Simple design to satisfy significant needs

## Slide 2: General Scope of A+P
When?
  Coexistence period
    (IPv6-enabled and IPv4-only hosts)
What for?
  IPv6 Sites having shared-only IPv4 address
  Possible port management by customer sites
  Possibly coexistence with ISP NATs
How?
  Assign to sites port-restricted IPv4 addresses
  Encapsulate IPv4 A+P packets in IPv6 packets

## Slide 3: Brief History
1999-2001 - RSIP (Realm Specific IP - RFC 3103)
  Experimental protocol for dynamic A+P on mesh topologies
2008-2009 - revival
  July 2008: draft-despres-v6ops-apbp-01
  Sept 2008: draft-bajko-v6ops-port-restricted-ipaddr-assign-00
  Oct 2008: draft-boucadair-port-range-00
  Oct 2008: draft-ymbk-aplusp-00
  Nov 2008: Common presentation at IETF 73
  …
  Nov 2009: aplusp BOF

## Slide 4: Identified Variants WITHIN the Scope
Hubs-and-Spokes or Mesh Topologies
Dynamic and/or Static assignments
Port-range specification:
  First&Last ports
  Mask&Value of ports
  Port Prefix

## Slide 5
The IETF 73 Common Presentation
…
…